*******************************************************************************
                                    23440A2
*******************************************************************************

CUPL(WM)        5.0a Serial# 60008009
Device          virtual  Library DLIB-h-40-1
Created         Tue Apr 03 05:58:28 2018
Name            23440A2
Partno          E28 74S287
Revision        1.0
Date            March 2018
Designer        Digital Equipment Corporation
Company         None
Assembly        0001
Location        None

===============================================================================
                            Expanded Product Terms
===============================================================================

!cdf =>
    !BM11
  # unused
  # !BM4

cdf.oe  =>
    G1 & G2

!cif =>
    !BM10
  # unused
  # !BM4

cif.oe  =>
    G1 & G2

!let_io =>
    !BM4 & !BM5 & BM9 & BM678 & !cdf & !cif
  # !BM4 & !BM9 & BM678 & !cdf & !cif
  # !BM4 & !BM678 & !cdf & !cif
  # BM4 & !cdf & !cif

let_io.oe  =>
    G1 & G2

!unused =>
    EN5 & EN9
  # !BM5 & EN9
  # !BM9 & EN5
  # !BM5 & !BM9

unused.oe  =>
    G1 & G2



===============================================================================
                                 Symbol Table
===============================================================================

Pin Variable                                    Pterms   Max     Min    
Pol   Name              Ext     Pin     Type     Used   Pterms  Level   
--- --------            ---     ---     ----    ------  ------  -----   

    BM4                         3        V        -       -       -     
    BM5                         4        V        -       -       -     
    BM9                         7        V        -       -       -     
    BM10                        6        V        -       -       -     
    BM11                        5        V        -       -       -     
 !  BM678                       15       V        -       -       -     
    EN5                         1        V        -       -       -     
    EN9                         2        V        -       -       -     
 !  G1                          13       V        -       -       -     
 !  G2                          14       V        -       -       -     
 !  cdf                         9        V        3       0       4     
    cdf                 oe      9        X        1       0       1     
 !  cif                         10       V        3       0       4     
    cif                 oe      10       X        1       0       1     
 !  let_io                      12       V        4       0       4     
    let_io              oe      12       X        1       0       1     
    unused                      11       V        4       0       4     
    unused              oe      11       X        1       0       1     


LEGEND    D : default variable         F : field      G : group
          I : intermediate variable    N : node       M : extended node
          U : undefined                V : variable   X : extended variable
          T : function