Program:	DASM.EXE V1.1

Release date:	December 13, 1997

Author:		John Wilson <wilson@dbit.com>

Description:	DASM is a simple disassembler for Z-80, 8051, 8080/8085, or
		8086 binary files.  The file base address may be anywhere in 64
		KB so ROM images may be disassembled as easily as .COM files.
		The disassembler performs an execution trace before generating
		output to put labels in the right places as much as possible,
		and it tries to distinguish code from data, but it is possible
		for it to fool itself by making symbol table entries for
		addresses that are really indices.  A mechanism is provided for
		feeding the disassembler a file containing a list of entry
		points at which to begin the execution trace, so after each
		disassembly you can inspect the output and add addresses from
		any newly discovered jump tables, dispatch tables, computed
		jumps etc. to the file so the next disassembly will be closer
		to complete.

		Ideally the disassembler would figure out these things itself
		but that would require very sophisticated tracing of register
		contents which would make the disassembler several orders of
		magnitude more complicated.  For now it simply performs a "dry
		run" disassembly starting at each entry point specified, adding
		each jump (or call) target to the symbol table, recursing for
		both paths when it reaches a CALL or conditional jump
		instruction, and stopping when it reaches a halt or
		unconditional return instruction, or a label that it's been to
		before (so it won't get caught in loops).  Then a linear
		disassembly is done starting at the specified starting address,
		producing labels and code or data depending on the type of
		access that created the symbol table entry for the most recent
		label.

Command line:	DASM [filename[.COM]] [/switches]

		The "filename" parameter is the name of the binary file, with a
		default extension of ".COM".  The output file has the same name
		but with the extension changed to ".ASM" (which better not have
		been the input file's extension!).  If no filename is
		specified, standard input and output are used.

		The switches are all optional and must start with the current
		DOS SWITCHAR, which is "/" by default.  They are:

		/S:hhhh
		Sets the address where disassembly starts (beginning of file by
		default).

		/E:hhhh
		Sets the address where disassembly ends (end of file by
		default).

		/F:hhhh
		Sets the file's load address (0100 by default), i.e. defines
		the relationship between file addresses and memory addresses.

		/T:hhhh
		Sets the transfer address where the trace begins (0100 by
		default).

		/T:@file
		Gives the name of a file containing a list of hex entry
		addresses separated by white space and/or <CRLF> pairs.  If an
		address has a '#' suffix then it is entered in the symbol table
		as a "data" address.  Otherwise it is entered as a "code"
		address (i.e. jump target) and an execution trace is begun at
		that address.

		/C:xxxx
		Specifies which CPU's mnemonics are to be used for disassembly:

		/C:8051 Intel MCS-51 mnemonics
		/C:8080	Intel MCS-80/MCS-85 mnemonics (syn. /I)
		/C:8086	Intel iAPX-86 (etc.) mnemonics (syn. /N)
		/C:Z80	Zilog Z-80 mnemonics

Copyright:	This program is copyright (C) 1995, 1997 by John Wilson.  All
		rights reserved.  The program may be freely distributed
		provided that no charge is made for distribution, and that
		proper credit is given to John Wilson in all copies, whether
		modified or not.

		All trademarks referenced are used for identification purposes
		only and are the property of their respective owners.