PUTR V1.28
                             FILE TRANSFER PROGRAM
                     Copyright (C) 1995-1998 by John Wilson
                              All rights reserved
                           Release date:  11-Jun-1998
        
             PUTR is a copyrighted but freely distributable utility for
        transferring files between various file systems and various
        media.  It is named after PUTR.SAV (Peripheral Utility Transfer
        Routines), the utility which performs the same function under
        the DEC TSS/8.24 operating system for the PDP-8.
        
             The only file systems currently fully supported are
        OS/(27)8, RT-11, and PC-DOS;  read-only access to RSTS/E disks
        is also available.  Support for COS-310 text files is planned
        (and existed in an ancient version that was never released) but
        not yet re-implemented (COS-310 binary files are accessed the
        same way as with OS/8).  Support for the TSS/8 PUTR and COPY
        DECtape formats may be added later, so that PUTR can live up to
        its name.  All file systems other than PC-DOS must be logically
        mounted and assigned a logical device name before use.  This is
        done with the MOUNT command.  PUTR is mainly intended to work on
        logical devices contained in disk image files (normally a
        block-by-block copy of the foreign disk), but it also supports
        raw SCSI disks (through an ASPI driver), DEC TU58 tape drives
        (plugged into a COM port), RX50 (including a double sided
        variant) and RX33 floppy disks or RX01/02/03 26-sector workalike
        disks mounted on a 1.2 MB drive, and RX24, RX23, and RX26 720
        KB/1.44 MB/2.88 MB disks on an appropriate 3.5" drive (even
        though none of these was supported by standard DEC controllers
        on machines using these file systems).
        
             PUTR can format any of these types of floppy disks.  Note
        that most PC floppy controllers don't work correctly in single
        density mode (some made by SMC, WD, Goldstar, Intel (but not the
        82078), and National Semiconductor are known to work).  On a
        controller with a working single density mode, the RX01 format
        is exactly compatible with genuine RX01 disks (i.e.  IBM 3740
        format) mounted in an 8" drive connected in place of a 1.2 MB
        one (using an adapter cable).  The "RX02" format is actually IBM
        System 34 format, since DEC's 8" DD disks use a strange
        combination of SD headers and DD data fields that can't be done
        with a PC FDC.  The 26-sector 5.25" disk formats are compatible
        with those used by the Ersatz-11 PDP-11 emulator, a demo version
        of which is available from FTP.DBIT.COM in the /pub/e11
        directory.
        
             When PUTR is run, it looks for an indirect command file
        named "PUTR.INI", first in the current directory, then in the
        directory where the executable is located (for PC-DOS 3.0 and
        later only).  If found, this file is opened as an indirect
        command file before the first command prompt.  This is a
        convenient place to put SET commands, and MOUNT commands for the
        disk image file(s) that you usually use.


        FILENAMES

        [ldevu:][dir][filename]

        As much as possible, the filename syntax is intended to look
        similar to that of the host operating system for the volume on
        which the file is located.

        The ldevu:  parameter is the logical device and unit number
        where the file is located.  The device name is one or two
        letters with an optional unit number in the range 0-255.
        Logical devices are mounted using the MOUNT command, or they may
        be PC-DOS drives (which are all implicitly mounted under the
        native file system (i.e.  PC-DOS)).  The device name syntax is
        intended to mimic that of the DEC PDP-11 OSes for convenience
        only, at the moment no significance is attached to the device
        name (different units of the same device name have nothing to do
        with each other, and for example DL0:  need not be an RL01/02
        image).  This may change.  If the ldevu:  parameter is omitted,
        the current logged-in logical device is assumed (you log into a
        device by typing the device name and a colon at the prompt, just
        like in PC-DOS).

        The dir parameter is the directory in which the file is located
        (by default, the current working directory on that logical
        device).  With PC-DOS drives this is the usual sequence of
        directory names separated by \ (or / if that isn't your
        SWITCHAR).  RT-11 drives use the same syntax as PC-DOS, to refer
        to nested logical disk files (LD:);  the default extension is
        ".DSK".  "."  and ".."  are fake directory names and have the
        same meanings as under PC-DOS.  Note that PUTR doesn't assume
        that it can tell the difference between a directory and an
        ordinary file (because under RT-11 there is no difference), so
        all pathname elements must end in \ (except the final one in a
        CD command).  So if you want to list the parent directory, type
        "DIR ..\" instead of "DIR ..".  RSTS drives use directory names
        of the form [proj,prog], with the project and programmer numbers
        in decimal.  The one-character logical names !, #, $, %, and &
        also work.

        The filename syntax depends on the file structure of the drive;
        under all supported file structures it is of the form
        "filename.ext", where the length of the filename and extension
        have fixed limits for each OS.  Note that the parsing and
        wildcard matching routines make no assumptions about filename
        syntax (except for adding default "*"s depending on whether they
        see a "."  anywhere in the filespec), so it is possible to fool
        them.  For example, typing "DIR ????????A.*" on a PC-DOS disk
        will not give an error message, but it's impossible for anything
        to match this spec.  The wildcard parser is smarter than the one
        in PC-DOS -- '*' and '?' really work the way they should (in
        PC-DOS a '*' is equivalent to filling out the rest of the field
        with '?'s instead of really matching 0 or more characters, and
        in PC-DOS '?' will match a blank, which IMHO it shouldn't).


        COMMANDS


        @ filename[.CMD]

        Redirects input so that commands come from the specified
        indirect command file (with default extension ".CMD").  Indirect
        files chain rather than nesting, if an "@" command appears
        inside an indirect file the file is closed and new input comes
        from the specified file.  At end of file input reverts to the
        keyboard.


        BOOT ldevu:

        On RT-11 volumes only, makes a volume bootable.  The volume must
        contain the needed .SYS files (monitor, system device handler,
        TT:  device handler), there are prompts that let you choose
        which monitor to boot and which device handler the bootstrap
        should be for.  At each prompt you may enter a blank line to
        display a list of all .SYS files on the volume, or a filename
        (default extension ".SYS") to use.  The action performed is
        exactly equivalent to COPY/BOOT under RT-11.


        CD ldevu:dir

        Changes the current working directory on the specified drive
        (default is the current logged-in drive).  If no directory is
        given the current working directory is displayed.


        CLS

        Clears the screen.


        COPY[/BINARY][/OVERRIDE] ldevu:inspec ldevu:outspec

        Copies the specified file(s), converting between file systems if
        necessary.  Files are assumed to be ASCII (NULs are squeezed
        out, two 12-bit words are unpacked to three 8-bit characters,
        etc.)  unless the /BINARY switch is given;  this default may be
        changed with the SET COPY command.  If an output file has the
        same name as an existing file in the same directory, then the
        existing file is deleted, unless it is protected;  the /OVERRIDE
        switch overrides this protection.  Not all file systems support
        protection.  In a binary copy between 12- and 16-bit media, the
        12-bit words are considered to be right-justified in 16-bit
        words (PDP-11 byte order);  the remaining four bits are ignored
        on input and written as 0 on output.


        COPY/DEVICE[/FILES][/BINARY] ldevu:[inspec] ldevu:[outspec]

        Does an image copy from one device to another, or between a
        device and a file.  By default the copy is done in logical block
        order, which is to say the 512-byte blocks are copied in order
        starting at block 0.  If you're copying a floppy disk (or an
        image of one) then /BINARY means to copy in physical sector
        order, starting with cylinder 0 head 0 sector 1, and proceeding
        in sequential sector order, copying both surfaces of each
        cylinder (if double sided) before proceeding to the next
        cylinder.  This copies all sectors of the disk, even those not
        used by the DEC interleave schemes (on RX01, RX02, and RX03
        disks, DEC leaves out track 0), and the resulting image files
        are more likely to be in the right order if they aren't really
        DEC disks.  This use of /BINARY is not affected by the SET COPY
        command.


        DELETE[/NOQUERY][/OVERRIDE] ldevu:filespec

        Deletes the specified file(s), prompting before each unless
        /NOQUERY is specified.  If a file is protected, it is not
        deleted unless the /OVERRIDE switch is given.


        DIRECTORY ldevu:wildcard [/FULL]

        Displays a directory of the indicated file(s).  /FULL gives the
        starting block numbers of files as well on OS/8 or RT-11
        volumes.


        DISMOUNT ldevu:  [/UNLOAD]

        Undoes the effect of a MOUNT command (q.v.).  Closes any image
        file associated with the logical device, or releases the COM
        port or floppy drive or SCSI device, and deletes the logical
        name definition.  /UNLOAD ejects the disk on SCSI drives that
        support this.


        EXIT

        Returns to PC-DOS.


        FORMAT d:  /devtype /ostype

        Formats the disk in PC-DOS floppy drive d:  to the type
        specified by /devtype (/RX01, /RX02, /RX03, /RX23, /RX24, /RX26,
        /RX33, /RX50, /RX52 -- default depends on drive type and is
        /RX50 for 1.2 MB drives or if the drive type is unknown).  The
        /ostype switch is optional and tells PUTR to write a blank
        directory structure for the specified OS.  It may also affect
        the interleave and skew used for formating, if appropriate for
        that OS.

        Note that for RX50 format, double density disks (e.g.  PC 360 KB
        disks) should be used rather than the PC high density 1.2 MB
        disks.  Opinion is divided as to whether the hub rings should be
        peeled off before use -- as they age they may slide slightly out
        of place so that the disk doesn't center properly, but then
        again they're there to protect the disk and without them it's
        more likely to get damaged.  In any case the 1.2 MB disks don't
        erase/rewrite properly in double density mode (RX50s are double
        density disks), even if they appear to format OK (which might
        happen if they were bulk erased first) they can't be trusted as
        RX50s.


        FORMAT dev:filename /devtype /ostype

        Creates an image file of the specified device type.  The file is
        initialized to zeros and an empty bad sector file is written if
        appropriate (you will be prompted for a pack serial number for
        device types that have them).  If no device type is given then
        PUTR assumes nothing and just prompts for the file size and
        creates a zeroed file of that size.  As above, if /ostype is
        specified then a blank directory is written.


        INITIALIZE vol /devtype /ostype

        Writes a blank directory on the specified volume or image file
        (only /OS8 and /RT11 are allowed as /ostype switches at this
        time).  Prompts for any needed information.  "vol" is a file,
        floppy drive, SCSI device, or COM port name the same as in
        FORMAT and MOUNT.  For initializing RT-11 volumes, there is a
        "/SEGMENTS:n" switch which sets the number of directory segments
        (default depends on size of volume as with RT-11 DUP.SAV).


        MOUNT ldevu:  image /devtype /ostype

        Mounts a disk image on a logical device name for later use.
        "ldevu:"  is a logical device name (1 or 2 letters) and optional
        unit number.  The device name is arbitrary, but I may change
        things so that the device name dictates the emulation (i.e.
        "DL1:"  must be an RL01 or RL02) since that will make it
        possible to have useful defaults for /devtype in case file size
        alone isn't enough to tell.

        "image" is the location of the disk image.  Possibilities are as
        follows:

        [d:][path\]filename[.DSK] (name of a DOS file)

             The specified file contains a raw image of the disk.
             This is known as an "image file" or "container file",
             and is commonly obtained by downloading a disk from a
             live machine over a serial or network connection,
             although PUTR can also create them itself (see
             FORMAT).

        d:  (name of a PC floppy drive)

             The raw floppy disk is used to hold the volume.  This
             should not be confused with an image file on a DOS
             diskette, the disk uses the foreign file system and in
             most cases will interchange with the foreign machine.
             In a MOUNT command, if the "ldevu:"  logical device
             name is omitted, the floppy name will be used.  For
             example you may "MOUNT B:  /RT11 /RX50" and then "DIR
             B:".

        SCSIht_l:  (SCSI disk)

             This form allows a raw SCSI disk to be mounted using a
             foreign file system.  The "SCSIht_l:"  device name
             specifies a SCSI disk (accessed through an ASPI
             manager) at host adapter "h" (A=0, B=1, etc.), target
             "t", and LUN "l", where h, t, and l (as well as the
             underscore character) are all optional (the defaults
             are "SCSIA0_0:").  On most systems there will be only
             one SCSI host adapter, and most disks have only one
             logical unit, so in most cases the device name may be
             something like "SCSI5:", which specifies SCSI target
             #5.

        COMn:bbbbb/DRIVE:u (TU58 tape drive)

             This specifies an actual DEC TU58 drive connected to
             COM port "n", at baud rate "bbbbb" (default is 38400),
             unit u (0 or 1, default is 0).

        The /devtype switch specifies the device type of the image;  the
        defaults are auto-sensed except for TU58 drives where obviously
        the default is always /TU58.  With image files the default
        device type depends on the file size, and is the largest defined
        device less than or equal to the file in length.  With floppies
        various reads are attempted to detect the disk type.
        Possible switches are as follows:

             /RX01 = RX01 disk, 5.25" RX01 workalike
             /RX02 = 5.25" RX02 workalike
             /RX03 = DS 5.25" RX02 workalike

                  NOTE:  for image files of the above devices, the file
                  size is used to determine which disk type it is and
                  whether the file is a block-by-block image (as
                  obtained by a "COPY/DEVICE/FILES DY0:  FLOPPY.IMG"
                  command under RT-11, for example) which has had
                  interleave and skew applied to it by the PDP-11 device
                  driver that read it, or a sector-by-sector image (as
                  might be obtained by any simple program that reads the
                  sectors off sequentially and puts them in order into a
                  file).  Block-by-block image files of 8" disks are
                  slightly smaller because the interleave/skew scheme
                  skips track 0.

             /RX23 = 1.44 MB 3.5" disk
             /RX24 = 720 KB 3.5" disk
             /RX26 = 2.88 MB 3.5" disk
             /RX33 = 1.2 MB 5.25" disk
             /RX50 = 400 KB 5.25" disk

                  NOTE:  RX50 image files are the same size whether they
                  have interleave or not, so PUTR tries it both ways
                  while trying to guess the OS type.

             /RX52 = DS RX50, 800 KB 5.25" disk (my own name)

        The following switches are also supported:  /RA60, /RA70, /RA71,
        /RA72, /RA73, /RA80, /RA81, /RA82, /RA90, /RA92, /RK02, /RK05,
        /RK06, /RK07, /RL01, /RL02, /RS03, /RS04, /TU56, /TU58.  These
        switches set the device type to the indicated DEC drive model.
        Since there is no way to connect most of these devices directly
        to a PC (unlike floppies), the effect of these switches is to
        specify the exact size of the volume, and for the FORMAT
        command, there is special handling of RL01/02 and RK06/07 drives
        for building a blank bad sector track and deducting the correct
        amount from the RT-11 volume size to allow for replacement
        blocks.

        The /ostype switch specifies the file structure on the device;
        it must be /RSTSE, /RT11, /OS8, or /FOREIGN.  If none is
        specified then PUTR examines the home block (or performs a
        directory consistency check for OS/8 volumes) to guess the disk
        format.  If the volume appears to have no known directory, or
        appears to be valid for more than one file structure, then a
        message is displayed and the volume is not mounted.  Mounting a
        disk with /FOREIGN would be pointless (since no directory
        operations are allowed) except that it makes it usable with the
        COPY/DEVICE command so it can be used to transfer an image of
        the disk to or from a file.

        There are a few miscellaneous switches.  /INTERLEAVE and
        /NOINTERLEAVE tell whether an image file is interleaved (i.e.  a
        block-by-block copy of a floppy disk so the data are in block
        order, not sector order) or non-interleaved (i.e.  a
        sector-by-sector copy so the data are in sector order).  The
        default is to guess based on the image file size (or prompt in
        the case of FORMAT, which takes the same switches).
        /PARTITION:n specifies the RT-11 DU:  partition number (default
        is 0).  /RONLY and /RW tell whether the device should be mounted
        for read-only or read/write access.  The default is read/write.

        All of the above switches may be given in any order.


        QUIT

        Returns to PC-DOS.


        SET COPY {ASCII | BINARY}

        Sets the default transfer mode for the COPY command (initially
        ASCII).  Intended mainly for use in the PUTR.INI command file.


        SET DISMOUNT {NOUNLOAD | UNLOAD}

        Sets the default unload action of DISMOUNTs, both explicit, and
        implied by QUITting, or reMOUNTing the pseudo-device as
        something else.  Default is NOUNLOAD.  Intended for use in
        PUTR.INI with drive models where the disk shouldn't be left in
        the drive when it's powered off.


        SET FDC {COMPATICARD | GENERIC}

        Tells PUTR whether your floppy disk controller is a Micro
        Solutions CompatiCard IV, or just a generic PC floppy
        controller.  If it is a CompatiCard, PUTR maintains the TG43
        signal (for 8" drives) by writing to port 3F0h;  normal FDCs
        have no writable port at that address and don't do anything when
        it gets written so the default is COMPATICARD to cover
        everything, but if your FDC does strange things when that port
        is written you should SET FDC GENERIC.


        SET MORE {OFF | ON}

        Turns **MORE** processing on or off;  the default is on.  As
        above, intended mainly for use in PUTR.INI.


        SHOW ldevu:

        Shows the medium and file system types for the specified logical
        device.


        TYPE ldevu:wildcard

        Types the specified file(s) on the terminal, printing the
        filename(s) first.


        WIPEOUT ldevu:dir

        Writes zeros over all < UNUSED > areas so that disk image files
        will compress smaller with GZIP (etc.)  and/or transfer faster
        with Kermit (etc.).  Supported only for OS/8 and RT-11.



        Note:

        "Ersatz" and "E11" are trademarks of Digby's Bitpile, Inc.  All
        other trademarks are used for identification purposes only and
        are the property of their respective owners.



        John Wilson
        Digby's Bitpile, Inc. DBA D Bit
        11 Bank Street
        Troy, NY  12180
        USA
        +1 (518) 271-6824
        +1 (518) 272-3853 fax
        <wilson@dbit.com>
        www.dbit.com