RTS8V3.DOC





















                                  DISCLAIMER

                This document file was created by scanning  the
                original  document and then editing the scanned
                text.  As much as possible, the  original  text
                format  was restored.  Some format changes were
                made to insure this  document  would  print  on
                current laser printers using 60 lines per page.
                The  original  spelling  and  grammar  has been
                preserved.


                1-Sep-1996





                                                        RTS/8

                                                    User's Manual

                                                Order No. AA-0724D-TA













                                 February 1979




                                   ABSTRACT

           This manual describes version 3 of RTS/8, the real-time
           operating system for the PDP-8 which allows up to 127
           tasks to run concurrently. Described are the Executive
           Requests which permit intertask communication, the Monitor
           Console Routine which permits the user to control task
           execution from a terminal, and the message formats for
           DIGITAL supplied tasks.



     SUPERSESSION/UPDATE INFORMATION: This manual supersedes DEC-08-ORTMA-C-D.

     OPERATING SYSTEM AND VERSION:    RTS/8, V3










           --------------------------------------------------------
           | To order additional copies of this document, contact |
           |  the Software Distribution Center, Digital Equipment |
           |  Corporation, Maynard, Massachusetts 01754           |
           --------------------------------------------------------


            digital equipment corporation - maynard, massachusetts


                                              First Printing, February 1979

     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation. Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this document.

     The software described in this document is furnished under a license
     and may only be used or copied in accordance with the terms of such
     license.

     No responsibility is assumed for the use or reliability of software on
     equipment that is not supplied by DIGITAL or its affiliated companies.








              Copyright (c) 1979 by Digital Equipment Corporation








     The postage-prepaid READER'S COMMENTS form on the last page of this
     document requests the user's critical evaluation to assist us in
     preparing future documentation.


     The following are trademarks of Digital Equipment Corporation:



              DIGITAL             DECsystem-10        MASSBUS
              DEC                 DECtape             OMNIBUS
              PDP                 DIBOL               OS/8
              DECUS               EDUSYSTEM           PHA
              UNIBUS              FLIP CHIP           RSTS
              COMPUTER LABS       FOCAL               RSX
              COMTEX              INDAC               TYPESET-8
              DDT                 LAB-8               TYPESET-11
              DECCOMM             DECSYSTEM-20        TMS-11
              ASSIST-11           RTS-8               ITPS-10
              VAX                 VMS                 SBI
              DECnet              IAS                 PDT
              DATATRIEVE          TRAX






                                                                    3/79-15






                                   CONTENTS

                                                                       Page

     PREFACE                                                           vii

     CHAPTER  1         INTRODUCTION                                   1-1

              1.1       RTS/8 DESCRIPTION                              1-1
              1.2       REAL-TIME OPERATION                            1-3

     CHAPTER  2         USING TASKS UNDER RTS/8                        2-1

              2.1       RTS/8 TASKS                                    2-1
              2.2       CONCEPTS OF TASK COMMUNICATION                 2-1
              2.2.1       Task Synchronization                         2-2
              2.2.2       Intertask Messages                           2-4
              2.3       PRIORITY                                       2-5
              2.4       TASK INTERRUPTS AND SCHEDULING                 2-6
              2.5       CREATING RTS/8 TASKS                           2-6
              2.6       RUNNING AN RTS/8 SYSTEM                        2-8

     CHAPTER  3         RTS/8 EXECUTIVE REQUESTS                       3-1

              3.1       COMMUNICATION WITH THE RTS/8 EXECUTIVE         3-1
              3.2       EXECUTIVE REQUESTS                             3-4
              3.3       EXAMPLE OF EXECUTIVE REQUESTS FOR MESSAGE
                        AND EVENT FLAGS                                3-28
              3.4       EXECUTIVE REQUEST WAIT STATES                  3-30

     CHAPTER  4         RTS/8 SYSTEM TASKS                             4-1

              4.1       RTS/8 SYSTEM TASK SUMMARY                      4-1
              4.2       CASSETTE HANDLER                               4-3
              4.2.1       Handler Function                             4-3
              4.2.2       Utility Function Handler                     4-6
              4.3       CASSETTE FILE SUPPORT HANDLER                  4-8
              4.4       CLOCK HANDLER                                  4-11
              4.5       CONSOLE AND NONCONSOLE TERMINAL HANDLERS       4-16
              4.5.1       EMT Task                                     4-21
              4.6       EXIT TASK                                      4-23
              4.7       FLOPPY DISK HANDLER                            4-24
              4.8       LINCTAPE HANDLER                               4-29
              4.9       LINE PRINTER HANDLER                           4-32
              4.10      MASS STORAGE HANDLERS                          4-34
              4.11      OS/8 FILE SUPPORT TASK                         4-38
              4.12      OS/8 SUPPORT TASK                              4-40
              4.12.1      OS/8-RTS/8 Communication (OS8COM)            4-41
              4.12.2      Other Techniques                             4-43
              4.13      PDP-8A NULL TASK                               4-44
              4.14      POWER FAIL TASK                                4-45
              4.15      UDC/ICS HANDLER                                4-46
              4.15.1      AI (Analog Input)                            4-48


                                      iii

                              CONTENTS (Cont.)

                                                                       Page

              4.15.2      AO (Analog Output)                           4-49
              4.15.3      CS (Change of State)                         4-50
              4.15.4      DI (Digital Input)                           4-51
              4.15.5      DO (Digital Output)                          4-51
              4.15.6      DCT (Disable Contacts)                       4-52
              4.15.7      DC (Disable Counter)                         4-53
              4.15.8      ECT (Enable Contacts)                        4-54
              4.15.9      EC (Enable Counter)                          4-55
              4.15.10     GC (Generic Code)                            4-56
              4.15.11     RC (Read Counter)                            4-57
              4.15.12     UDC/ICS Status/Error Conditions              4-58

     CHAPTER  5         MONITOR CONSOLE ROUTINE                        5-1

              5.1       MCR FUNCTIONS                                  5-1
              5.2       MCR COMMAND SYNTAX                             5-1
              5.3       MCR COMMANDS                                   5-2
              5.3.1       CANCEL                                       5-3
              5.3.2       DATE                                         5-3
              5.3.3       DEPOSIT                                      5-4
              5.3.4       DISABLE                                      5-4
              5.3.5       ENABLE                                       5-5
              5.3.6       EXAMINE                                      5-5
              5.3.7       EXIT                                         5-5
              5.3.8       NAME                                         5-5
              5.3.9       OPEN                                         5-6
              5.3.10      POST                                         5-6
              5.3.11      REQUEST                                      5-7
              5.3.12      STOP                                         5-8
              5.3.13      SYSTAT                                       5-8
              5.3.14      TIME                                         5-10
              5.3.15      MCR Errors                                   5-10

     CHAPTER  6         NONRESIDENT TASKS                              6-1

              6.1       NONRESIDENT TASK DESCRIPTION                   6-1
              6.1.1       Checkpointable Tasks                         6-2
              6.1.2       Modified Tasks                               6-3
              6.1.3       Interaction Between Tasks                    6-3
              6.2       MEMORY PARTITIONS                              6-3
              6.2.1       FREE Command                                 6-4
              6.2.2       Writing Nonresident Tasks                    6-5

     CHAPTER  7         PROGRAMMING TECHNIQUES                         7-1

              7.1       OVERVIEW                                       7-1
              7.2       PERFORMING A RESCHEDULE                        7-1
              7.2.1       Writing Delicate Code                        7-1
              7.2.2       Inhibiting Task Switching                    7-3
              7.3       MULTIPLE EVENT FLAG WAITS                      7-5
              7.4       EXECUTIVE INTERNAL TASK TABLES                 7-6
              7.4.1       Task State Table (TSTABL)                    7-7
              7.4.2       Task Flags Table (TFTABL)                    7-8


                                      iv

                              CONTENTS (Cont.)

                                                                       Page
              7.4.3       Task Input Message Queue Header Table
                          (MSGTBL)                                     7-10
              7.4.4       Residency Table (RESTBL)                     7-10
              7.4.5       Partition Table (PARTBL)                     7-11
              7.4.6       Task Table Structure                         7-11
              7.4.7       Direct References to System Tables           7-14
              7.5       KL8-A SUPPORT                                  7-15

     APPENDIX A         RTS/8 DISTRIBUTED SOURCE FILES AND MNEMONICS   A-1

     APPENDIX B         RTS/8 FLOWCHARTS                               B-1

     APPENDIX C         GLOSSARY                                       C-1

     INDEX                                                         Index-1



                                    FIGURES

     FIGURE   2-1       Message Format and Linking of Messages         2-4
              4-1       Cassette Handler Unit Word Format              4-4
              4-2       Cassette Handler Call Function Word Format     4-5
              4-3       Cassette Handler Status Return Word Format     4-5
              4-4       Cassette Handler Utility Call                  4-7
              4-5       Cassette File Support Handler Unit Word
                        Format                                         4-10
              4-6       Clock Handler Command Word Format              4-14
              4-7       Terminal Handler I/O Mode Command and
                        Length Word Format                             4-20
              4-8       Terminal Handler ASSGN Mode Command Word
                        Format                                         4-20
              4-9       Floppy Disk Handler Unit Word Format           4-27
              4-10      Floppy Disk Handler Status Word Format         4-27
              4-11      LINCtape Handler Unit Word Format              4-31
              4-12      Line Printer Handler I/O Mode Command and
                        Length Word Format                             4-33
              4-13      Line Printer Handler ASSGN Mode Command
                        Word Format                                    4-33
              4-14      Mass Storage Handlers Unit Word Format         4-36
              4-15      Mass Storage Handlers Function Word Format     4-37
              4-16      OS8F Call Function Word                        4-39
              4-17      UDC/ICS Handler Subchannel and Gain Word
                        Format                                         4-48
              4-18      UDC/ICS Handler Subchannel and Value Word
                        Format                                         4-49
              6-1       Nonresident Task Implementation                6-2
              7-1       Executive Internal Task Table Structure        7-12



                                    TABLES

     TABLE    1-1       RTS/8 System Tasks                             1-2
              2-1       Summary of Event Flag States                   2-3

                                       v

                              CONTENTS (Cont.)

                                                                       Page


                                TABLES (Cont.)


     TABLE    3-1       Summary of Executive Requests                  3-2
              3-2       Symbolic Names for Specifying WAITBITS         3-5
              3-3       Summary of Wait States Incurred by Executive
                        Requests                                       3-31
              4-1       Cassette Handler Status Register Bits          4-4
              4-2       Cassette Header Formats                        4-9
              4-3       Clock Handler Commands                         4-12
              4-4       Terminal Handler Commands                      4-18
              4-5       Floppy Status Bit Descriptions                 4-26
              4-6       OS/8 Floppy Disk Interleave Scheme             4-28
              4-7       UDC/ICS Operations                             4-47
              4-8       Generic Code Values                            4-57
              4-9       UDC/ICS Messages                               4-58
              5-1       MCR Command Summary                            5-2
              7-1       Task Switch Flag (TSWFLG) States               7-5
              7-2       Waitbit Descriptions                           7-8



































                                      vi






				    PREFACE


     This manual describes the PDP-8 Real-Time  Operating  System  (RTS/8).
     RTS/8  is a system that you generate using the RTS/8 system generation
     procedures.  The system that you  create  is  individualized  to  your
     needs.   Knowledge  of  PDP-8 assembly language programming (MACREL or
     PAL8) is essential for a complete understanding of  this  manual.   In
     addition, you should be familiar with real-time systems in general and
     with the operation and use of the development system  for  the  PDP-8,
     OS/8. 
     
     This manual only describes how you use  the  RTS/8  operating  system.
     See  the  RTS/8  System  Generation  Manual  for information on how to	       _________________________________
     generate this operating system. 
     
     Chapters 1 and 2 present introductory information.  If you have  never
     used  RTS/8  before,  these chapters present sufficient information so
     that you can place the information in the  remainder  of  this  manual
     into  a  framework.  Also, you should carefully read Section 2.5 which
     overviews the procedure which  you  should  use  when  creating  RTS/8
     tasks. 
     
     Chapter 3 documents RTS/8 Executive Requests.   These  requests  serve
     two  functions:  they  are  the  means by which tasks communicate with
     each other and they are the means by which a  task  communicates  with
     the RTS/8 Executive. 
     
     Chapter 4 discusses the message formats that user tasks must use  when
     they request a DIGITAL-supplied handler to perform an I/O operation. 
     
     Chapter 5 examines the RTS/8 Monitor Console  Routine.   This  routine
     allows you to communicate interactively with an RTS/8 system. 
     
     Chapter 6 describes non-resident tasks.  A non-resident task is a task
     which the Executive brings into memory when it is executable.  You use
     non-resident tasks when memory space is at a premium because more than
     one non-resident task can share the same part of memory. 
     
     The information in Chapter 7,  "Programming  Techniques"  is  for  the
     experienced  PDP-8  user.   You  should  read  it  only  after you are
     familiar with RTS/8. 
     












				      vii




     The following PDP-8 manuals will be helpful for review and reference:
     
	  Introduction to Programming (DEC-08-XINPA-A-D)	  ___________________________

	  OS/8 Handbook (DEC-S8-OSHBA-A-D)	  _____________

	  MACREL/LINK User's Manual (AA-5664B-TA)	  _________________________

	  Small Computer Handbook (90P45)	  _______________________
     
	  PDP-8A Minicomputer Handbook (EB0621976)	  ____________________________
     
	  UDC8 Universal Digital Control Subsystem Maintenance Manual	  ___________________________________________________________
	  (46H745)
     
	  ICS8 Industrial Control Subsystem Maintenance Manual (EKOICS8MM)	  ____________________________________________________
     
     This manual describes how you use an RTS/8 system if  it  was  created
     using  the  RTS/8  system  generation procedures as this procedure was
     distributed by DIGITAL.  Because it is possible to modify  the  System
     Generation procedure, the RTS/8 system that is created may differ from
     the generalized RTS/8 system that this manual  describes.   Therefore,
     you must determine if there are any differences between the system you
     are using and that which the DIGITAL System Generation  procedure  can
     create. 
































				     viii






				   CHAPTER 1

				 INTRODUCTION


     1.1  RTS/8 DESCRIPTION

     RTS/8 is a compact Real-Time System for the PDP-8 family of processors
     (except  for  the  PDP-8S).   This  system allows you to run up to 127
     tasks concurrently, each competing for system resources. 
     
     As do other real-time systems, RTS/8 responds  to  both  internal  and
     external  events.  These events permit timely execution and scheduling
     of tasks.  Thus, you may use RTS/8 for monitoring  and  controlling  a
     number of processes. 
     
     The RTS/8 Executive controls the  execution  and  interaction  of  all
     tasks.   This  Executive  decides  which  tasks should run (basing its
     decisions on the priorities of any  other  runnable  task  or  tasks),
     services these tasks by means of Executive Requests (which are special
     processing routines within the Executive), and administers interactive
     communication. 
     
     RTS/8 includes system tasks that control most  standard  I/O  devices,
     including  RK8,  RK8E,  and  RL01  moving-head  disks,  DF32  and RF08
     fixed-head  disks,  TC08  DECtape,   RX8   floppy   disks,   LINCtape,
     DECcassette,  and  LS8,  LS8E, LP8, and LV8 line printers.  (Note that
     RTS/8 does not  support  TD8E  DECtape.)  These  tasks,  described  in
     Chapter 4, are listed in Table 1-1. 
     
     The Monitor Console Routine (see Chapter  5),  provides  you  with  an
     interface  between  the  console terminal and the system.  The Monitor
     Console  Routine  accepts  a  series  of  interactive  commands  which
     control,  inspect,  and,  to  some  extent, debug the system.  It also
     allows you to schedule  and  execute  tasks  at  specified  intervals,
     suspend task execution, and print system status information. 
     
     RTS/8 also contains a system task that allows a  single  copy  of  the
     OS/8  operating system to run in the background.  Thus, you may create
     a real-time  foreground-OS/8  background  system.  With  OS/8  in  the
     background, you may assemble, debug, edit, and link programs. 













     
				      1-1

			         INTRODUCTION


    				   Table 1-1
			      RTS/8 System Tasks
     
     ----------------------------------------------------------------------
     | Task Name | File Name |		  Task Function			  | 
     |-----------|-----------|--------------------------------------------|
     | _       	 | RTS8.MA   | RTS/8 Executive 				  |
     | CLOCK     | CLOCK.MA  | Clock Handler Task			  |
     | CSA       | CSA.MA    | Cassette Driver Task			  |
     | CSAF      | CSAF.MA   | Cassette File Support Task		  |
     | DTA       | DTA.MA    | TC08 DECtape Driver Task			  |
     | EXIT      | EXIT.MA   | Exit Task				  |
     | LPT       | LPT.MA    | Line Printer Driver Task			  |
     | LTA       | LTA.MA    | LINCtape Driver Task			  |
     | MCR       | MCR.MA    | Monitor Console Routine			  |
     | null task | MCR.MA    | Null Task (contained within MCR)		  |
     | NULL8A  	 | NULL8A.MA | Null Task for PDP-8A			  |
     | OS8       | OS8.MA    | OS/8 Support Task			  |
     | OS8F      | OS8F.MA   | OS/8 File Support Task			  |
     | PWRF      | PWRF.MA   | Power Fail Task				  |
     | RF08/DF32 | RF08.MA   | RF08/DF32 Fixed-Head Driver Task		  |
     | RK8       | RK8.MA    | RK8 Disk Driver Task			  |
     | RK8E      | RK8E.MA   | RK8E Disk Driver Task			  |
     | RL01      | RL01.MA   | RL01 Disk Driver Task			  |
     | RX8A      | RX.MA     | Floppy Disk Handler (1st Controller)	  |
     | RX8B      | RX.MA     | Floppy Disk Handler (2nd Controller)	  |
     | RX8C      | RX.MA     | Floppy Disk Handler (3rd Controller)	  |
     | RX8D      | RX.MA     | Floppy Disk Handler (4th Controller)	  |
     | SWAP      | SWAP.MA   | Nonresident Task Swapper			  |
     | TTY       | TTY.MA    | Terminal Driver Task (1st Driver)	  |
     | TTYl      | TTY.MA    | Terminal Driver Task (2nd Driver)	  |
     | TTY2      | TTY.MA    | Terminal Driver Task (3rd Driver)	  |
     | TTY3      | TTY.MA    | Terminal Driver Task (4th Driver)	  |
     | TTY4      | TTY.MA    | Terminal Driver Task (5th Driver)	  |
     | UDC/ICS   | UDCICS.MA | Universal Digital Controller 		  |
     |           |           | Industrial Controller Subsystem		  |
     |           |           | Handler task 				  |
     |--------------------------------------------------------------------|
     |									  |
     |                   	     NOTE				  |
     |									  |
     |		    TTYl-4  and  RX8A-D  are  not  on  the 		  |
     | 		    distribution Medium.  They are files which		  |
     |		    the RTS/8 System Generation Program			  |
     |		    creates.						  |
     ----------------------------------------------------------------------
     
     RTS/8 supports both resident and nonresident tasks.  (A resident  task
     is  a  task that resides permanently in memory;  a nonresident task is
     one in which a portion of the task resides on a mass storage  device.)
     The  Executive loads a nonresident task into memory only as it becomes
     executable.  By allowing several tasks  to  share  the  same  area  of
     memory,  RTS/8 minimizes the amount of memory that it needs to execute
     user tasks. 


				      1-2

			         INTRODUCTION     


     1.2  REAL-TIME OPERATION

     RTS/8 is a real-time  multiprogramming  system;   that  is,  it  is  a
     software  framework  that allows more than one task to share available
     resources (such as memory, CPU time, and peripheral  devices)  and  to
     respond  to  events  in  real-time.   A  real-time system is a type of
     multiprogramming system that  provides  immediate  or  near  immediate
     response to external events. 
     
     Real-time multiprogramming operations require the precisely  organized
     interaction of the following major elements: 
     
	  o  Executive--the RTS/8 Executive is the kernel of the RTS/8 
	     system;  it is the software that directs task execution. 
     
	  o  Tasks--a task is a sequence of instructions that  directs  the
	     computer in manipulating data to achieve some goal.  Tasks are
	     either user-written or supplied by DIGITAL. 
     
	  o  Memory--memory is the hardware storage medium in  which  tasks
	     actually reside when they execute. 
     
     Multiprogramming allows the execution of  many  tasks  simultaneously. 
     If  a  task is waiting for the completion of an I/O operation (or some
     other condition is blocking it),  and  thus  cannot  use  the  central
     processor,  RTS/8 switches control to another task so that you may use
     available CPU time.  This increases system efficiency;  that  is,  you
     get  more  work  done because no program puts the CPU on hold while it
     waits for an event or information. 
     


























				      1-3




     

				   CHAPTER 2

			    USING TASKS UNDER RTS/8


     2.1  RTS/8 TASKS

     The RTS/8 Executive is the controlling program in  the  RTS/8  system. 
     One  of  its  major  functions is to decide which task should run.  It
     bases its decision on the priorities of the runnable (or active) tasks
     (those  tasks  not waiting for completion of any I/O or other events). 
     It also services tasks by means of Executive Requests.  (See Chapter 3
     for a discussion of Executive Requests.) 
     
     Each task in an RTS/8 system is given a unique  task  priority  number
     when  a  user generates the system.  Up to 127 (177 octal) tasks, each
     with its own task priority, can run at one time.  A task number,  once
     assigned,  cannot  change  during  the  execution  of the RTS/8 system
     because RTS/8 uses a fixed priority system. 
     
     A task priority number serves the following purposes: 
     
	  o  The RTS/8 Executive uses the number as  an  index  to  various 
	     system tables which contain information about each task. 
     
	  o  Other tasks use this number to  reference  a  particular  task
	     when  performing certain Executive Requests (such as sending a
	     message). 
     
	  o  The task number determines the task's priority--the lower  the
	     number, the higher the priority of the task. 
     
     The executive uses five internal tables to maintain information  about
     the tasks in the system.  Chapter 7 discusses these tables. 
     
     
          2.2  CONCEPTS OF TASK COMMUNICATION
     
     RTS/8 is event driven;  that is, the  highest-priority  runnable  task
     executes continuously until: 
     
	  o  It completes its function, or
     
	  o  Some event or condition in the system suspends it.

     Another change or condition can reactivate the task.  (Task scheduling
     is discussed in Section 2.4.) 







     
				      2-1

			    USING TASKS UNDER RTS/8
     
     
		-------------------- NOTE --------------------
	     	|					     |
		|  A task is self-starting if  you  include  |
		|  the  appropriate  instruction within the  |
		|  task (see Section 2.5). A task may  also  |
		|  start  another task, or you may start it  |
		|  at the terminal  console  by  using  the  |
		|  Monitor Console Routine.		     |
		----------------------------------------------     

     RTS/8 performs two main types of task communication: 
     
	  1.  Task synchronization through the use of event flags 
     
	  2.  Intertask messages 
     
     
     2.2.1  Task Synchronization
     
     Whenever two processes execute independently, one process may need  to
     wait  until  the other completes executing.  For example, consider the
     PDP-8 terminal interface.  The PDP-8, when it is ready to  generate  a
     character,  alerts the terminal by issuing a Load Teleprinter Sequence
     (TLS) instruction.  The PDP-8 must now wait in a loop if it wishes  to
     do further I/O immediately.  For example, 
     
	  TSF 	    /SKIP ON TELEPRINTER FLAG
	  JMP.-1
	  .     
	  .     
	  .     
     
     The processor cannot transmit the next character  until  the  terminal
     raises  the  ready  flag  to  signal  that  it  has  printed the first
     character.  When the terminal raises this flag,  the  processor  exits
     from the wait loop and proceeds to load the next character. 
     
     Similarly, RTS/8 provides event flags as signalling  mechanisms.   (An
     event  flag  is  simply  a location which you choose that contains the
     status of an event.) These flags synchronize tasks  with  each  other. 
     The events are either: 
     
	  1.  Physical processes  such  as  a  clock  ticking  or  a  valve
	      closing, or 
     
	  2.  Conceptual occurrences such as a certain string of characters
	      which you type, or the scheduling of a task for execution. 
     
     Like device flags, an event flag can  denote  either  a  "busy"  or  a
     "completed"  state (designated as PENDING and FINISHED, respectively). 
     Thus, a task can direct another task to perform  an  action.   At  the
     time  of  the  request,  it  sets the event flag to the PENDING value. 
     When the  second  task  completes  the  action,  it  issues  the  POST
     Executive  Request.  This  request sets the event flag to the FINISHED
     value, a process known as "posting the event flag." 

				      2-2

			    USING TASKS UNDER RTS/8

     
     As a simple example, if the first task is waiting for the  event  flag
     with the following instructions: 
     
	  TAD event flag  	  /LOAD EVENT FLAG IN AC
	  SZA CLA 		  /IF EVENT FINISHED, SKIP
	  JMP .-2 		  /KEEP TRYING
	  .     
	  .     
	  .     
     
     then the posting of the event flag causes the first task to exit from
     its loop only when the second task completes its processing. 
     
     Since this loop ties up the  PDP-8  processor,  event  flags  have  an
     additional  state, WAITING.  In the above example, the addition of the
     WAITING state now allows the first task to tell  the  RTS/8  Executive
     that  it will wait until the event flag signifies that the second task
     completes the event. 
     
     The WAIT code is as follows:
     
	  CAL 
	  WAITE
	  event flag
     
     (CAL is a system mnemonic meaning JMS 20 and WAITE is the mnemonic for
     the RTS/8 Executive Request that waits for an event flag.) 
     
     The WAIT returns execution control to the task issuing  the  WAITE  if
     the  event  flag  is  zero  (or FINISHED).  If the flag is PENDING (or
     greater than zero), the Executive changes it to WAITING and  the  task
     issuing  the WAITE becomes non-runnable (that is, its WAITBITS word is
     now non- zero). 
     
     If the issuing task sends a message to a second  task,  the  Executive
     automatically  makes  the event flag PENDING when the message is sent. 
     If the issuing task is  using  the  event  flag  to  synchronize  task
     actions,  this task must change the flag to PENDING before issuing the
     WAIT.  (It may set the flag with an ISZ command.) 
     
     Table 2-1 summarizes RTS/8 event flag states.

     
				   Table 2-1
			 Summary of Event Flag States
     
		-----------------------------------------------
		| Event Flag State  |           Value         |
		|-------------------|-------------------------|
		|     FINISHED 	    |   0		      |
		|		    |			      |
		|     PENDING 	    |   > 0		      |
		|		    |			      |
		|     WAITING 	    |   < 0 (4000 + Task No.) |
		-----------------------------------------------
     
				      2-3

			    USING TASKS UNDER RTS/8


     When an RTS/8 Executive Request posts the event flag, the task WAITING
     for  it  is  automatically taken out of Event Flag Wait.  (If no other
     blocking condition exists, the waiting task  is  again  runnable.   It
     resumes execution when higher priority tasks cannot run.) 
     
     
     2.2.2  Intertask Messages
     
     Just as event flags under RTS/8 are similar to hardware device  flags,
     messages  are similar to hardware I/O instructions (for example, TLS). 
     That is, messages start a task (providing that the task is WAITING for
     a message) and, at the same time, they pass information to the task. 
     
     All RTS/8 messages consist of  a  3-word  message  header  immediately
     followed  by the information to be exchanged between the tasks.  (Only
     the RTS/8 system uses the message  header.)  The  first  word  of  the
     message header is the event flag for the message. 
     
     When a task sends a message, the RTS/8 Executive sets the  event  flag
     to the PENDING state.  This signifies that a task has sent the message
     but the task receiving the messages has not  finished  processing  the
     event associated with the flag. 
     
     The  receiving  task  must  post  the  event  flag  when  it  finishes
     performing  the  action signalled by the message.  This posting serves
     two purposes. 
     
	  1.  It informs the task that sent the message (the "sender") that
	      the receiver performed the action. 
     
          2.  It allows the task to send the message  again  (see  Item  2,
	      below). 
     
     If a task is waiting to receive more than one message, RTS/8 uses  the
     second  and  third  words of the message header to link these messages
     together (see Figure 2-1).  The second word  is  a  CDF  (Change  Data
     Field)  instruction  to  the field of the next message.  If the second
     word is 0, then this is the last message. 
     
     The third word of the message is a pointer to the next message. 
     
     If the receiving task is not actively waiting  for  a  message,  RTS/8
     places  the message on the receiving task's "input message queue." The
     Executive queues all messages  that  a  task  receives  in  decreasing
     priority  order.   For  example, the Executive queues a message from a
     priority 3 task ahead of any message sent by another task  except  the
     tasks  with  priorities 1 and 2.  Also, RTS/8 queues messages from the
     same task in the order in which that task issues them. 
     
     Sending a message does not physically move the message information  to
     the receiving task;  instead a SEND operation establishes a pointer to
     the location of the first data word of the message. 
 
     The implications of RTS/8 not moving a message to the receiving task's
     work area are: 

				      2-4

			    USING TASKS UNDER RTS/8


       RTS/8
     EXECUTIVE        MESSAGE	      MESSAGE	      MESSAGE
      MSGTBL		 1		 2		 3
     ---------       ---------       ---------       ---------
     |  CDF  |   --->| Event |   --->| Event |   --->| Event | <-
     |-------|   |   | FLag  |   |   | Flag  |   |   | Flag  |  |
     |  PTR  |----   |-------|   |   |-------|   |   |-------|  |  Message
     ---------       |  CDF  |   |   |  CDF  |   |   |   0   |  |  Header
		     |-------|   |   |-------|   |   |-------|  |
	      	     |  PTR  |----   |  PTR  |----   |       | <-
		     |-------|       |-------|       |-------|
		     |	     |	     |	     |	     |	     | <-
		     |	     |	     |	     |	     |	     |  |
		     |	     |	     |	     |	     |	     |  |  Message
		     |	     |	     |	     |	     |	     |  |  Content
		     ---------	     |	     |	     |	     |  |
		    		     |	     |	     |	     | <-
				     |	     |	     ---------
				     ---------

	       Figure 2-1 Message Format and Linking of Messages 
     

    	  1.  You should not have the sender modify data in a message while 
	      the event flag for the message is PENDING. 
     
	  2.  A task cannot send the same message a second time before  its 
	      event  flag  is FINISHED the first time. (Note, however, that 
	      the task can send other messages while a message is pending.) 
	      RTS/8  enforces  this rule by checking the message event flag 
	      on a SEND Executive Request;  it  puts  the  sender  into  an 
	      Event Flag Wait State if the message is still PENDING. 
     
	  3.  It is legal for the receiving task to  store  information  in 
	      the  body  of  the  message.   In  this  way,  a receiver can 
	      "answer"  without  the  complications  of  sending  a  return 
	      message.   For  example,  when  a task sends a message to the 
	      disk driver  task  requesting  I/O,  the  driver  places  the 
	      operation's  status in a specific word in the message.  Thus, 
	      this word indicates whether an error occurs. 
     
     
     2.3  PRIORITY
     
     The priority of a task  is  established  when  a  user  generates  the
     system.  This number is in the range 1 to 127 (decimal), where a lower
     number indicates a higher priority.  The  highest-priority  task  that
     has  access  to  all  the  resources  it  needs  controls  the central
     processor.  When that  task  becomes  blocked  (to  wait  for  an  I/O
     transfer  to  complete,  for example), the Executive looks for another
     task to use the processor.  The chosen task is the one  that  has  the
     highest priority, has access to all the resources it needs, and is not
     waiting for any event to occur. 


     
				      2-5

			    USING TASKS UNDER RTS/8


     In an RTS/8 installation that mixes real-time applications  with  less
     urgent  work,  the real-time tasks usually have a high priority.  This
     arrangement ensures that the Executive gives CPU time to the real-time
     tasks ahead of other, less urgent tasks. 
     
     
     2.4  TASK INTERRUPTS AND SCHEDULING
     
     A task, once it is running, releases the  CPU  only  if  an  interrupt
     occurs  or  if the task itself issues an Executive Request that places
     it into a wait state. 
     
     An interrupt is a break in the normal operation of the task caused  by
     a  signal  from outside the processor.  When the processor receives an
     interrupt, it looks for the  appropriate  interrupt  service  routine. 
     The  SKPINS  Executive  Request  is  the means by which you link these
     interrupt routines together into a skip chain.  Note  that  this  skip
     chain  is  the  path  which  the  Executive takes when looking for the
     interrupt service routine and is  independent  of  the  tasks  in  the
     system. 
     
     When an interrupt occurs, the Executive follows the skip  chain  until
     it  finds  the  appropriate  interrupt  service  routine.   After  the
     interrupt routine services the request, control returns to either  the
     interrupted  task  or  the  RTS/8 scheduler.  If control passes to the
     scheduler, RTS/8 runs the highest priority task that  is  not  waiting
     for an event or message. 
     
     RTS/8 has a table of reserved words in its Executive.  (Each  word  is
     called a WAITBITS word.) A task is runnable only when this word equals
     zero.  If any bit is nonzero, then the task is waiting for some  event
     to  occur.   The  kinds of events are listed in Table 3-2.  Thus, when
     the WAITBITS equals zero, the Executive can run a  task  because  that
     task  is  not  waiting for an event or action.  This table of reserved
     words is ordered by task priority.  When the RTS/8 scheduler  examines
     this  table,  it  selects  the  highest  priority task that has a zero
     WAITBITS entry.  Therefore, the only time that a higher-priority  task
     can run after control passes to a lower priority task is when: 
     
	  1.  A lower priority task finishes processing the event which  is 
	      the  cause  of a higher-priority event being in a wait state, 
	      or 
     
	  2.  An interrupt service routine removes the  condition  blocking
	      the higher-priority task. 

     
     2.5  CREATING RTS/8 TASKS 
     
     You create RTS/8 tasks in the same manner  as  you  would  create  any
     other  program  on  the PDP-8.  The only influences RTS/8 has on these
     programs are: 
     
	  1.  You must include the MACREL .TASK macro in the task (this  is
	      explained below). 
     
				      2-6

			    USING TASKS UNDER RTS/8


	  2.  If the task is nonresident (see Chapter 6),
     
	  3.  If there is to be intertask communication (see Chapter 3), or 
     
	  4.  If a task uses a DIGITAL-supplied task (see Chapter 4). 
     
     All RTS/8 tasks must include the MACREL .TASK macro.   This  macro  is
     placed  in the parameter file during system generation.  Its source is
     within the SCRIPT.MA  source  program  distributed  with  RTS/8.   The 
     format for calling this macro is: 
     
	  .TASK TASK-NUMBER,TASK-NAME,STARTING-ADDRESS,INITIAL-WAIT,VERSION
     
     where:
     
	  TASK-NUMBER	      is the  RTS/8  task  number  which  you  must
			      supply;   DIGITAL recommends that you use the
			      symbolic name that was or will be  used  when
			      the system is generated.

	  TASK-NAME	      is the symbolic  name  used  when  the  RTS/8
			      system  was  generated.   You  may  omit this
			      parameter.   If  you  omit  it,   the   macro
			      computes this string from TASK-NUMBER.
     
	  STARTING-ADDRESS    is  optional.   If  you  omit  this  symbolic
			      address,  it  defaults  to the START label in 
			      the task. You would  provide  this  value  in 
			      symbolic  form  so  that  MACREL may know the 
			      proper field (as MACREL labels have  a  field 
			      attribute). 
     
	  INITIAL-WAIT	      is an optional value.  If you do not  include
			      this parameter, the task is runnable when you
			      start the RTS/8 system.  You  may  provide  a
			      symbolic  or  absolute  WAITBITS  value  (see
			      Section 3.2.1).   (In  previous  versions  of
			      RTS/8,  it  was obligatory for you to include
			      this value.)
	  VERSION 	      is an optional value.  If  you  include  this
			      value, it is the initial value of the MQ.  If
			      you omit this value, it defaults to the value
			      of the label VERS.
     
     RTS/8 requires Version 2 of MACREL.
     
     Examples:
     
	  .TASK CLOCK
     
     This declaration uses all of the defaults.
     
	  .TASK TEST,,STEST,RUNWT


     
				      2-7

			    USING TASKS UNDER RTS/8


     This declaration is for task TEST which starts  at  symbolic  location
     STEST and is in RUNWT when the RTS/8 system begins running. 
     
     If a task wishes to communicate with another task, it should  use  one
     of  the  RTS/8 Executive Requests.  Chapter 3 describes these requests
     and Table 3-1 summarizes them. 
     
     If a task you write uses one of the DIGITAL-supplied  tasks,  it  must
     send a message to that task.  Chapter 4 presents the formats that your
     tasks must use when they send messages to  these  tasks.   (Chapter  3
     describes the way in which you send these messages.) 
     
     Because you normally create an RTS/8 system that  uses  DIGITAL  tasks
     and  sends  messages  using  Executive Requests, you should create the
     tasks before you generate the RTS/8 system.  DIGITAL  recommends  that
     you  write  and  add tasks to an RTS/8 system one at a time.  That is,
     after you create one task, you should use the RTS/8 System  Generation
     to  create  a minimum system that will support the task.  In this way,
     you can effectively monitor the interaction between tasks as  you  are
     building the RTS/8 system.  Experience has shown that this is the best
     method of locating bugs in real-time systems. 

     
     2.6  RUNNING AN RTS/8 SYSTEM 
     
     In response to the period that the OS/8 monitor prints, type 
     
	  R Sname

     where:
     
	  S     is the default  character  supplied  by  the  RTS/8  System
		Generation program. 
     
	  name 	is the 1  to  5  character  name  supplied  by  the  person 
		building the system. 

     After you type this command, the RTS/8 system is running. 
     
     For more information, see the RTS/8 System Generation Manual.				   ______________________________
     















				      2-8






				   CHAPTER 3

			   RTS/8 EXECUTIVE REQUESTS


3.1  COMMUNICATION WITH THE RTS/8 EXECUTIVE

     RTS/8 tasks communicate with the  RTS/8  Executive  through  Executive
     Requests.  When an RTS/8 system is running, it normally uses locations
     20-27 in a field as the communication region across field  boundaries.
     (However,  if  a field contains OS/8, the Executive does not use these
     locations after OS/8 is running.) You may call the  Executive  in  any
     field via a JMS 20 (or CAL) instruction.


		 -------------------- NOTE --------------------
		 |					      |
		 |  When a user generates an  RTS/8  system,  |
		 |  it included the equate		      |
		 |					      |
		 |	 CAL = JMS 20			      |
		 |					      |
		 |  in its symbol table.   Consequently,  it  |
		 |  is not necessary for you to include this  |
		 |  equate in any task that you may write.    |
		 ----------------------------------------------

     The data field (DF) does not have to be any specific value when a task
     issues a CAL because the code in location 20

	  o  Sets the DF to the instruction field (IF),

	  o  Sets the IF to 0, and

	  o  Jumps to the RTS/8 Executive.

     Table 3-1 gives  a  summary  of  Executive  Requests.   Although  this
     chapter  presents  all  Executive  Requests, full presentations of the
     RESCHED and FREE Executive Requests appear in Chapter 7.

    The RTS/8 Executive does not honor requests to switch tasks  that  come
    from  an  interrupt  if  the interrupted task's program counter (PC) is
    less than 100 (octal).  This prevents a second Executive  Request  from
    destroying  the  RTS/8  Executive's  entry  point  (location 20 in each
    field).  Therefore, no task may  have  instructions  that  the  central
    processor  will  execute  below  location  100  in any field (except as
    noted in Chapter 7).








				      3-1

			   RTS/8 EXECUTIVE REQUESTS


		 -------------------- NOTE --------------------
		 |					      |
		 |  You should not write executable code  in  |
		 |  ZSECTs  that  the linker can place below  |
		 |  location 100 (octal) in a  field.   This  |
		 |  is  usually  a  fatal  error.  Also, you  |
		 |  must not write executable code which has  |
		 |  an  ASECT  that may be linked below 1000  |
		 |  (octal) in  field  0.   These  locations  |
		 |  constitute the RTS/8 Executive.	      |
		 |					      |
		 |  If   you   must    include    executable  |
		 |  instructions in a ZSECT, you must insure  |
		 |  that this code executes  above  location  |
		 |  77 (octal) in every field.  Note that in  |
		 |  the   field   containing    the    RTS/8  |
		 |  Executive,  approximately  one  half  of  |
		 |  page  0  is  available  for  user  code.  |
		 |  Also, if your RTS/8 system has OS/8, you  |
		 |  have   five   auto-increment   registers  |
		 |  available.  If OS/8 is not in the  RTS/8  |
		 |  system, you have six available.	      |
		 ----------------------------------------------

     You use many of the Executive Requests  for  intertask  communication.
     This,  however,  does  not imply that tasks must communicate with each
     other.  A task can execute independently of all other tasks.

				   Table 3-1
			 Summary of Executive Requests
	     -----------------------------------------------------
             |        |	Symbolic  |				 |
             | Code   |   Name    |	      Description	 |
	     |--------|-----------|------------------------------|
             |    0   |  SEND     |  Send a message to a task    |
	     |	      |		  |				 |
             |    1   |  RECEIVE  |  Look for and/or  receive  a |
	     |	      |		  |  message from a task	 |
	     |	      |		  |				 |
             |    2   |  WAITE    |  Wait for any event flag for |
	     |	      |		  |  a   specific   task  to  be |
	     |	      |		  |  posted			 |
	     |	      |		  |				 |
             |    3   |  RUN      |  Run a task			 |
	     |	      |		  |				 |
             |    4   |  SUSPND   |  Suspend execution of a task |
	     |	      |		  |				 |
             |    5   |  POST     |  Post an event flag		 |
	     |	      |		  |				 |
             |    6   |  SKPINS   |  Insert code into  interrupt |
	     |	      |		  |  skip chain			 |
	     -----------------------------------------------------
		                        (continued on next page)



				      3-2

			   RTS/8 EXECUTIVE REQUESTS


			       Table 3-1 (Cont.)
			 Summary of Executive Requests

	     -----------------------------------------------------
             |        |	Symbolic  |				 |
             | Code   |   Name    |	      Description	 |
	     |--------|-----------|------------------------------|
             |    7   |  DERAIL   |  Derail (that  is,  force  a |
	     |	      |		  |  task's  execution  to a new |
	     |	      |		  |  address)			 |
	     |	      |		  |				 |
	     |    8   |  BLKARG   |  Block a task  from  running |
	     |	      |		  |  for a specified reason 	 |
	     |	      |		  |				 |
	     |    9   |  SENDW    |  Send a message and wait for |
	     |	      |		  |  it to be received		 |
	     |	      |		  |				 |
	     |   10   |  UNBARG   |  Signal that a reason that a |
	     |	      |		  |  task    is   blocked   from |
	     |	      |		  |  running no  longer  exists. |
	     |	      |		  |  (A  task may be blocked for |
	     |	      |		  |  more than one reason)	 |
	     |	      |		  |				 |
	     |   11   |  RESCHD   |  Force the  RTS/8  Scheduler |
	     |	      |		  |  to run			 |
	     |	      |		  |				 |
	     |   12   |  WAITX    |  Wait for a particular event |
	     |	      |		  |  flag to be posted		 |
	     |	      |		  |				 |
	     | 4000   |  FREE     |  Allow another task to  take |
	     |	      |		  |  control of a partition	 |
	     -----------------------------------------------------

     WAITM (which is discussed in Chapter 7) is a  special  RTS/8  mnemonic
     you use for waiting for multiple event flags.





















				      3-3

			   RTS/8 EXECUTIVE REQUESTS


     3.2  EXECUTIVE REQUESTS

     --------------					     --------------
     |		  |					     |		  |
     |   BLKARG   | 					     |   BLKARG   |
     |		  --------------------------------------------		  |
     |									  |
     | Use the BLKARG Executive Request to prevent a task from running.	  |
     |									  |
     | Format:								  |
     |	      TAD TSKNUM						  |	
     |	      CAL							  |
     |	      BLKARG							  |
     |	      WAITBITS							  |
     |									  |
     | where:								  |
     |	     TSKNUM    is the number of the task to be blocked.		  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     BLKARG    is an Executive Request mnemonic.		  |
     |	     WAITBITS  is one or more of the values defined in Table 3-2. |
     |									  |
     ----------------------------------------------------------------------

     You prevent a task from running (that is, you block it) by  issuing  a
     BLKARG  Executive Request.  This Executive Request sets one or more of
     the bits in a special, reserved location in a task's Task  Table  (see
     Section  7.3)  called  the Task Flags Word.  The Executive checks this
     location whenever one task calls another or whenever the task is in  a
     runnable position.  Only when this word equals zero is a task runnable.
     
     TSKNUM is a location or literal that contains the number of  the  task 
     to  be  blocked.   If  TSKNUM contains a zero, the issuing task blocks 
     itself.
     

		  ------------------- NOTE -------------------
		  |					     |     
		  | The  TSKNUM=0  form  of  this  Executive |
		  | Request is the only legal way for a task |
		  | to block itself.  If TSKNUM is equal  to |
		  | the issuing task's number, the action of |
		  | this Executive Request is undefined  and |
		  | unpredictable results will occur.	     |
		  --------------------------------------------
     
     The WAITBITS specify one or more bits to be set in a task's Task Flags
     Word.   (They  are called WAITBITS because the bits in the task's Task
     Flags Word  indicate  the  reason  or  reasons  that  a  task  is  not 
     runnable.)  Note  that  a  task is runnable only when this word equals 
     zero.
     
     Symbolic  names  for  specifying  the  conditions  for  blocking  (and
     unblocking)  a  task in the WAITBITS word are given in Table 3-2.  The
     symbolic names listed in the table are equates  established  when  the
     system was generated.
     
				      3-4

			   RTS/8 EXECUTIVE REQUESTS


				   Table 3-2
			Symbolic Names for Specifying WAITBITS

     ----------------------------------------------------------------------
     | Symbolic  |	   |						  | 
     |   Name    |  Value  |		 	    Meaning		  |
     |-----------|---------|----------------------------------------------|
     |  NONRWT   |  4000   |  Nonresident  Wait--this  task  cannot  run  |
     |		 |	   |  because it is not in memory.		  |
     |		 |	   |						  |
     |  EFWT     |  2000   |  Event Flag Wait--this task is  waiting  for |
     |		 |	   |  an  event  flag  (which  contains a WAITING |
     |		 |	   |  value corresponding to  this  task)  to  be |
     |		 |	   |  posted.					  |
     |		 |	   |						  |
     |  RUNWT    |  1000   |  Run Wait--This task is waiting for a RUN ER |
     |		 |	   |  to  be  executed with its number in the AC, |
     |		 |	   |  or for the operator to type a REQUEST  task |
     |		 |	   |  command to the Monitor Console Routine (see |
     |		 |	   |  Chapter 5).				  |
     |		 |	   |						  |
     |  SWPWT    |  0400   |  Swap Wait--This task cannot run because  it |
     |		 |	   |  is  in  the  process  of being brought into |
     |		 |	   |  memory.					  |
     |		 |	   |						  |
     |  EORMWT   |  0200   |  Event or Message Wait--This task is waiting |
     |		 |	   |  for an event flag to be posted or a message |
     |		 |	   |  to arrive, whichever happens first.	  |
     |		 |	   |						  |
     |  USERWT   |  0100   |  User Wait--This bit is reserved for use  by |
     |		 |	   |  user-written  tasks.   RTS/8  does  not use |
     |		 |	   |  this bit.					  |
     |		 |	   |						  |
     |  ENABWT   |  0040   |  Enable Wait--This task  is  waiting  to  be |
     |		 |	   |  enabled.   Used only by the Monitor Console |
     |		 |	   |  Routine.  (See Chapter 5 for an explanation |
     |		 |	   |  of the ENABLE and DISABLE commands.)	  |
     |		 |	   |						  |
     |  MSGWT    |  0020   |  Message Wait--This task is  waiting  to  be |
     |		 |	   |  sent a message.				  |
     |		 |	   |						  |
     |           |  0010   |  Reserved for future expansion.		  |
     |		 |	   |						  |
     |           |  0004   |  Reserved for future expansion.		  |
     |		 |	   |						  |
     |           |  0002   |  Reserved for future expansion.		  |
     |		 |	   |						  |
     |  DNEWT    |  0001   |  Task does not exist.  A  user  task  should |
     |		 |	   |  never set or clear this bit.		  |
     ----------------------------------------------------------------------






				      3-5

			   RTS/8 EXECUTIVE REQUESTS
        Examples:

     You place task 14 into User Wait by executing the following code.

	  TAD	  (14)
	  CAL
	  BLKARG
	  USERWT

     Task PRINT is placed into Run Wait by executing the following code.

	  TAD (PRINT)
	  CAL
	  BLKARG
	  RUNWT











































				      3-6

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   DERAIL   |					     |   DERAIL	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the DERAIL Executive Request to modify the execution of a task |
     | by  transferring  control  to  a special subroutine when that task |
     | becomes runnable.						  |
     |									  |
     | Format:								  |
     |	      TAD TSKNUM						  |
     |	      CAL							  |
     |	      DERAIL							  |
     |	      ADDR							  |	
     |									  |
     | where:								  |
     |	     TSKNUM    is the number of the task to be derailed.	  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     DERAIL    is an Executive Request mnemonic.		  |
     |	     ADDR      is the actual or symbolic starting location of the |
     |	      	       subroutine.     					  |
     |									  |
     ----------------------------------------------------------------------

     You use the DERAIL Executive Request to force a task's execution to  a
     new  address.   This  address  is  normally  the  address of a special
     subroutine of the task.  Note that this Executive Request does not set
     or clear any of the WAITBITS.
     
     The DERAIL Executive Request simulates a "JMS ADDR" for the task whose
     number  is in location TSKNUM (which is the derailed task).  Note that
     RTS/8 assumes that ADDR is in the same field  as  the  derailed  task.  
     The  Executive  stores  the  derailed task's program counter (from its 
     Task State Table entry) in location ADDR, and also  sets  the  program 
     counter entry in its Task State entry to ADDR + 1.
     
     Two important points concerning the operation of the DERAIL  Executive
     Request are:
     
	  1.  The DERAIL  Executive  Request does  not  save  the  derailed 
	      task's   accumulator,   link,   and   data   field  settings;  
	      therefore, the derail subroutine must save and restore  these 
	      values.  In this sense, a derail subroutine is very much like 
	      an interrupt at the task level.
     
	  2.  DERAIL does not alter the contents  of  the  derailed  task's 
	      Task Flags word.  If the derailed task is not runnable, RTS/8 
	      does not execute the derail subroutine until the task becomes
	      runnable.
     
     Generally, a high priority task uses the DERAIL Executive  Request  to
     signal  lower priority tasks that an emergency condition occurred.  As 
     an example, it is sometimes necessary to  abort  all  processes  in  a 
     process-control  environment  if  the  room  temperature  exceeds some 
     critical  value.   You  may  program  a  task  that  checks  for  this 

				      3-7

			   RTS/8 EXECUTIVE REQUESTS


     temperature  every ten seconds.  However, it is inefficient to include 
     shutdown code in this "watchdog  task"  for  all  machinery  that  the 
     processor  controls.   A   better solution is to provide a location to 
     which each equipment-controlling task can be derailed in order to shut 
     down its own piece of equipment.

     Example:
     
     An example of a derail subroutine is as follows:
     
          DENTRY, 0       	      /DERAIL ROUTINE ENTRY POINT
		  DCA SAVAC           /SAVE AC
		  RAR
		  DCA SAVLNK          /SAVE LINK
		  RDF
		  TAD (CDF)
		  DCA SAVDF           /SAVE DATA FIELD
		  CDF .FLD
		  .       	      /HANDLE EMERGENCY CONDITION
		  .
	 	  .		      /BRANCH TO "RESUME" IF YOU WANT
		  .		      / TO RESUME WHERE YOU LEFT OFF
		  .       	      /BRANCH TO "NOGO" IF NOT
	  RESUME, TAD SAVLNK          /RESTORE LINK
		  CLL RAL
		  TAD SAVAC
	  SAVDF,  HLT      	      /RESTORE DF
		  JMP I DENTRY        /RESUME (SAME FIELD)
	  NOGO,   CLA CLL
		  CDF .FLD
		  JMP RESTRT          /RESTART TASK
	  SAVAC, 0
	  SAVLNK, 0

     
			       Dangers of DERAIL
     
     A task can get into serious trouble if the Executive derails it  while
     it  is  already  in  a  derail routine.  If this situation occurs, the
     original processor state is lost.  There is no simple solution to this
     problem.   You  cannot  simply  turn  off the interrupts in the derail
     routine;  a second derail may occur before the Executive executes  the
     first  derail  routine.  Consequently, you must ensure that a task can
     only be derailed by one other task in the system.
     

			   Restrictions Using DERAIL
     
     If a task is not runnable, derailing it does  not  make  it  runnable.  
     For  example,  if a task is in Event Flag Wait, it will remain in this 
     state until the event occurs.  When the task finally posts  the  event 
     flag,  the  receiving  task  wakes  up and begins to run in its derail 
     routine rather than in the mainline routine.  Thus, derailing  a  task 
     so  that  it can perform some important job immediately may not always 
     work because a task may be in a wait state and not be able to run  for 

				      3-8

			   RTS/8 EXECUTIVE REQUESTS


     some  time.  For example, if the task were in Message Wait at the time 
     of the DERAIL Executive Request, the  derail  routine  would  not  run
     until  a  message  came  in for that task.  Furthermore, if some event 
     causes the routine sending the message to shut off, then the receiving 
     task will never run.
     
     A partial solution to this restriction is  to  code  the  task  to  be
     derailed  so  that  it  always  waits  for  events  by using the WAITX
     Executive Request instead of WAITE.  If you subsequently  derail  this
     task, it is first taken out of MSGWT or EORMWT and then derailed.
     
     An example of the code for this situation is as follows:

	  TAD TSKNUM
	  CAL
	  DERAIL
	  DENTRY  		  /DERAIL ADDRESS
	  TAD TSKNUM
	  CAL
	  UNBARG  		  /UNBLOCK THE TASK FROM
	  MSGWT ! EORMWT  	  / MESSAGE-RELATED WAITS
	  .
	  .
	  .
	  CAL
	  WAITX
	  EFLAG
	  .
	  .

     This works because both the RECEIVE and the WAITX  Executive  Requests
     move  the program counter back to the location of the CAL before going
     into a wait state.  Thus, no harm can occur if the Executive takes the
     task  out  of  that wait state for an incorrect reason.  When the task
     resumes running at that point, it  re-executes  the  CAL  (RECEIVE  or
     WAITX)  and  goes  back into the wait state as necessary.  This method 
     does not work if the task was in  Event  Flag  Wait  due  to  a  WAITE 
     Executive Request because the task would resume running as if the task 
     posted the event flag when, in fact, it had not.  A way to  circumvent 
     this problem (other than WAITX) is for the task to do WAITM instead of 
     a WAITE, and then poll the event  flag  upon  waking  up.   (WAITM  is 
     discussed in Chapter 7.)














				      3-9

			   RTS/8 EXECUTIVE REQUESTS



     --------------					     --------------
     |		  |					     |		  |
     |    FREE	  |					     |    FREE	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the FREE Executive Request to indicate that the Executive  can |
     | swap  a nonresident task out of a partition if another nonresident |
     | task wishes to use it.						  |
     |									  |
     | Format:								  |
     |	      CAL							  |
     |	      COMMND+FREE     						  |
     |									  |
     | where:								  |
     |	     CAL       is an RTS/8 mnemonic.				  |
     |	     COMMND    is an Executive Request that can put a task into a |
     |		       wait state.					  |
     |	     FREE      is an Executive Request mnemonic.		  |
     |									  |
     ----------------------------------------------------------------------

     When a nonresident task is in a wait state, you should  allow  another
     nonresident request to use its memory partition if it needs to.  Thus,
     the FREE Request tells  the  Executive  that  it  can  swap  the  task
     currently  in  a  portion  of memory to the swapping device if another
     task is ready to execute in the same partition. 
     
     If no other nonresident task is ready to run, the Executive  does  not
     swap out the task currently in memory. 
     
     If the Executive Request to which you append the FREE Request does not
     put  the nonresident task into a wait state, the Executive ignores the
     FREE request. 
     
     Section 6.2.1 discusses the FREE request.




















				     3-10

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |    POST	  |					     |    POST	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the POST Executive  Request  to  set  an  event  flag  to  the |
     | FINISHED (zero) state.						  |
     |									  |
     | Format:								  |
     | 	      TAD EFPTR   /POINTER TO EVENT FLAG			  |
     | 	      CAL							  |
     | 	      POST							  |
     | 	      CDF EFFLD   /FIELD OF EVENT FLAG				  |
     |									  |
     | where:								  |
     |	     EFPTR     is the location of the event flag.		  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     POST      is an Executive Request mnemonic.		  |
     |	     EFFLD     is the field of the event flag.			  |
     |									  |
     ----------------------------------------------------------------------

     A task signals that it has received a message or completed an event by
     using a POST Executive Request. 
     
     The POST Executive Request sets the  event  flag  pointed  to  by  the
     accumulator  in  the field of the CDF to the FINISHED (or zero) state. 
     If its previous state was WAITING, the POST Executive  Request  clears
     the  event  flag wait bit of the waiting task's WAITBIT.  (This is the
     EORMWT bit.) It also sets the PENDING flag to  zero.   This  Executive
     Request  never places the calling task into a wait state.  If the task
     waiting for the event flag has a  higher  priority  than  the  calling
     task,  the  Executive  transfers  control to the higher priority task. 
     Note that the lower priority task remains runnable;  that is, none  of
     its  WAITBITS  are  set.   However, this lower-priority task runs only
     when no other higher priority task is runnable. 
     
     See Section 3.3 for an example of the POST Executive Request.


















				     3-11

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   RECEIV	  |					     |   RECEIV	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use a RECEIV Executive Request to specify that a task is to  await |
     | a message before proceeding.					  |
     |									  |
     | Format:								  |
     | 		     TAD TSKNUM						  |
     | 		     CAL						  |
     | 		     RECEIV						  |
     |        MADDR, 0							  |
     |									  |
     | where:								  |
     | 	     TSKNUM    is the task from which  the  receiving  task  will |
     |                 receive  a message; or, if TSKNUM equals zero, the |
     |                 task can receive a message from any task.	  |
     |         CAL     is an RTS/8 mnemonic for JMS 20.			  |
     |         RECEIV  is an Executive Request mnemonic. 		  |
     |         MADDR   is the address of the message.			  |
     |									  |
     ----------------------------------------------------------------------

     The RECEIV Executive Request is the means by which a  task  tells  the
     Executive  that  it wishes to receive a message.  The Executive places
     both the address of the message in MADDR and a CDF  to  the  message's
     field in the accumulator. 
     
     If the accumulator is zero when a task  issues  the  RECEIV  Executive 
     Request, the RTS/8 Executive examines the calling task's (that is, the
     task executing the RECEIV) input message queue.  If there are messages
     in  the  calling task's input message queue, the Executive removes the
     first (i.e., the highest priority) message from the queue  and  places
     the  address of its first data word in MADDR.  It also stores a CDF to
     the field of the message in the accumulator. 
     
     If the accumulator is nonzero when a task issues the RECEIV  Executive
     Request,  the  Executive  searches  the  calling  task's input message
     queue.  It looks for a message whose sender's task number is the  same
     as  the  number  in  the  accumulator.  If it finds such a message, it
     removes it from the queue as specified above;  if it does not  find  a
     message, it places the issuing task in Message Wait. 
     
     		  ------------------- NOTE -------------------
		  |					     |     
		  | When a task is  in  Message  Wait  after |
		  | executing a  RECEIV  Executive  Request, |
		  | its  program  counter,  as stored in the |
		  | Task  State  Table  (see  Section  7.3), |
		  | points  back  to the location containing |
		  | the CAL.  Thus, when a message comes in, |
		  | the    task   re-executes   the   RECEIV |
		  | Executive  Request   and   accepts   the |
		  |					     |

				     3-12

			   RTS/8 EXECUTIVE REQUESTS


		  |					     |
		  | message.   This  mechanism  is  normally |
		  | transparent.  One implication is that no |
		  | harm  is  done  by  taking a task out of |
		  | Message  Wait  because,  once  the  task |
		  | starts  up again, it will re-execute the |
		  | RECEIV Executive  Request  and  go  back |
		  | into Message Wait. 			     |
     		  --------------------------------------------

     Normally, if there are no messages in the input message queue  when  a
     task performs a RECEIV, the task is put into Message Wait.  However, a
     1 in bit O of the accumulator (i.e., the accumulator is negative) when
     a task issues a RECEIV indicates that the task is not willing to wait.
     With  no messages in the input message queue (or none sent by the task
     whose number is in the accumulator), the task will continue to run (at
     location CAL + 3) with the accumulator equal to zero.   Thus,  a  zero
     accumulator  is  the means by which the RTS/8 Executive informs a task
     that there are no messages (of the desired type) PENDING. 
     
     A major restriction in using this Executive Request  is  that  a  task
     cannot  send  the  same message twice.  If a task attempts to send the
     same message a second time, the Executive prevents  this  action  from
     occurring  by  placing  the  task  in  Event Flag Wait until the first
     instance of the message has been processed  and  posted.   The  second
     instance  of  the  message  is then sent and the Executive removes the
     offending task from Event Flag Wait.  However,  if  the  same  message
     (that  is,  the  same event flag) is sent by two separate tasks, RTS/8
     may stop executing as this is probably a user error.  If this  occurs,
     you must reload the RTS/8 system.
    
     See Section 3.3 for an example of the RECEIV command.
























				     3-13

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   RESCHD	  |					     |   RESCHD	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the RESCHD Executive Request to force the RTS/8  scheduler  to |
     | run.								  |
     |									  |
     | Format:								  |
     | 	      CAL							  |
     |	      RESCHD							  |	
     |									  |
     | where:								  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     RESCHD    is an Executive Request mnemonic.		  |
     |									  |
     ----------------------------------------------------------------------

     You use the RESCHD Executive Request in conjunction with writing  code
     that  more than one task uses.  After a task finishes manipulating the
     shared code, you must check certain conditions and go directly to  the
     RTS/8  scheduler.   Checking  these  conditions is the function of the
     RESCHD Executive Request.

     Section 7.1.2 discusses the RESCHD request.































				     3-14

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |    RUN	  |					     |    RUN	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the RUN Executive Request to run a task.			  |
     |									  |
     | Format:								  |
     |	      TAD TSRNUM						  |
     |	      CAL							  |
     |	      RUN							  |
     |									  |
     | where:								  |
     |	     TSKNUM    is the number of the task to be run.		  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     RUN       is an Executive Request mnemonic.		  |
     |									  |
     ----------------------------------------------------------------------

     The RUN Executive Request is equivalent to the following instructions:

	  TAD TSKNUM
	  CAL
	  UNBARG
	  RUNWT

     This request exists because the Executive performs this function often
     enough  to justify a shorthand version.  See the UNBARG discussion for
     more information.

     An example of the RUN Executive Request is included  with  the  SUSPND
     discussion.
























				     3-15

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |    SEND	  |					     |    SEND	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the SEND Executive Request to send a message to a task.	  |
     |									  |
     | Format:								  |
     | 	      CAL							  |
     |	      SEND							  |
     |	      TSKNUM							  |
     |	      MESSAG							  |
     |									  |
     | where:								  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     SEND      is an Executive Request mnemonic.		  |
     |	     TSKNUM    is the number of the task to which  a  message  is |
     | 		       being sent.					  |
     |	     MESSAG    is the location of the message being sent.	  |
     |									  |
     ----------------------------------------------------------------------

     The SEND Executive Request sends the location of the message  labelled
     MESSAG in the field of the CAL instruction to the task whose number is
     TSKNUM.  If the receiving task has a higher priority than  the  sender
     and is waiting for a message, RTS/8 transfers control to the receiver.
     If this occurs, the sending task is still runnable;  however, it  does
     not  regain  control  of the processor until all other higher priority
     tasks are in a wait state. 
     
     A SEND Executive Request places the event flag into a  PENDING  state.
     If  the event flag in location MESSAG is already PENDING (that is, the
     event flag is nonzero and the message is still busy  from  a  previous
     SEND),  the sender is put into Event Flag Wait on location MESSAG, and
     the Executive only performs the  SEND  when  the  event  flag  becomes
     FINISHED (zero).  You should ensure that only one task sends a message
     because the Executive remembers only the last request to send a "busy"
     message;   the  first  task  could  then remain permanently dormant in
     Event Wait because the Executive took the  wrong  task  out  of  Event
     Wait.  Only after a task acknowledges receipt can the task (or another
     task) send the same message. 
     
     See Section 3.3 for an example of the SEND command.













				     3-16

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   SENDW	  |					     |    SENDW	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the SENDW Executive Request to send a message and to wait  for |
     | an acknowledging response.					  |
     |									  |
     | Format:								  |
     |	      CAL							  |
     |	      SENDW							  |
     |	      TSKNUM							  |
     |	      MESSAG							  |
     |									  |
     | where:								  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     SENDW     is an Executive Request mnemonic.		  |
     |	     TSKNUM    is the number of the task that  will  receive  the |
     |		       message.						  |
     |	     MESSAG    is the address of the first word of the message.   |
     |									  |
     ----------------------------------------------------------------------

     The SENDW Executive Request is equivalent to a SEND Executive  Request
     followed  immediatly by a WAITE Executive Request;  that is, the SENDW
     Executive Request is equivalent to the following sequence: 

	  CAL
	  SEND    	  /SEND THE MESSAGE
	  TSKNUM
	  MESSAG
	  CAL
	  WAITE   	  /WAIT FOR RECEIVER TO ACKNOWLEDGE
	  MESSAG

     See the SEND and WAITE discussions for further information.




















				     3-17

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   SKPINS	  |					     |   SKPINS	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the SKPINS Executive Request to insert an interrupt processing |
     | routine into the interrupt skip chain.				  |
     |									  |
     | Format:								  |
     |	      CAL							  |
     |	      SKPINS							  |
     |	      MODULE							  |
     |									  |
     | where:								  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     SKPINS    is an Executive Request mnemonic.		  |
     |	     MODULE    is the  address  (in  the  current  field)  of  an |
     |		       interrupt processing routine.			  |
     |									  |
     ----------------------------------------------------------------------

     The RTS/8 Executive is able to receive and dismiss hardware interrupts
     and  to  perform  interrupt-initiated task switching. However, it does
     not provide room for an interrupt skip chain.  Instead, the skip chain
     is  literally a chain which the Executive dynamically builds at system
     start-up time using SKPINS Executive Requests  which  you  include  in
     tasks. 
     
     Whenever a task executes a SKPINS  Executive  Request,  the  Executive
     inserts  the interrupt routine at the end of the interrupt skip chain. 
     (This is usually done by tasks at system start-up time only.) The last
     interrupt  routine  which  the  Executive  includes  in the skip chain
     points to the RTS/8 interrupt dismiss routine as its "next module." In
     this  way,  you control the order in which RTS/8 links the skip chain.
     This means that the Executive encounters most-used  interrupts  first. 
     For  example,  if  a  task  is  not  runnable at system start- up, the
     Executive places its interrupt routine into the chain  only  when  the
     task becomes runnable. 
     
     SKPINS always inserts the interrupt routine at the  end  of  the  skip
     chain, and you usually execute a SKPINS Executive Request in a task as
     "once-only" code at system start-up time.  Therefore, if all tasks are
     runnable,  RTS/8  links  the routines in the skip chain by priority of
     the task which inserts them. 
     
     Note that the order of  the  skip  chain  can  differ  from  the  task
     priority  order.   If  a higher-priority task is not runnable when you
     start up the system, then the Executive may link  a  task's  interrupt
     routine  into  the  skip chain in a position that is farther away from
     the beginning of the chain than that of a lower-priority request.   It
     is important to remember that the function of the skip chain is not to
     order the priorities but rather the path that the Executive takes when
     it looks for an interrupt processing routine. 


     
				     3-18

			   RTS/8 EXECUTIVE REQUESTS


     If you wish to control the order of the skip chain, you should  create
     an RTS/8 system that contains only one runnable task when you start-up
     the system.  The function of this task  would  be to  make  the  tasks
     runnable in the order in which interrupt routines should link into the
     skip chain.  This task should then block itself permanently after  the
     Executive  links  all  tasks.   For example, you may use the following
     code to block a task permanently. 
     
	  CLA
	  CAL
	  BLKARG
	  (-1)

     After this code executes, this task blocks itself on all the  WAITBITS
     and frees its partition. 
     
     Once  an  interrupt  routine  receives  control,  there  are   several
     restrictions on its execution: 
     
	  1.  The interrupt routine must  clear  the  interrupt's  hardware
	      flag.
     
	  2.  The interrupt routine is entered  with  the  Data  Field  and
	      Instruction  Field  of  the next interrupt routine;  you must
	      correct this--as shown in the  example  interrupt  processing
	      routine  example  following  this  list--before the processor
	      executes any indirect addressing.
     
	  3.  An interrupt  routine  can  not  issue  any  RTS/8  Executive
	      Requests.
     
	  4.  An  interrupt  routine  must  not  compute  excessively  when
	      interrupts  are  off.  Typical execution time should be under 
	      75 microseconds.  If  you  need  considerably  more  computer 
	      time,  you  should schedule a task to perform this processing 
	      by posting an event flag.  You use a POSTDS instruction  (see 
	      7 below) to wake up the task.
     
	  5.  Interrupt routines must not  turn  on  interrupts  because  a 
	      second   interrupt   destroys  the  processor  state  of  the 
	      interrupted task.
     
	  6.  Upon entering the interrupt routine, the Executive saves  the
	      processor  state.   However,  it may not save the contents of 
	      the Multiplier Quotient, EAE, FPP, etc.  Therefore, interrupt
	      routines  requiring the use of these resources must save them
	      before processing the interrupt, and then restore them before
	      leaving the interrupt routine.
     
	  7.  Interrupt routines should dismiss the  interrupt  by  setting 
	      the  Instruction  Field  to  RTS8 (which is a system mnemonic 
	      that equals the field in which the RTS/8  Executive  resides) 
	      and issuing a POSTDS instruction.  (POSTDS is simply an RTS/8
	      mnemonic for JMP I 24.)  When  the  Executive  dismisses  the
	      interrupt,  it  can  post  an  event flag by setting the Data 

				     3-19

			   RTS/8 EXECUTIVE REQUESTS


	      Field to the field of the event flag and placing the location 
	      of  the  event  flag  in the accumulator prior to issuing the
	      POSTDS.
     
	      For example,
     
		  CDF .FLD          /DF = THIS FIELD
		  TAD (EVFLG)       /EVFLG CAN NOT BE AT LOCATION 0
		  CIF RTS8	    /RTS8 = EXECUTIVE FIELD
		  POSTDS	    /DISMISS INTERRUPT AND POST EVFLG
     
     If an interrupt routine will not  post  an  event  flag,  the  routine
     should  clear the accumulator prior to issuing the POSTDS instruction. 
     In this case, the data field DF is irrelevant. 
     
     The following  example  illustrates  the  structure  of  an  interrupt
     processing routine: 

	  MODULE, 0		     /THIS WORD GETS A POINTER
				     /   TO THE NEXT MODULE
		  0		     /MODULE ENTERED HERE--CONTAINS
				     /   CDF CIF TO NEXT MODULE FIELD
		  SKDR		     /SKIP ON DEVICE READY
		  JMP I MODULE	     /NOT READY--GO TO NEXT MODULE
				     /   IN CHAIN
		  CDF CIF .FLD	     /THIS ONE IS MINE--SET DF AND IF
				     /   CORRECTLY
		  .
		  .		     /INTERRUPT PROCESSING
		  .
		  CIF RTS8	     /DISMISS THE INTERRUPT, MAYBE
		  POSTDS 	     /   POST AN EVENT FLAG DEPENDING
				     /   UPON THE CONTENTS OF THE AC

     Using the above interrupt format, an RTS/8 Paper  Tape  Punch  handler
     task might contain the following sections of code: 
     
     In the initialization code (contained in a task that  is  runnable  at
     system start-up time):

	  START,  CAL		     /LINK THE PUNCH SKIP
		  SKPINS  	     /   INTO THE SKIP CHAIN
		  PTPINT
	  GETREQ, CAL
		  RECEIVE	     /WAIT FOR MESSAGE
		  .
		  .
		  .

     As a character punch subroutine used by the main body of the task:






				     3-20

			   RTS/8 EXECUTIVE REQUESTS


	  PUNCH,  0		     /ENTER WITH CHAR IN AC
		  DCA CHAR	     /SAVE CHAR
		  CAL		     /WAIT UNTIL PUNCH IS READY
		  WAITE
		  PTPEF		     /SET PUNCH EVENT FLAG
		  ISZ PTPEF	     /   TO THE PENDING STATE
		  TAD CHAR
		  CIF RTS8	     /SET INSTRUCTION FIELD TO THAT
				     /   OF RTS8 EXECUTIVE
		  PLS		     /LOAD PUNCH BUFFER SEQUENCE
		  CLA
		  JMP I PUNCH	     /RETURN
		  .
		  .
		  .

     In the interrupt skip chain code:

	  PTPINT, ZBLOCK 2	     /USED TO CHAIN SKIPS
		  PSF		     /CHECK PUNCH FLAG
		  JMP I PTPINT	     /NOT READY
		  CDF CIF .FLD	     /SET CORRECT DF, IF
		  PCF		     /CLEAR PUNCH FLAG -
		  TAD (PTPEF)
		  POSTDS	     /DISMISS INTERRUPT,
		  .		     /   POSTING PTPEF
		  .
		  .
	  PTPEF,  0		     /PUNCH INITIALLY READY
	  CHAR,   0

                  ------------------- NOTE -------------------
		  |					     |
	          | RTS/8 does not provide a  mechanism  for |
		  | removal  of  entries  from the interrupt |
		  | skip chain.				     |
		  --------------------------------------------



















				     3-21

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   SUSPND	  |					     |   SUSPND	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the SUSPND Executive Request to suspend  the  execution  of  a |
     | task.								  |
     |									  |
     | Format:								  |
     | 	      TAD TSKNUM						  |
     |	      CAL							  |
     |	      SUSPND							  |
     |									  |
     | where:								  |
     |	     TSKNUM    is the number of  the  task  to  be  blocked  from |
     |		       running.						  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     SUSPND    is an Executive Request mnemonic.		  |
     |									  |
     ----------------------------------------------------------------------

     The  SUSPND  Executive  Request  is  equivalent   to   the   following
     instructions:

	  TAD TSKNUM
	  CAL
	  BLKARG
	  RUNWT
     
     This Executive Request exists  because  the  Executive  performs  this
     function  often enough to justify a shorthand version.  See the BLKARG
     discussion for more information.
     
     The following example shows how you use SUSPND in a task:
     
     A data collection task is to print a report  every  1000  data  points
     without interrupting the data collection/reduction process.  At system
     start-up, the report generation task comes  up  running;   this  means 
     that the first report occurs when it first receives information.
     
     (In this simplified example, the data upon which  the  report  program
     operates may have been already updated for the next cycle before being
     reported.  A full example  would  require  a  scheme  such  as  double
     buffering to protect the data.)










     

				     3-22

			   RTS/8 EXECUTIVE REQUESTS


			       Data Control Task
     
	  DLOOP,     TAD (-1750)     /1000 DECIMAL
		     DCA COUNT
	  DATALP,    CAL
		     WAITE
		     DATAEF  	     /WAIT FOR DATA READY
		     .		     /   CODE TO STORE DATA
		     .		     /   POINT IN BUFFER
		     .		     /GET A DATA POINT
		     ISZ COUNT       /   AND PROCESS IT
		     JMP DATALP      /COUNT OFF 1000 POINTS
		     TAD (REPORT)
		     CAL	     /RUN REPORT TASK
		     RUN
		     JMP DLOOP       /KEEP COLLECTING
	  COUNT,     0
     

			    Report Generation Task
     
	  RLOOP,     CAL	     /AC=0, SUSPEND
                     SUSPND	     /   UNTIL NEEDED
                     JMS TITLE       /HAS BEEN RUN
		     .     
		     .		     /PRINT REPORT
		     .		     /   WITH TITLE
		     JMP RLOOP	     /REPORT OVER; GO BACK
				     /   AND WAIT
     
     To eliminate interference with the data collection, REPORT should have
     a lower priority than DATA.























     
				     3-23

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   UNBARG	  |					     |   UNBARG	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the UNBARG Executive  Request  to  specify  that  a  condition |
     | preventing a task from running no longer exists.			  |
     |									  |
     | Format:								  |
     |	      TAD TSKNUM						  |
     |        CAL							  |
     |        UNBARG							  |
     |        WAITBITS							  |
     |									  |
     | where:								  |
     |	     TSKNUM    is the number of the task to be unblocked.	  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |       UNBARG    is an Executive Request mnemonic.		  |
     |	     WAITBITS  is one or more of the values defined in Table 3-2. |
     |									  |
     ----------------------------------------------------------------------

     You use the UNBARG Executive Request to clear one or more  bits  in  a 
     task's  Task  Flags  Word.  These bits represent reasons why a task is
     not runnable.  Note that a task may not be running because of  several
     conditions;   executing  an UNBARG upon one condition may not make the
     task runnable.  A task can be runnable only if all  of  the  bits  are
     zero. 
     
     TSKNUM contains the number  of  the  task  to  unblock,  and  WAITBITS
     specifies  one  or more bits to be cleared in task TSKNUM's Task Flags
     word.  If the Task Flags  word  becomes  zero  as  a  result  of  this
     operation,  TSKNUM becomes runnable.  Note that if TSKNUM has a higher
     priority than the issuing task and  becomes  runnable,  the  Executive
     transfers  control  to  the  higher priority task.  The lower priority
     task remains runnable;   that  is,  none  of  its  WAITBITS  are  set. 
     However,  the  lower  priority task will run only when no other higher
     priority task is runnable. 
     
     This Executive Request is a no-op (no operation) if it  has  a  TSKNUM
     equal to the issuing task's number. 
     
     Example:
     
     The Executive takes task 14 out of User  Wait  when  it  executes  the
     following code.
     
	  TAD (14)
	  CAL
	  UNBARG
	  USERWT
     
     However, if task 14 had been blocked with the following code


     
				     3-24

			   RTS/8 EXECUTIVE REQUESTS


	  TAD (14)
	  CAL
	  BLKARG
	  USERWT ! RUNWT
     
     then the execution of the above UNBARG would  not  unblock  this  task
     because the UNBARG does not clear the RUNWT bit.

















































				     3-25

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   WAITE	  |					     |   WAITE	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use a WAITE Executive Request to wait for any event flag for  this |
     | task to be posted.						  |
     |									  |
     | Format:								  |
     | 	      CAL							  |
     |	      WAITE							  |
     |	      EFLAG							  |
     |									  |
     | where:								  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     WAITE     is an Executive Request mnemonic.		  |
     |	     EFLAG     is the location of the event flag.		  |
     |									  |
     ----------------------------------------------------------------------

     The WAITE Executive Request prevents a task  from  running  until  the
     Executive posts any event flag.

     The WAITE Executive Request checks the status of location  EFLAG  and, 
     if  it  is  FINISHED,  returns  control to the caller.  If the task is 
     runnable and EFLAG is FINISHED, control returns immediately.  If EFLAG 
     is  PENDING,  the  Executive changes its state to WAITING and puts the
     calling task into Event Flag Wait.  After another  task  or  interrupt
     routine posts location EFLAG, the calling task again becomes runnable.
     
     In most cases, you must initialize the event flag (that is, set it  to
     1)  before  using  it;   this  is  particularly  true  when  a task is 
     initiating an event to  be  completed  by  another  task.   Also,  the 
     waiting  task  must reset the event flag before using it again because 
     the event flag does not reset itself.
     
		  ------------------- NOTE -------------------
		  |					     |     
		  | In some applications, you may be waiting |
		  | for multiple event flags.  In this case, |
		  | the task runs whenever a task  posts  an |
		  | event flags, and not necessarily the one |
		  | specified in the WAITE.  To ensure that  |
		  | a  task  posts  a particular event flag, |
		  | use the WAITX Executive Request. 	     |
		  --------------------------------------------

     See Section 3.3 for an example of the WAITE command.








				     3-26

			   RTS/8 EXECUTIVE REQUESTS


     --------------					     --------------
     |		  |					     |		  |
     |   WAITX	  |					     |   WAITX	  |
     |		  --------------------------------------------		  |
     |									  |
     | Use the WAITX Executive Request to wait for a particular event  to |
     | be posted.
     |									  |
     | Format:								  |
     | 	      CAL							  |
     |	      WAITX							  |
     |	      EFLAG							  |
     |									  |
     | where:								  |
     |	     CAL       is an RTS/8 mnemonic for JMS 20.			  |
     |	     WAITX     is an Executive Request mnemonic.		  |
     |	     EFLAG     is the location of the event flag to be posted.	  |
     |									  |
     ----------------------------------------------------------------------

     The WAITX Executive Request causes a task to wait for a specific event
     posting, rather than any posting.
     
     The WAITX Executive Request, although similar in most respects to  the
     WAITE  Executive Request, differs from it in that if the event flag is
     not FINISHED, the  task  goes  into  EORMWT,  Event  or  Message  Wait 
     (instead  of  EFWT);  moreover, the task's program counter points back 
     to the location containing the CAL of this  Executive  Request.   (The 
     program  counter  of  a  task executing a WAITE points to the location 
     following EFLAG.) Thus, when  the  task  resumes  execution,  it  will 
     re-execute the WAITX.
     
     If you or the Executive clear the EORMWT bit  for  some  reason  other 
     than  the  posting of the event flag in question, the task immediately 
     goes back into EORMWT.  Consequently, control never  flows  past  this 
     Executive  Request  unless  a task actually posts that event flag.  If 
     you use a WAITE and if the task is waiting for multiple  event  flags, 
     then  the  task  conceivably  could start up after the WAITE Executive 
     Request.  This is because some  other  event  flag--one  that  you  no 
     longer  care  about--was  posted.   This situation cannot occur with a 
     WAITX.

     See Section 3.3 for an example of the WAITX Executive Request.













				     3-27

			   RTS/8 EXECUTIVE REQUESTS


     3.3  EXAMPLE OF EXECUTIVE REQUESTS FOR MESSAGE AND EVENT FLAGS

     The following example illustrates the RTS/8 Executive Requests dealing
     with  messages  and  event  flags.   A  description  of  the execution 
     sequence follows the example.

				     Task A

     A1	     ALOOP,  CAL     __
		     SEND	     /SEND TASK B MESSAGE 1
		     B
		     MES1
		     CAL
		     SEND	     /SEND TASK B MESSAGE 2
		     B
		     MES2
     A3      	     CAL     __
                     WAITX	     /WAIT ONLY FOR MESSAGE 1
                     MES1
     A4		     JMP ALOOP       /LOOP     __
             MES1,   ZBLOCK 3	     /MESSAGE 1
                     15		     /RANDOM NUMBERS
		     37
		     23
	     MES2,   ZBLOCK 3	     /MESSAGE 2
		     -1		     /RANDOM NUMBERS
		     4


				     Task B
     B1      BLOOP,  CAL     __
		     RECEIVE	     /GET A MESSAGE
	     MADDR,  0
     B2		     DCA EFCDF       /SAVE MESSAGE CDF FOR POST     __
		     TAD EFCDF
     B4		     DCA .+1	     /PUT CDF INLINE     __
     B5		     HLT	     /CDF TO MESSAGE FIELD     __
     B6		     TAD I MADDR     /GET 1ST DATA WORD OF MESSAGE     __
		     		     / (DO NOTHING WITH IT)
     B7		     CLA     __
     B8		     STA CLL RTL     /-3 IN AC     __
     B9		     TAD MADDR       /AC POINTS TO MESSAGE EVENT FLAG     __
     B10	     CAL     ___
		     POST	     /DECLARE MESSAGE RECEIVED
		     EFCDF, HLT      /CDF TO MESSAGE FIELD HERE
     Bll	     JMP BLOOP       /LOOP     ___










				     3-28

			   RTS/8 EXECUTIVE REQUESTS


     The flow of execution in this example depends  on  which  of  the  two 
     tasks  has  higher  priority.  Assuming that at some time both A and B 
     become runnable and that task A has higher priority, the  sequence  of 
     execution is as follows:

	 Sequence		   Reason for Execution	 ________		   ____________________

	    A1	    Task A has higher priority than Task B.	    __

	    A2	    Task A has higher priority than Task B.	    __

	    A3	    Task A has higher priority than Task B.	    __

	    B1	    Task A is  now  in  Event  Flag  Wait  since  MES1  was	    __
                    PENDING;  MES1 is now in waiting state.

	  B2-B10    Task A is still waiting;  the RECEIVE  at  B1  received	  ______
		    MES1.
		
	    A4	    The post at B10 posted MES1 and "woke up" A, which  has	    __
		    a higher priority than B.

	    A1      A continues executing.	    __

	    A2      A tries to send MES2 again;  B has  not  yet  processed	    __
		    it;  MES2 is pending.

	    Bll	    Therefore, A is put into  Event  Flag  Wait  and  B  is	    ___
		    resumed;  MES2 is not waiting.

	  Bl-B10    B now RECEIVes and posts MES2.	  ______

	    A2      This brings A  out  of  Event  Flag  Wait;   the  RTS/8	    __
		    Executive has modified task A's program counter so that
		    it will re-execute the offending SEND.

	    A3      A3 now waits for MES1 to be posted.	    __

     If Task B has higher priority, the sequence of execution is:

	    B1      Task B has higher priority than Task A.	    __

	    A1      Task B is placed in Message Wait  since  there  are  no	    __
		    messages in its input queue.  Task A then sends MES1 to
		    Task B.

	  B2-B10    Task A's message brings task B  out  of  Message  Wait;	  ______
		    since B has a higher priority, A is stopped and B runs.

	    Bll     The post at B10 sets MES1 to FINISHED but has no  other	    ___
		    effect.

	    B1      Now Task B tries to get another message.	    __



				     3-29

			   RTS/8 EXECUTIVE REQUESTS


	    A2      There are no other messages;  therefore, Task B is  put	    __
		    into Message Wait, and A is run.

	  B2-Bll    Task A sends MES2 which wakes up B;  B processes MES2,	  ______

	    B1      Returns for more,	    __

	    A3      And is put into Message Wait.  Since MES1 is FINISHED,	    __

	    A4      The WAITE at A3 has no effect and Task A	    __

	    A1      Loops back to A1 and sends MES1 again.	    __


     3.4  EXECUTIVE REQUEST WAIT STATES

     Table 3-3 is a summary of Executive Request Wait states.







































				     3-30

			   RTS/8 EXECUTIVE REQUESTS


				   Table 3-3
	     Summary of Wait States Incurred by Executive Requests

     ----------------------------------------------------------------------
     |     ER	   | Wait State |      Condition	|  PC Suspended	  |
     |		   |		|			|       at	  |
     |-------------|------------|-----------------------|-----------------|
     |		   |		|			|		  |
     | BLKARG  	   | any (given | If task = self       	|    "CAL"+3	  |
     |		   |  argument) |			|		  |
     |		   |		|			|		  |
     | DERAIL      | none    	|	_ 		|	_	  |
     |		   |		|			|		  |
     | POST	   | none	|	_		|	_	  |
     |		   |		|			|		  |
     | RECEIVE	   | MSGWT   	| If no messages 	|    "CAL"	  |
     | (No wait    |		| in input queue	|		  |
     | if AC=4000) |		| and AC positive	|		  |
     |		   |		|			|		  |
     | RESCHD	   | none	|	_		|	_	  |
     |		   |		|			|		  |
     | RUN	   | none	|	_		|	_	  |
     |		   |		|			|		  |
     | SEND	   | none	| EFWT for SEND if 	|    "CAL"	  |
     |		   |		| message busy at "CAL"	|		  |
     |		   |		|			|		  |
     | SENDW	   | EFWT	| If message free 	|    "CAL"+3	  |
     |		   |		| but event flag	|		  |
     |		   |		| not FINISHED		|		  |
     |		   |		|			|		  |
     |		   | EFWT	| If message busy 	|    "CAL"	  |
     |		   |		|			|		  |
     | SKPINS	   | none	|	_		|	_	  |
     |		   |		|			|		  |
     | SUSPND	   | RUNWT	| If task = self 	|    "CAL"+2	  |
     |		   |		|			|		  |
     | UNBARG	   | none	|	_		|	_	  |
     |		   |		|			|		  |
     | WAITE	   | EFWT	| If event flag 	|    "CAL"+3	  |
     | (No wait if |		|			|		  |
     | EF "done")  |		|			|		  |
     |		   |		|			|		  |
     | WAITX	   |  EORMWT	| If specified event	|    "CAL"	  |
     |		   |		| flag not FINISHED	|		  |
     |____________________________________________________________________|
     |									  |
     | NOTE: (a) "CAL" denotes the address of the CAL instruction in  the |
     |		 Executive Request.					  |
     |	     (b) A message is said to be busy if its event flag  has  not |
     |		 yet been posted by its previous user.			  |
     ----------------------------------------------------------------------





				     3-31






                                   CHAPTER 4

                              RTS/8 SYSTEM TASKS


     4.1  RTS/8 SYSTEM TASK SUMMARY

     The RTS/8 system includes  system  tasks  that  control  most  of  the
     standard  DIGITAL  PDP-8  I/O  devices.   Also included are tasks that
     provide interactive system control from the console terminal and  that
     allow  a  single  copy  of  the  OS/8  operating  system to run in the
     background of a foreground/background system.

     The system tasks in the RTS/8 system are as follows:

          1.  Cassette Handler--allows you to read data on a tape cassette.              ________________

          2.  Cassette File Support Handler--allows you to look up,  enter,              _____________________________
              and delete files from a DECcassette in CAPS-8 format.

          3.  Clock Handler--performs actions after a  specified  time  has              _____________
              elapsed.

          4.  Console and Non-console Terminal  Handlers--handle  a  single              __________________________________________
              terminal in either line or character mode.

          5.  Exit Task--permits special processing before making  an  exit              _________
              from RTS/8.

          6.  Floppy Disk Handler--provides support for the use  of  single              ___________________
              and double density floppy disks.

          7.  LINCtape  Handler--supports   both   OS/8   and   DIAL-format              _________________
              LINCtapes.

          8.  Line Printer Handler--supports LS8, LS8E, LP8,  or  LV8  line              ____________________
              printer.

          9.  Mass Storage Handlers--control  the  passing  of  information              _____________________
              from  these devices to and from memory for the RK8, RK8E, and
              RLO1 moving head disks, DF32 and RF08 fixed-head  disks,  and
              TC08  DECtape  units.   These handlers read and write data in
              the standard OS/8 block format.

         10.  OS/8 Files Support Task--allows you to look up,  create,  and              _______________________
              delete  files  in  OS/8  directories  from a foreground task.
              This task, when you use it with the  mass  storage  handlers,
              provides  the  capability to read or write OS/8 files on mass
              storage devices.  The OS/8 Support Task is not necessary  for
              using this task.





                                      4-1

                             RTS/8 SYSTEM TASKS


         11.  OS/8  Support  Task--supports  the  execution  of   an   OS/8              ___________________
              operating  system  in the background.  The OS/8 Files Support
              Task is not necessary for using this task.

         12.  PDP-8A Null Task--counts in decimal and displays this  number              ________________
              on the LED display accumulator of the PDP-8A.

         13.  Power Fail Task--provides for an  orderly  shutdown  when  AC              _______________
              power  is  lost  (if  you   have power fail hardware and core
              memory).   Also  allows  a  programmed  restart  when   power
              returns.

         14.  UDC/ICS Handler--allows you to control the various  types  of              _______________
              UDC/ICS modules.

     The remainder of this chapter describes tasks supplied by DIGITAL.


                  ------------------- NOTE -------------------
                  |                                          |
                  | The tasks actually in your RTS/8  system |
                  | are  dependent  upon  the  configuration |
                  | established   when   the   system    was |
                  | generated.                               |
                  --------------------------------------------































                                      4-2

                             RTS/8 SYSTEM TASKS


     4.2  CASSETTE HANDLER

     The  Cassette  Handler  (CSA)   allows   you   to   read   and   write
     variable-length records on DECcassettes, as well as to perform various
     special functions (such as rewind and write end-file marks).  One copy
     of the Cassette Handler can operate up to eight units.

     There are two general categories of cassette operation:

          1.  Handler functions--read and write.

          2.  Utility functions--rewind, backspace  file  gap,  write  file
              gap, backspace block gap, and skip to file gap.


     4.2.1  Handler Function

     ----------------------------------------------------------------------
     | Use the Cassette Handler to perform I/O on a tape cassette.        |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                CALL+UNIT                                           |
     |                RW+FIELD+NOSTORE                                    |
     |                BUFADD                                              |
     |                SIZE                                                |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       CALL      specifies whether you  are  making  a  handler  or |
     |                 utility call.                                      |
     |       UNIT      is the device unit of the cassette.                |
     |       RW        specifies whether you are  performing  a  read  or |
     |                 write operation.                                   |
     |       FIELD     is the field of the I/O  buffer  in  the  standard |
     |                 mass storage handler format (see Section 4.10).    |
     |       NOSTORE   specifies whether information will be stored.      |
     |       BUFADD    is the address of the I/O buffer in field FIELD.   |
     |       SIZE      is the record size.                                |
     |       STATUS    is a location where the Handler places I/O  status |
     |                 messages.                                          |
     ----------------------------------------------------------------------

     You use the Cassette Handler to perform read and write operations on a
     cassette.

     Cassette conventions specify a record size of 200 (octal)  bytes,  but
     you  can  use  any  size  up  to  377  (octal);   that is, the Handler
     transfers 8 bits.  This record buffer cannot cross  field  boundaries.
     For  a  read  operation,  the  buffer  is  optional (although you must
     include its word in the message), according to bit 11 of Word 5.

     You can use the NOSTORE capability for advancing through a long file.



                                      4-3

                             RTS/8 SYSTEM TASKS


     Word 8 contains the contents of status register B, which is defined by
     the bit setting as follows:

                                   Table 4-1
                     Cassette Handler Status Register Bits

                        -----------------------------
                        |  Bit  |        Meaning    |
                        |-------|-------------------|
                        |   4   |  CRC/block error  |
                        |   5   |  Timing           |
                        |   6   |  EOT/BOT          |
                        |   7   |  EOF              |
                        |   8   |  Drive empty      |
                        |   9   |  Read/write       |
                        |  10   |  Write lockout    |
                        |  11   |  Ready            |
                        -----------------------------

     The following listing describes the words and meaningful bit positions
     of the Message Format.

          Word 4 bit  0 = 0        Utility Call
                 bit  0 = 1        Handler Call
                 bits 9-11         Cassette Unit

          Word 5 bit  0 = 0        Read
                      0 = 1        Write
                 bits 6-8          Field of Buffer
                 bit 11            Do not store data
                                   (applicable to read only)

          Word 6                   Buffer Address
          Word 7                   Record size in bits 4-11
          Word 8                   Status Return

                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^       ^                          \___________/
     0:  Handler call \___|       |                                |
     1:  Utility call /           |                                |
                                  |                                |
     RL01 Mode ___________________|                                |
                                                                   |
     Unit _________________________________________________________|

                 Figure 4-1 Cassette Handler Unit Word Format








                                      4-4

                             RTS/8 SYSTEM TASKS


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^                      \__________________/   ^
     0:  Read  \__________|                               |             |
     1:  Write /                                          |             |
                                                          |             |
     Field _______________________________________________|             |
                                                                        |
     0:  Read into memory \_____________________________________________|
     1:  Check data       /

             Figure 4-2 Cassette Handler Call Function Word Format

                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                                          ^   ^   ^   ^   ^   ^    ^    ^
     CRC/block error _____________________|   |   |   |   |   |    |    |
                                              |   |   |   |   |    |    |
     Timing __________________________________|   |   |   |   |    |    |
                                                  |   |   |   |    |    |
     EOT/BOT _____________________________________|   |   |   |    |    |
                                                      |   |   |    |    |
     EOF _____________________________________________|   |   |    |    |
                                                          |   |    |    |
     Drive empty _________________________________________|   |    |    |
                                                              |    |    |
     Read/write ______________________________________________|    |    |
                                                                   |    |
     Write lookout ________________________________________________|    |
                                                                        |
     Ready _____________________________________________________________|

             Figure 4-3 Cassette Handler Status Return Word Format

     At the end of each cassette operation, you should examine  Word  8  to
     check for any errors that might occur during an I/O operation.

     Examples:

     A Cassette Handler message to write 100 bytes from a  buffer  starting
     at 21200 to cassette unit 3 is as follows:

                     UNIT3=3                 /INITIALIZE VARIABLES TO BE
                     HANDLR=4000             /   USED IN MESSAGE
                     WRITE=4000
                     SIZE=100
                     .
          MSG1,      ZBLOCK 3
                     HANDLR+UNIT3            /HANDLER OPERATION ON UNIT 3
                     <XEDF BUFFER>+WRITE     /WRITE FROM FIELD OF "BUFFER"
                     BUFFER
                     SIZE                    /100 BYTES LONG
          MSGER1,    0000                    /STATUS RETURN

                                      4-5

                             RTS/8 SYSTEM TASKS


     To read and not store 200 bytes from unit 2, the message is:

                     READ=0                  /INITIALIZE VARIABLES USED
                     NOSTOR=1                /   USED IN MESSAGE
                     HANDLR=4000
                     UNIT2=2
                     SIZE=200
                     .
                     .
                     .
          MSG2,      ZBLOCK 3
                     HANDLR+UNIT2            /HANDLER OPERATION ON UNIT 2
                     NOSTOR+READ             /READ AND DON'T STORE
                     0000                    /UNUSED
                     SIZE                    /200 BYTES
          MSGER2,    0000                    /STATUS RETURN


     4.2.2  Utility Function Handler

     ----------------------------------------------------------------------
     | Use the Utility Handler to perform  auxiliary  operations  upon  a |
     | CAPS-8 formatted cassette.                                         |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                CALL+UNIT                                           |
     |                FUNCTN                                              |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       CALL      specifies if the operation is a utility or handler |
     |                 call.                                              |
     |       UNIT      is the  logical  device  upon  which  the  message |
     |                 performs the action.                               |
     |       FUNCTN    is the operation which the Handler performs.       |
     |       STATUS    is a word indicating the status of the operation.  |
     ----------------------------------------------------------------------

     You  use  the  Utility  Function  Handler  to  perform  the  following
     operations:

          1.  Rewind--place the cassette at its first record.

          2.  Backspace File Gap--place the read/write  head  at  the  last
              file gap marking.

          3.  Write  File  Gap--write  a  file  gap  at  the  current  tape
              position.

          4.  Backspace  Block  Gap--place  the  read/write  head  at   the
              previous record.

          5.  Skip--place the read/write head  at  the  next  file  on  the
              cassette.

                                      4-6

                             RTS/8 SYSTEM TASKS


     If the Handler encounters an error, it normally retries the  operation
     three  times.   The exceptions occur when a write lock out occurs on a
     write operation or when  an  error  appears  while  reading  a  cyclic
     redundancy check.

     The CAPS-8 User's Manual (DEC-8E-OCASA-A-D) is  suggested  reading  if
     you are unsure of cassette conventions.

     For a utility function, the words after the RTS/8 message  header  are
     as follows:

          Word 4 bit  0 = 0        Utility Call
                 bit  0 = 1        Handler Call
                 bits 9-11         Cassette Unit

          Word 5 (function in bits 6-8):
                      10           Rewind
                      30           Backspace File Gap
                      40           Write File Gap
                      50           Backspace Block Gap
                      70           Skip to File Gap

          Word 6 (see Figure 4-4)

                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                                                  \________/
     Function: _______________________________________|
     1 Rewind
     3 Backspace file gap
     4 Write file gap
     5 Backspace block gap
     7 Skip to file gap

                   Figure 4-4 Cassette Handler Utility Call


     For example, to request a rewind on unit 1, the message is:

                     UTILTY=0        /SET UP VARIABLES FOR USE IN
                     UNITl=1         /   MESSAGE FORMAT
                     REWIND=10
                     .
                     .
                     .
          MSG3,      ZBLOCK 3
                     UTILTY+UNIT1    /UTILITY OPERATION ON UNIT 1
                     REWIND          /REWIND
          MSGER3,    0000            /STATUS RETURN






                                      4-7

                             RTS/8 SYSTEM TASKS


     4.3  CASSETTE FILE SUPPORT HANDLER

     ----------------------------------------------------------------------
     | Use the Cassette File Support  Handler  to  look  up,  enter,  and |
     | delete files from a DECcassette in CAPS-8 format.                  |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                COMMND+UNIT                                         |
     |                ADRHED                                              |
     |                ADRFLD                                              |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       COMMND    can be ENTER, LOOKUP, or CLOSE.                    |
     |       UNIT      is the device number.                              |
     |       ADRHED    is the address of the header for ENTER and LOOKUP, |
     |                 or the status return for a CLOSE operation.        |
     |       ADRFLD    is the field of the header.                        |
     |       STATUS    is the status return location for ENTER and LOOKUP |
     |                 operations.                                        |
     ----------------------------------------------------------------------

     The Cassette File Support  Handler  (CSAF)  supports  the  DECcassette
     CAPS-8  format.   Thus,  it allows a calling task to look up and enter
     files on cassettes in that format.  This Handler requires the Cassette
     Handler Task (CSA) to perform the I/O operations.

     The Cassette File Support  Handler  performs  the  following  cassette
     operations:

          o  ENTER--enters a file name into the cassette directory.

          o  LOOKUP--finds a file name in the cassette directory.

          o  CLOSE--closes the currently open file, enters its directory
                    information, and then rewinds the cassette.

     ENTER and LOOKUP require you to put appropriate information  into  the
     record  header  area  which  CSAF uses to perform the file operations.
     The header area is at least 40 (octal) words  long  and  cannot  cross
     field boundaries.

     For ENTER and LOOKUP, the format of the header area must conform  with
     cassette  standards  (and therefore be compatible with CAPS-8).  These
     formats are listed in Table 4-2.










                                      4-8

                             RTS/8 SYSTEM TASKS


                                   Table 4-2
                            Cassette Header Formats

             ----------------------------------------------------
             | Byte (octal)  |                Use               |
             |---------------|----------------------------------|
             | 0-5           |  Filename                        |
             |               |                                  |
             | 6-10          |  Filename extension              |
             |               |                                  |
             | 11            |  File Type                       |
             |               |     1 = ASCII                    |
             |               |     0 = undefined                |
             |               |                                  |
             | 12-13         |  File Record Length              |
             |               |  (currently word 12 must equal 0)|
             |               |                                  |
             | 14-15         |  Unused                          |
             |               |                                  |
             | 16-23         |  Date (ASCII) specified as       |
             |               |  ddmmyy                          |
             |               |                                  |
             | 24-37         |  Unused                          |
             |--------------------------------------------------|
             | Reference is to 8-bit bytes, one per word, right |
             | justified.                                       |
             ----------------------------------------------------

     For an ENTER operation, if the Handler finds a file with the name  you
     specify in the header area on the unit, it deletes the file.

     For a LOOKUP operation, the Handler returns the  record  size  of  the
     file  in  location HEADER+13 (byte 13).  If it cannot find the file or
     if an error occurs, this location contains a 0.

     A REWIND operation automatically follows a CLOSE operation.

     Word definitions for a CSAF message are as follows:

          Word 4  bit  0 = 1       ENTER
                  bit  1 = 1       LOOKUP
                  bit  2 = 1       CLOSE
                  bits 9-11        UNIT

          Word 5                   Address of header for ENTER and  LOOKUP;
                                   status return for CLOSE
          Word 6                   Field of header  for  ENTER  and  LOOKUP
                                   (bits 6-8)
          Word 7                   Status return for ENTER and LOOKUP

     In all cases, the status return is the contents of status register  B.
     For further information, see the CAPS-8 User's Manual.                                      ____________________




                                      4-9

                             RTS/8 SYSTEM TASKS


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                         \_________/                         \___________/
                              |                                    |
           Function: _________|                                    |
           1 Close                                                 |
           2 Lookup                                                |
           4 Enter                                                 |
                                                                   |
           Unit ___________________________________________________|

          Figure 4-5  Cassette File Support Handler Unit Word Format


     Examples:

          MSG4,      ZBLOCK 3
                     4000           /ENTER ON UNIT 0
                     6400           /INFORMATION IN HEADER
                                    /   STARTING AT 6400
                     0010           /   OF FIELD 1
                     0000           /STATUS RETURN

          MSG5,      ZBLOCK 3
                     1003           /CLOSE ON UNIT 3
                     0000           /STATUS RETURN





























                                     4-10

                             RTS/8 SYSTEM TASKS


     4.4  CLOCK HANDLER

     ----------------------------------------------------------------------
     | Messages sent to the clock handler direct it  to  perform  actions |
     | after time intervals which you also specify in the message.        |
     |                                                                    |
     | Message Format:                                                    |
     |                CLKMSG, ZBLOCK 3                                    |
     |                        COMMND+CLASS+TSKNUM                         |
     |                        TIMEHI                                      |
     |                        TIMELO                                      |
     |                        EXTRA1                                      |
     |                        EXTRA 2                                     |
     |                                                                    |
     | where:                                                             |
     |       CLKMSG    is a label identifying  the  start  of  the  clock |
     |                 message  (the  Executive uses this location for an |
     |                 event flag).                                       |
     |       COMMND    is one of the commands listed in Table 4-1.        |
     |       CLASS     is an  optional  specification  which  allows  the |
     |                 clock CANCEL command to remove groups of requests; |
     |                 you may  add  a  CLASS  designator  to  all  clock |
     |                 requests  other  than  a  CANCEL  request to label |
     |                 those requests for possible future cancelation.    |
     |       TSKNUM    is  the  task  to  receive  message  beginning  at |
     |                 CLKMSG,  TSKNUM=0  means that the task sending the |
     |                 message is also the receiving task.                |
     |       TIMEHI/LO specify a time interval from the present  time  in |
     |                 terms  of "system ticks" (TIMEHI is the high-order |
     |                 word and TIMELO is the low-order word of a double- |
     |                 precision number).                                 |
     |       EXTRA1    and EXTRA2 are words used by some of the  commands |
     |                 listed in Table 4-1.                               |
     ----------------------------------------------------------------------

     The Clock Handler accepts RTS/8 messages and inserts the entries  into
     an  internal  clock  queue.   As  the  entries become due, the Handler
     removes them from the queue;  the Handler then  decodes  and  executes
     the request.


                 ------------------- NOTE -------------------
                 |                                          |
                 | You should be careful that  you  do  not |
                 | exceed   the   queue   length  that  was |
                 | specified  when  the  RTS/8  system  was |
                 | generated.  If the handler receives more |
                 | messages than its queues can store,  the |
                 | system   behaves   unpredictably.    The |
                 | default and minimum queue length  is  16 |
                 | (decimal) entries.                       |
                 --------------------------------------------

     In the following discussion of the Clock Handler,  "system  ticks"  is
     defined  as  the number of hardware ticks that occur in one second and

                                     4-11

                             RTS/8 SYSTEM TASKS


     is machine dependent.  This system ticks value  is  called  HERTZ.   A
     second  value,  called  SHERTZ, is the number of system ticks that the
     Clock Handler will receive before it generates a software interrupt.

     The maximum interval that you  can  enter  in  TIMEHI  and  TIMELO  is
     (2**24)/SHERTZ.   If SHERTZ is 60, then this interval is approximately
     three days.

     The Clock Handler maintains the current TIME-OF-DAY (in  system  ticks
     until  midnight) in symbolic locations TODH (high-order) and TODL (low
     order) in page 0 of field 0.  When TIME-OF-DAY reaches zero (i.e.,  at
     midnight),  it  resets the location to -(SHERTZ*86400) (24 hours until
     midnight).  The Handler then increments by  one  day  the  OS/8-format
     date  word  in  symbolic location DATE in page 0 of field 0.  If HERTZ
     and SHERTZ are different, the Handler places a  value  (computed  when
     the system was generated) into location TODX.  This value is the two's
     complement of the number of hardware ticks HERTZ remaining  until  the
     Clock Handler generates a software interrupt.

     Note  that  SHERTZ  must  be  less   than   192   for   the   quantity
     -(SHERTZ*86400) to be contained in 24 bits.

     COMMND, in the above Message Format statement, is the type of  request
     and has the meanings listed in Table 4-3.


                                   Table 4-3
                            Clock Handler Commands

     ----------------------------------------------------------------------
     | Octal  |      Symbolic       |            Description              |
     |--------|---------------------|-------------------------------------|
     | 0000   |   MARKTIme          |  Post the event flag  CLKMSG  after |
     |        |                     |  the  specified  interval  elapses. |
     |        |                     |  The   Handler   ignores    TSKNUM, |
     |        |                     |  EXTRA1, and EXTRA2.                |
     |        |                     |                                     |
     | 1000   |   SCHEDUle          |  Post   the   event   flag   CLKMSG |
     |        |                     |  immediately.     Execute   a   RUN |
     |        |                     |  Executive Request on  task  TSKNUM |
     |        |                     |  after   the   specified   interval |
     |        |                     |  elapses.   The   Handler   ignores |
     |        |                     |  EXTRA1 and EXTRA2.                 |
     |        |                     |                                     |
     | 2000   |   TIMOUT            |  Post CLKMSG  immediately.   DERAIL |
     |        |                     |  task   TSKNUM  into  a  subroutine |
     |        |                     |  whose address is in  EXTRA1  after |
     |        |                     |  the  specified  interval  elapses. |
     |        |                     |  The Handler ignores EXTRA2.        |
     ----------------------------------------------------------------------
                                                 (continued on next page)





                                     4-12

                             RTS/8 SYSTEM TASKS


                               Table 4-3 (Cont.)
                            Clock Handler Commands

     ----------------------------------------------------------------------
     | Octal  |      Symbolic       |            Description              |
     |--------|---------------------|-------------------------------------|
     | 3000   |   PERIODically      |  Post CLKMSG immediately.   Execute |
     |        |                     |  a  RUN  Executive  Request on task |
     |        |                     |  TSKNUM   after    the    specified |
     |        |                     |  interval   elapses,   and  requeue |
     |        |                     |  this  command  with   the   values |
     |        |                     |  EXTRA1/EXTRA2    in    place    of |
     |        |                     |  TIMEHI/TIMELO.    This   has   the |
     |        |                     |  effect   of   running   the   task |
     |        |                     |  periodically with the  new  period |
     |        |                     |  EXTRA1/EXTRA2.                     |
     |        |                     |                                     |
     | 4000   |   REMOTE MARKTIme   |  Post   the   event   flag   CLKMSG |
     |        |                     |  immediately.   After the specified |
     |        |                     |  interval  elapses,  post   another |
     |        |                     |  event  flag.   You  place a CDF to |
     |        |                     |  the flag's  field  in  EXTRA1  and |
     |        |                     |  its address in EXTRA2.             |
     |        |                     |                                     |
     | 7000   |   CANCEL            |  Cancel  clock  requests  for  task |
     |        |                     |  TSKNUM     and     post     CLKMSG |
     |        |                     |  immediately.  The Handler  ignores |
     |        |                     |  TIMEHI,    TIMELO,   EXTRA1,   and |
     |        |                     |  EXTRA2.  If CLASS  is  zero,  this |
     |        |                     |  command  cancels all requests.  If |
     |        |                     |  CLASS is a nonzero number  between |
     |        |                     |  1  and 3, the Handler cancels only |
     |        |                     |  those  requests  with   the   same |
     |        |                     |  CLASS   number.   Note  that  only |
     |        |                     |  another  clock  request  can   set |
     |        |                     |  these  bits.   (You  set  them  by |
     |        |                     |  indicating  a  CLASS  bit  in  any |
     |        |                     |  clock message except a CANCEL.)    |
     ----------------------------------------------------------------------

     In all clock message formats, you  must  include  all  indicated  word
     positions,  even  if  the  command  ignores  the word.  For example, a
     MARKTIME request might be:

          CLKMSG, ZBLOCK 3
                  MARKTIME
                  0
                  170
                  ZBLOCK 2

     Figure 4-6 illustrates bit positions in the Clock Handler Command Word
     Format.




                                     4-13

                             RTS/8 SYSTEM TASKS


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                         \_________/ \_____/ \___________________________/
                              |         |                 |
        Command: _____________|         |                 |
        0 MARKTIME                      |                 |
        1 SCHEDULE                      |                 |
        2 TIMOUT                        |                 |
        3 SCHEDULE PERIODICALLY         |                 |
        4 REMOTE MARKTIME               |                 |
        7 CANCEL                        |                 |
                                        |                 |
        Class Number ___________________|                 |
                                                          |
        Task Number ______________________________________|

                 Figure 4-6 Clock Handler Command Word Format


     In some cases, you may require an immediate response to a  clock  tick
     (if  this  feature  exists  in  your RTS/8 system).  The clock handler
     allows you to supply a subroutine to perform this response.  Note that
     the  Clock  Handler  calls  this  routine  at  the interrupt level and
     interrupts remain disabled.   Also,  the  subroutine  returns  to  the
     normal clock interrupt processing with a

          CDF CIF RTS8    /RETURN TO EXECUTING FIELD
          JMP I SUBN      /   OF CALLER

     To enable the linkage of the subroutine, first  place  the  subroutine
     address  in  the  global  ALARML  then place a CIF to the field of the
     subroutine in ALARMH.  Note that the order of placement  is  critical.
     (Setting  them  in  the  reverse  order  causes  unpredictable  system
     actions.) To disable this function, simply zero ALARMH.

     Should the  immediate  response  subroutine  wish  to  post  an  event
     variable,  it  may  do  so  with the POSTDS interrupt release.  If the
     routine issues a POSTDS, the Executive does not clear the clock  flag;
     consequently,  the  interrupt  occurs  again.   The immediate response
     subroutine should remember that it posted the event, so that it avoids
     an infinite loop.














                                     4-14

                             RTS/8 SYSTEM TASKS

                 ------------------ NOTES -------------------
                 |                                          |
                 | 1.  You use this  routine  at  your  own |
                 |     risk.                                |
                 |                                          |
                 | 2.  You must not perform  any  Executive |
                 |     Requests  as  you  are  at interrupt |
                 |     level.                               |
                 |                                          |
                 | 3.  Immediate    Response     Subroutine |
                 |     processing  time should be kept to a |
                 |     minimum  (approximately  50   micro- |
                 |     seconds) as its time is added to the |
                 |     regular clock  interrupt  processing |
                 |     time.                                |
                 --------------------------------------------

     Examples:

                    CAL            /WITH A 60HZ SYSTEM TICK RATE
                    SENDW          /   THIS CAUSES THE CURRENT TASK
                    CLOCK          /   TO "GO TO SLEEP" FOR 2 SEC.
                    SLEEPM
                    .
                    .
                    .
          SLEEPM,   ZBLOCK 3        /MESSAGE HEADER
                    0               /SET EVENT FLAG AFTER INTERVAL
                    0; 170          /INTERVAL IS 120 (DECIMAL)
                                    /   SYSTEM TICKS

     If you change the value 170 in the  above  example  to  the  assembler
     expression  2^SHERTZ,  the  preceding  sequence becomes configuration-
     independent.

                    CAL             /RUN THE TASK REPORT ONCE
                    SEND            /   EVERY HOUR, INDEFINITELY,
                    CLOCK           /   ASSUMING A 60HZ SYSTEM
                    RUNMSG          /   TICK RATE
                    .
                    .
                    .
          RUNMSG,   ZBLOCK 3        /MESSAGE HEADER

                    PERIODICALLY SCHEDULE
                                    /RUN REPORT AFTER SPECIFIED
                                    /   INTERVAL AND PERIODICALLY
                                    /   THEREAFTER
                    0; 1            /FIRST RUN IS ALMOST IMMEDIATELY
                                    /   (1/60 SECOND)
                    64; 5654        /PERIOD BETWEEN RUNS IS 216000
                                    /   (DECIMAL) SYSTEM TICKS =
                                    /   3600 SECONDS = 1 HOUR




                                     4-15

                             RTS/8 SYSTEM TASKS


     4.5  CONSOLE AND NONCONSOLE TERMINAL HANDLERS

     ----------------------------------------------------------------------
     | Use the Console and non-Console Terminal Handlers to make  use  of |
     | terminals.                                                         |
     |                                                                    |
     | Message Format 1:                                                  |
     |                  ZBLOCK 3                                          |
     |                  COMMND+LENGTH                                     |
     |                  INBUF                                             |
     |                  OUTTXT                                            |
     |                                                                    |
     | Message Format 2:                                                  |
     |                  ZBLOCK 3                                          |
     |                  ASSGN+TSKNUM                                      |
     |                                                                    |
     | Message Format 3:                                                  |
     |                  ZBLOCK 3                                          |
     |                  -2                                                |
     |                  CDF OUTBUF                                        |
     |                  COMMND+LENGTH                                     |
     |                  INBUF                                             |
     |                  OUTTXT                                            |
     |                                                                    |
     |where:                                                              |
     |      COMMND     is one of the commands listed in Table 4-4.        |
     |      LENGTH     specifies the maximum size of the input buffer  or |
     |                 the number of characters to input.                 |
     |      INBUF      is a pointer to the input buffer or is a  zero  if |
     |                 no  input  (the  input  buffer must be in the same |
     |                 field as the output buffer).                       |
     |      OUTTXT     is the first word of the output text or a  pointer |
     |                 to it.                                             |
     |      ASSGN      is an RTS/8 mnemonic having a value  of  200  that |
     |                 causes  the  Handler  to be assigned to a specific |
     |                 task (or deassigned if TSKNUM=0).                  |
     |      OUTBUF     is the field of the output buffer.                 |
     ----------------------------------------------------------------------

     The RTS/8 Terminal Handler operates upon a terminal in either line  or
     character  mode.   You  specify  line  mode  if  you wish the Terminal
     Handler to input or output one line of text at a time.  You  terminate
     input in line mode with a carriage return or an ESCAPE character.  You
     may also edit the line using the DELETE (or RUBOUT) and CONTROL/U (^U)
     characters.   (DELETE  deletes the last valid character you type and U
     deletes the  entire  line.)  Character  deletion  and  other  terminal
     characteristics are determined when the system was generated.

     The character mode specifies how many characters the Terminal  Handler
     processes.   The Handler does not echo character mode input;  instead,
     it terminates this mode when the character count becomes greater  than
     the number of characters that you specify.

     You use FORMAT 1 when you write text and optionally read text.


                                     4-16

                             RTS/8 SYSTEM TASKS


     You use FORMAT 2 when you assign the Terminal Handler  to  a  specific
     task.   To  deassign  the  terminal,  the task possessing the terminal
     sends a separate message specifying that TSKNUM equals zero.

     You use FORMAT 3 when the output buffer is in a different  field  from
     that of the message.

     At the time the system is generated, a Terminal Handler is made either
     console  (i.e.,  it  talks  to  the MCR) or nonconsole.  (Note that an
     RTS/8 system can have only one Console Terminal Handler.) The  Console
     Terminal  Handler  invokes the MCR whenever you type a CONTROL/C (^C);
     nonconsole terminals treat ^C the same as any  other  character.   For
     the  Console  Handler,  ^C wakes up the MCR by posting the MCR's event
     flag.

     When an RTS/8 system is generated, a Terminal Handler can be  made  to
     have  a read timeout (if the system has a Clock Handler).  If there is
     no read timeout, the terminal can wait indefinitely  (except  for  EMT
     messages,  see  Section  4.5.1)  for a read operation to complete.  If
     read timeout is specified, the Terminal Handler may abort the  request
     which  is  "hanging"  the  terminal.   First, the Handler checks if it
     received any characters.  If the task  is  receiving  characters,  the
     Handler  continues the read operation;  if not, the Handler checks its
     request queue.  If there are no additional requests for  the  Handler,
     the  "hung"  operation  retains  control.  Otherwise, RTS/8 aborts the
     read operation and the Handler gives control to another  task  in  the
     system.   However, if a task owns a terminal because of an ASSGN, only
     a request that it issues can cause a timeout.  If, in this  case,  the
     task times out, the Handler does not post the aborted request.


                  ------------------- NOTE -------------------
                  |                                          |
                  | If the Handler aborts the input request, |
                  | it  will  print  a ^U.  It also places a |
                  | 4000 after the last  character  success- |
                  | fully input into the input buffer.       |
                  --------------------------------------------

     Legal commands, which you may combine, are listed in Table 4-4.
















                                     4-17

                             RTS/8 SYSTEM TASKS


                                   Table 4-4
                           Terminal Handler Commands

     ----------------------------------------------------------------------
     | Octal  |Symbolic |       Action if       |     Action if not       |
     | Command| Command |       Specified       |     Specified           |
     |--------|---------|-----------------------|-------------------------|
     | 4000   | NOPACK  | Output text is in     | Output text is in       |
     |        |         | unpacked ASCII, one   | packed 6-bit, two       |
     |        |         | character per word,   | characters per word     |
     |        |         | terminated by a 0000. | terminated by a 00.     |
     |        |         |                       |                         |
     | 2000   | NOCRLF  | Do not type a CR/LF   | Type a CR/LF after      |
     |        |         | after the message.    | typing the message.     |
     |        |         |                       |                         |
     | 1000   | IND     | OUTTXT points to the  | OUTTXT is the first     |
     |        |         | first word of the     | word of the output      |
     |        |         | output text.          | text.                   |
     |        |         |                       |                         |
     | 0400   | NOLINE  | Input is in character | Input is in line mode;  |
     |        |         | mode;  terminated     | terminated by a CR or   |
     |        |         | after LENGTH input    | ESCAPE.  The length is  |
     |        |         | characters read.      | still tested.           |
     ----------------------------------------------------------------------

     The following is a discussion of other aspects of the Terminal Handler
     format.

          LENGTH         is a 7-bit field which specifies the maximum  size
                         of the input buffer (if input is in line mode), or
                         the number of characters to input (if input is  in
                         character mode).  If the input is in line mode and
                         there are LENGTH-1 characters in the input buffer,
                         every character that you enter overwrites the last
                         character in the buffer.  The  Handler  posts  the
                         message  event  flag only when you type a carriage
                         return or an ESCAPE.

          INBUF          is a pointer to the input buffer.  If this word is
                         zero,  the  Handler  does not read data.  If it is
                         non-zero, the Handler fills the input buffer  with
                         characters  that  it  packs  one per word and also
                         forces the parity bit (bit 4) on.  If input is  in
                         line  mode,  the  last  character  of  the line is
                         followed by a zero  word  (if  a  carriage  return
                         terminates  the  line)  or a -1 (7777) word (if an
                         ESCAPE  character  terminates  the  line).   If  a
                         timeout   occurs  or  the  EMT  aborts  the  input
                         message, the Handler places a 4000 after the  last
                         word successfully input.

          ASSGN = 200    assigns  the  Terminal  Handler  to  task  TSKNUM,
                         causing  the  Terminal  Handler to accept messages
                         only from the task that you specify.   If  another
                         task  tries  to  SEND  a  message  to the Terminal

                                     4-18

                             RTS/8 SYSTEM TASKS


                         Handler while it is assigned, the  Handler  places
                         the  message  in  the  Terminal  Handler's Message
                         Input  Queue;   RTS/8  does  not  remove  it   for
                         processing  by  the  Terminal  Handler  until task
                         TSKNUM releases it.  The task to which you  assign
                         the Terminal Handler can release the assignment by
                         sending a message assigning the  Terminal  Handler
                         to  task  number  0.  This assignment message does
                         not perform any I/O.

          TSKNUM         is a 7-bit field used with the  ASSGN  command  to
                         specify  the  task number of the task to which you
                         are assigning the  terminal.   If  this  field  is
                         zero,  the  Handler  deassigns  the  terminal. The
                         zero assignment allows the terminal task to accept
                         commands from any task.

          OUTBUF         is the field of the output  buffer.   You  specify
                         this  value (in Message Format 3) if the buffer is
                         in a field different  from  that  of  the  message
                         call.

     RTS/8 permits you to use a single terminal for both the foreground and
     background  (see  Chapter  2  of  the RTS/8 System Generation Manual).                                           ______________________________
     When  you  start-up  the  system,  the  terminal  "belongs"   to   the
     foreground.    Typing   a  CONTROL/B  (^B)  switches  control  to  the
     background.  Conversely, typing a CONTROL/F (^F) while the  background
     "owns" the terminal switches it to the foreground.

     The change to the  background  occurs  only  at  a  message  boundary.
     Consequently,  you must terminate any input characters with a carriage
     return or ESCAPE  to  allow  the  ^B  to  take  effect.   However,  ^F
     transfers control immediately to the foreground.

     If you type a ^F while  in  the  foreground  or  a  ^B  while  in  the
     background, the Handler treats the commands as no-ops.

     The following two figures illustrate bit  positions  in  the  Terminal
     Handler.

















                                     4-19

                             RTS/8 SYSTEM TASKS


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^   ^   ^   ^   ^  \___________________________/
                          |   |   |   |   |___            |
     Command (bits 0-4)   |   |   |   |_____ |            |     __________________
     0:  Packed ASCII   \_|   |   |_______ | |            |
     1:  Unpacked ASCII /     |_________ | | |            |
                                       | | | |            |
     0:  CR/LF at end of message    \__| | | |            |
     1:  No CR/LF at end of message /    | | |            |
                                         | | |            |
     0:  OUTTXT is the first word    \___| | |            |
     1:  OUTTXT points to first word /     | |            |
                                           | |            |
     0:  Input in line mode      \_________| |            |
     1:  Input in character mode /           |            |
                                             |            |
     Bit 4 must be a 0 ______________________|            |
                                                          |
     Length (bits 5-11)                                   |     __________________
     If bit 3=1, no. of characters to input   \___________|
     If bit 3=0, maximum size of input buffer /

     Figure 4-7 Terminal Handler I/O Mode Command and Length Word Format


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                         \_____________/  |  \___________________________/
                                |         |               |
            Unused _____________|         |               |
                                          |               |
            Bit 4 must be a 1 ____________|               |
                                                          |
            Task Number __________________________________|

          Figure 4-8 Terminal Handler ASSGN Mode Command Word Format

     Examples:

          HIYA,     ZBLOCK 3        /MESSAGE HEADER
                    0               /PACKED TEXT, END WITH CR/LF
                    0               /NO INPUT
                    TEXT "HELLO"    /TEXT TO BE OUTPUT

     Sending the above message to the Terminal Handler prints HELLO on  the
     terminal.

           QUEST,    ZBLOCK 3       /MESSAGE HEADER
                     NOCRLF+60      /PACKED TEXT, NO CR/LF
                                    /   48-CHARACTER INPUT LIMIT
                     ANSWER         /POINTER TO INPUT BUFFER
                     TEXT "TYPE THE ANSWER"

                                     4-20

                             RTS/8 SYSTEM TASKS


     Sending the above message to the Terminal Handler prints

     TYPE THE ANSWER:

     on the terminal  and  inputs  a  reply  without  first  returning  the
     carriage.   You could print the answer to this message on the terminal
     by sending the following message:

          TYPANS,    ZBLOCK 3       /MESSAGE HEADER
                     NOPACK+IND     /UNPACKED TEXT, INDIRECT, WITH CR/LF
                     0              /NO INPUT
                     ANSWER         /POINTER TO OUTPUT TEXT


     4.5.1  EMT Task

     ----------------------------------------------------------------------
     | Use the EMT (Emergency Message Task) to  send  emergency  messages |
     | which originate from a task not in control of the terminal.        |
     |                                                                    |
     | Message Format 1:                                                  |
     |                  ZBLOCK 3                                          |
     |                  COMMND+LENGTH                                     |
     |                  INBUF                                             |
     |                  OUTTXT                                            |
     |                                                                    |
     | Message Format 2:                                                  |
     |                  ZBLOCK 3                                          |
     |                  -2                                                |
     |                  CDF OUTBUF                                        |
     |                  COMMND+LENGTH                                     |
     |                  INBUF                                             |
     |                  OUTTXT                                            |
     ----------------------------------------------------------------------

     If, while one task is using the terminal, another task wishes to  send
     an  emergency  message to the terminal, the sending task can interrupt
     the task presently in control of the terminal by sending  the  message
     to  the  EMT.   An emergency message overrides input waits, background
     ownership, terminal assignments, and CONTROL/S commands.

     The EMT sends messages to one and  only  one  terminal  in  any  RTS/8
     system.   If  the system has more than one terminal, the EMT sends the
     message to the terminal specified when the system was generated.

     The emergency message has the same  format  as  an  ordinary  terminal
     message.   However,  a  task sends the message to EMT rather than TTY.
     After a  task sends  the  message,  the  EMT  seizes  control  of  the
     terminal.  After  it  prints  the  message,  it  restores the Terminal
     Handler to its original state.






                                     4-21

                             RTS/8 SYSTEM TASKS


                  ------------------ NOTE --------------------
                  |                                          |
                  | If the terminal was waiting  for  input, |
                  | the  EMT  aborts the input request.  EMT |
                  | signals that it aborted input by placing |
                  | a word containing 4000 at the end of any |
                  | input already received.  It also  prints |
                  | a ^U on the terminal.  The input is then |
                  | returned to the task as if it were done. |
                  | It  is the responsibility of the calling |
                  | task to retry the input.                 |
                  --------------------------------------------

     Because the EMT breaks into the middle of the current  I/O  operation,
     the  message  may  be  unreadable unless you format it with separators
     such as carriage  returns  or  line  feeds.   You  may  also  find  it
     desirable  to  output  the  bell  character (^G) as a means of drawing
     attention to the message.

     As additional precautions, you may wish to 1) have the EMT continually
     output  the  emergency  message  until  it  receives   an  appropriate
     response, or 2) require a confirmation before further I/O can proceed.
     You  would  want to do this because the message could scroll off a CRT
     screen if another task transmits data to the CRT.
































                                     4-22

                             RTS/8 SYSTEM TASKS


4.6  EXIT TASK

     ----------------------------------------------------------------------
     | Use the exit task to perform special processing before  making  an |
     | exit from RTS/8.                                                   |
     ----------------------------------------------------------------------

     RTS/8 operations do not require the EXIT task.  However, if this  task
     is  in  your  system,  it  is run by the MCR EXIT command (see Section
     5.3.7).  Note that the EXIT task performs the same functions as  those
     performed  by the MCR EXIT command;  that is, it waits for any pending
     operations to be completed then turns off interrupts  and  returns  to
     the OS/8 operating system.

     In addition  to  normal  exit  processing,  the  EXIT  task  allows  a
     user-task  to request additional special exit processing just prior to
     shutting down RTS/8 by having the user-task send a message to the EXIT
     task.   This  message contains a single word, namely, the address of a
     routine (residing in the same field as  the  message)  that  the  task
     calls (with a JMS) at the time of the exit.

     When you type a MCR  EXIT  command,  these  routines  are  called  and
     executed in the priority order of calling tasks.

                  ------------------- NOTE -------------------
                  |                                          |
                  | Any message sent to the EXIT  task  will |
                  | not  get  posted.   Also, if you use the |
                  | MCR REQUEST  command  to  run  the  EXIT |
                  | task, the results are unpredictable.     |
                  --------------------------------------------

























                                     4-23

                             RTS/8 SYSTEM TASKS


4.7  FLOPPY DISK HANDLER

     ----------------------------------------------------------------------
     | Use the Floppy Disk Handler to perform I/O on a floppy.            |
     |                                                                    |
     | Message Format 1:                                                  |
     |                  ZBLOCK 3                                          |
     |                  CODE+DEL+MODE+UNIT                                |
     |                  RW+PAGES+FIELD                                    |
     |                  BUFADD                                            |
     |                  BLOKNO                                            |
     |                  STATUS                                            |
     |                                                                    |
     | Message Format 2:                                                  |
     |                  ZBLOCK 3                                          |
     |                  1000+CODE+DEL+MODE+UNIT                           |
     |                  RW+PAGES+FIELD                                    |
     |                  BUFADD                                            |
     |                  BLOKNO                                            |
     |                  STATUS                                            |
     ----------------------------------------------------------------------

     The format for this Handler is similar to other mass storage handlers;
     however,  the  fourth  word  is  different  (see Section 4.10 for more
     information).  When sending or receiving messages,  you  do  not  make
     distinctions between single and double density floppies as the handler
     has routines which determine the packing density.

     Message Format 2 exists to  maintain  compatibility  with  other  mass
     storage calls.  You would use it only if your task originally called a
     device using that format.

     The parameters of the above format statements are as follows:

          CODE  = 0        is  the  regular  condition.   The  Floppy  Disk
                           Handler  interprets  BLOKNO  as  an OS/8 logical
                           record number, and interprets pages in the  OS/8
                           sense  to  mean  the  number of PAGES of data to
                           transfer.  The Handler ignores the DEL bit.
                = 4000     is the special physical sector  condition.   The
                           Handler  ignores  PAGES  but  does  transfer one
                           segment,  namely,  the  segment   specified   by
                           BLOKNO.    The   Handler  interprets  BLOKNO  as
                           TTTTTTTSSSSS.  That is, the high order 7 bits of
                           this  word  represent  the physical track number
                           which must be in the range 0-76  decimal  (0-114
                           octal).    The   low-order   5  bits  of  BLOKNO
                           represent the sector number on that track.  This
                           number  must  be in the range 1-26 decimal (1-32
                           octal).

          DEL   = 0        ignores deleted data marks.
                = 2000     treats deleted marks (if CODE=4000) as follows:

                                1.  If writing a sector, write deleted data

                                     4-24

                             RTS/8 SYSTEM TASKS


                                    indication.   However, the Handler does
                                    not indicate this fact  in  the  STATUS
                                    word.

                                2.  If reading a sector, set bit 5  of  the
                                    STATUS  word  to  a  1  if  it  reads a
                                    deleted  data  indicator.   In  such  a
                                    case,  the  STATUS  word may be nonzero
                                    even though no physical error occurs.

          MODE  = 0        specifies transfer in 12-bit mode, which is  the
                           OS/8 format.  In 12-bit mode, the Handler places
                           the 64 (decimal) 12-bit words that  comprise  an
                           OS/8  floppy  sector  into the first 96 bytes of
                           the sector, while  the  last  32  bytes  contain
                           random  bit  patterns.  In 12-bit mode, a sector
                           contains 64 (decimal) 12-bit words of data.
                = 100      specifies transfer  in  8-bit  mode.   In  8-bit
                           mode,   an   8-bit   byte  on  the  floppy  disk
                           corresponds to the low order 8 bits of a  12-bit
                           word  in  memory.  The Handler does not transfer
                           data in the high order  4  bits  of  a  word  in
                           memory  to  the floppy.  In 8-bit mode, a sector
                           contains 128 (decimal) 8-bit bytes of data.

        UNIT               specifies the drive unit number.  It may be 0 or
                           1000.   The  number  0 refers to the unit on the
                           left of a dual drive.

        RW      = 0        reads data from floppy.
                = 4000     writes data to floppy.

        PAGES              specifies the number of pages to transfer (times
                           100  octal).   PAGES  =  0 transfers 40 pages (a
                           full field).  This value takes  the  range  0-37
                           (octal)  in  bits 1-5 of this word.  The Handler
                           ignores  PAGES  if  CODE=4000.   For  a   single
                           density floppy, if CODE equals 4000, the Handler
                           transfers either 100 (octal) 12-bit words or 200
                           8-bit  bytes (from 200 words) depending on MODE.
                           For  a  double  density  floppy,   the   Handler
                           transfers twice as much information.

        FIELD              is the standard RTS/8 mass storage FIELD  format
                           (see Section 4.10).

        BUFADD             specifies the address of the first word  of  the
                           buffer  containing  data.  FIELD  determines the
                           field of the buffer.  You specify the length  of
                           the  buffer  by  PAGES  if  CODE=0 or by MODE if
                           CODE=4000.

        BLOKNO             represents  the  first  logical  OS/8  block  to
                           transfer if CODE=0.  Each OS/8 block consists of
                           four sectors.  The Handler ignores track  0  and

                                     4-25

                             RTS/8 SYSTEM TASKS

                           it  employs  a  2  to  1  interleave scheme.  If
                           CODE=4000, this word contains the physical track
                           and sector numbers in the format TTTTTTTSSSSS.

        STATUS             receives the status of the  operation  upon  its
                           completion.  If it is negative, a hardware error
                           occurred.  If it is  zero,  no  error  occurred.
                           This word may be a positive, nonzero number only
                           if DEL=2000.  See Table 4-5 for descriptions  of
                           the STATUS bits.

                                   Table 4-5
                        Floppy Status Bit Descriptions

     ----------------------------------------------------------------------
     |     |                       Meaning if 1                           |
     |     |--------------------------------------------------------------|
     | Bit |       Single Density        |        Double Density          |
     |-----|--------------------------------------------------------------|
     | O   | Hard error                  | Hard error                     |
     | 1-3 | Not used by controller      | Not used by controller         |
     | 4   | Not used by RTS/8           | Selected Drive Ready           |
     | 5   | Deleted data indication     | Deleted data indication        |
     | 6,7 | Not used by controller      | Not used by controller         |
     | 8   | Reserved for future use     | RX02 Drive                     |
     | 9   | INIT done (can occur after  | INIT done (can occur after     |
     |     | temporary power failure to  | temporary power failure to     |
     |     | controller)                 | controller)                    |
     | 10  | Parity error                | Side 1 Ready                   |
     | 11  | CRC (Cyclic Redundancy      | CRC (Cyclic Redundancy Check)  |
     |     | Check) error                | error                          |
     ----------------------------------------------------------------------

     The following two figures illustrate bit positions and their meanings.

                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^   ^   ^           ^                         ^
                          |   |   |________   |                         |
                          |   |_________  |   |                         |
                          |__________  |  |   |                         |
     0:  Regular condition       \__|  |  |   |                         |
     1:  Special physical sector /     |  |   |                         |
         condition                     |  |   |                         |
                                       |  |   |                         |
     0:  Do not handle deleted marks \_|  |   |                         |
     1:  Handle deleted marks        /    |   |                         |
                                          |   |                         |
     RL01 Mode ___________________________|   |                         |
                                              |                         |
     0:  Transfer in 12-bit mode \____________|                         |
     1:  Transfer in 8-bit mode  /                                      |
                                                                        |
     0:  Left unit of dual drive  \_____________________________________|
     1:  Right unit of dual drive /

                                     4-26

                             RTS/8 SYSTEM TASKS


     CODE = 4000 (bit 0 set to 1) transfers one sector specified by BLOCKNO
     as follows:

                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                         \_________________________/ \___________________/
                                      |                       |
     Physical track no. ______________|                       |
     (0-114 octal)                                            |
                                                              |
     Sector no. on track _____________________________________|
     (1-32 octal)

                Figure 4-9 Floppy Disk Handler Unit Word Format


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^                   ^               ^    ^    ^
                          |                   |               |    |    |
        Hard error _______|                   |               |    |    |
                                              |               |    |    |
        Deleted data _________________________|               |    |    |
                                                              |    |    |
        INIT done ____________________________________________|    |    |
                                                                   |    |
        Parity error ______________________________________________|    |
                                                                        |
        CRC error ______________________________________________________|

              Figure 4-10 Floppy Disk Handler Status Word Format


     The largest legal OS/8 block number on a single density floppy disk is
     755  octal.  For a double density floppy, the largest legal OS/8 block
     number is 1733.  If you reference any block number  greater  than  755
     for  a  single density floppy or 1733 for a double density floppy, the
     Handler returns in STATUS the negative of the number of BLOKNO on  the
     device.

     Note that no hardware indication exists of a write  operation  to  the
     wrong  density media.  The Handler precedes most write operations by a
     directory  read  that  signals  the  device's   density.    For   more
     information  on  the  relationship  between  single and double density
     floppies, see the appropriate hardware and software manuals.

     Table 4-6 lists the standard OS/8 interleave  scheme  for  single  and
     double density floppies.






                                     4-27

                             RTS/8 SYSTEM TASKS


                                   Table 4-6
                      OS/8 Floppy Disk Interleave Scheme

     ----------------------------------------------------------------------
     |        OS/8   |     Floppy Sectors (track/sector--decimal)         |
     | Logical Block |----------------------------------------------------|
     |    (octal)    |       Single Density           |  Double Density   |
     |---------------|----------------------------------------------------|
     |      0        | 1/1     1/3     1/5     1/7    |  1/1     1/4      |
     |               |                                |                   |
     |      1        | 1/9     1/11    1/13    1/15   |  1/7     1/10     |
     |               |                                |                   |
     |      2        | 1/17    1/19    1/21    1/23   |  1/13    1/16     |
     |               |                                |                   |
     |      3        | 1/25    1/2     1/4     1/6    |  1/19    1/22     |
     |               |                                |                   |
     |      4        | 1/8     1/10    1/12    1/14   |  1/25    1/2      |
     |               |                                |                   |
     |      5        | 1/16    1/18    1/20    1/22   |  1/5     1/8      |
     |               |                                |                   |
     |      6        | 1/24    1/26    2/1     2/3    |  1/11    1/14     |
     |               |                                |                   |
     |      7        | 2/5     2/7     2/9     2/11   |  1/17    1/20     |
     |               |                                |                   |
     |      10       | 2/13    2/15    2/17    2/19   |  1/23    1/26     |
     |               |                                |                   |
     |      11       | 2/21    2/23    2/25    2/2    |  1/3     1/6      |
     |               |                                |                   |
     |      12       | 2/4     2/6     2/8     2/10   |  1/9     1/12     |
     |               |                                |                   |
     |      13       | 2/12    2/14    2/16    2/18   |  1/15    1/18     |
     |               |                                |                   |
     |      14       | 2/20    2/22    2/24    2/26   |  1/21    1/24     |
     |               |                                |                   |
     |      15       | 3/1     3/3     3/5     3/7    |  2/1     2/4      |
     |               |                                |                   |
     |      .        |                                |                   |
     |      .        |                                |                   |
     |      .        |                                |                   |
     ----------------------------------------------------------------------

     OS/8 does not use Track O and you cannot access it in the 12-bit mode.














                                     4-28

                             RTS/8 SYSTEM TASKS


     4.8  LINCTAPE HANDLER

     ----------------------------------------------------------------------
     | Use the LINCtape Handler to perform I/O on LINCtape which  is  in  |
     | either OS/8 or DIAL format.                                        |
     |                                                                    |
     | Message Format 1:                                                  |
     |                  ZBLOCK 3                                          |
     |                  MODE+UNIT                                         |
     |                  RW+PAGES+FIELD                                    |
     |                  BUFADD                                            |
     |                  BLOKNO                                            |
     |                  STATUS                                            |
     |                                                                    |
     | Message Format 2:                                                  |
     |                  ZBLOCK 3                                          |
     |                  1000+MODE+UNIT                                    |
     |                  RW+PAGES+FIELD                                    |
     |                  BUFADD                                            |
     |                  BLOKNO                                            |
     |                  STATUS                                            |
     ----------------------------------------------------------------------

     You normally use Message Format 1.  The second  format  (the  absolute
     block format) is for compatibility with tasks originally developed for
     devices using that format.

     The parameters of the above format statement are as follows:

          MODE  = 0       specifies OS/8.  An OS/8 LINCtape contains 200 or
                          201 (octal) words per physical block.
                = 4000    specifies DIAL  mode.   A  DIAL  LINCtape  should
                          contain 400 (octal) words per physical block.

                             ------------------- NOTE --------------------
                             |                                           |
                             | The LINCtape Handler does  not  check  to |
                             | determine  if  the  LINCtape  is properly |
                             | formatted for the specific mode.  Using a |
                             | LINCtape with an improper physical format |
                             | produces unpredictable results.           |
                             ---------------------------------------------

          UNIT            specifies the LINCtape unit number in the range 0
                          to 7.

          RW    = 0       reads data from LINCtape.
                = 4000    writes data to LINCtape.

          PAGES           specifies  the  number  of  128-word   pages   to
                          transfer   (times   100   octal).   For  example,
                          PAGES=2000  transfers  20  octal  pages  or  2048
                          words;   if  PAGES=0,  the  Handler  transfers 40
                          octal pages or 4096 words.


                                     4-29

                             RTS/8 SYSTEM TASKS


          FIELD           specifies the PDP-8 field in which  the  transfer
                          takes  place  (times  10  octal).   The format of
                          FIELD is in the standard OS/8 mass storage  field
                          format.     (See   Section   4.10   for   further
                          information.)

          BUFADD          is the starting  address  of  the  buffer  to  be
                          transferred.

          BLOKNO          is the block number on the device from which  the
                          transfer begins.  The Handler assumes all devices
                          have 256-word blocks.  On an OS/8  LINCtape,  two
                          consecutive  physical  blocks  comprise  one OS/8
                          logical block.  Note  that  only  the  first  128
                          words  in  each physical block contain meaningful
                          data.

                          When running in DIAL mode,  BLOKNO  represents  a
                          physical  LINCtape  block  number.  In this case,
                          PAGES must be even because the Handler  transfers
                          an   even   number   of   pages.    If  PAGES  is
                          (incorrectly) odd, the Handler does not  transfer
                          the  last  page.   The  exception to this is when
                          PAGES=1;  this value  instructs  the  Handler  to
                          transfer one block (2 pages).

          STATUS          is the one's complement of tape check (checksum).
                          The  value 0 means no error.  Note that STATUS is
                          always 0 on a write operation.  When the  handler
                          performs   any   operation,   it  attempts  three
                          software retries on a checksum read error.  Also,
                          the  hardware  performs  an  infinite  number  of
                          retries on most errors (write-lock-out, tape  not
                          mounted,  bad  spot  on tape) and does not return
                          control to RTS/8 until successful.


                 ------------------- NOTE -------------------
                 |                                          |
                 | In   the   OS/8   mode,   the    Handler |
                 | temporarily  destroys the word following |
                 | the end of the buffer while  a  LINCtape |
                 | operation  is  in progress.  The Handler |
                 | restores the location when it  completes |
                 | the  operation.  However, since RTS/8 is |
                 | a  real-time   system,   code   may   be |
                 | executing while the tape operation is in |
                 | progress.  Consequently, you must ensure |
                 | that  no  program  ever  references this |
                 | word while the LINCtape is  being  used. |
                 | Under  no  circumstances should the word |
                 | following the end of the  buffer  belong |
                 | to another task.                         |
                 --------------------------------------------


                                     4-30

                             RTS/8 SYSTEM TASKS


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^       ^                          \___________/
                          |       |                                |
        0:  OS/8 mode \___|       |                                |
        1:  DIAL mode /           |                                |
                                  |                                |
        RLO1 Mode ________________|                                |
                                                                   |
        Unit number _______________________________________________|

                 Figure 4-11 LINCtape Handler Unit Word Format











































                                     4-31

                             RTS/8 SYSTEM TASKS


4.9  LINE PRINTER HANDLER

     ----------------------------------------------------------------------
     | Use the Line Printer Handler  to  output  information  to  a  line |
     | printer.                                                           |
     |                                                                    |
     | Message Format 1:                                                  |
     |                  ZBLOCK 3                                          |
     |                  COMMND+LENGTH                                     |
     |                  ZBLOCK 1                                          |
     |                  OUTTXT                                            |
     |                                                                    |
     | Message Format 2:                                                  |
     |                  ZBLOCK 3                                          |
     |                  ASSGN+TSKNUM                                      |
     |                                                                    |
     | Message Format 3:                                                  |
     |                  ZBLOCK 3                                          |
     |                  -2                                                |
     |                  CDF OUTBUF                                        |
     |                  COMMND+LENGTH                                     |
     |                  ZBLOCK 1                                          |
     |                  OUTTXT                                            |
     |                                                                    |
     | where:                                                             |
     |       COMMND    is  one  of  the  commands  listed  in  Table  4-4 |
     |                 (Console Terminal Commands).                       |
     |       LENGTH    is the number of characters in the line.           |
     |       OUTTXT    is the first word of the output text or a  pointer |
     |                 to it.                                             |
     |       ASSGN     is an RTS/8 mnemonic having a value  of  200  that |
     |                 causes  the  Handler  to be assigned to a specific |
     |                 task (or deassigned if TSKNUM=0).                  |
     |       OUTBUF    is the field of the output buffer.                 |
     ----------------------------------------------------------------------

     You use FORMAT 1 to output text.

     You use FORMAT 2 to assign the Line  Printer  Handler  to  a  specific
     task.  To deassign the Handler, specify TSKNUM=0.

     You use FORMAT 3 when the output buffer is in a field  different  from
     that of the message.

     The RTS/8 Line Printer Handler outputs to an LS8, LS8E,  LP8,  or  LV8
     line  printer.   The format of messages to the Line Printer Handler is
     identical to the format of messages to the Terminal Handler,  but  the
     Handler  ignores  the  INBUF word of the Terminal Handler (represented
     above by ZBLOCK 1) and the LINE/NOLINE bit.   (The  INBUF  word  must,
     however, be present in the message.)

     The following figures  illustrate  the  bits  that  the  Line  Printer
     Handler uses.



                                     4-32

                             RTS/8 SYSTEM TASKS


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^   ^   ^   ^   ^   \__________________________/
                          |   |   |   |   |____           |
     Command (bits 0-4)   |   |   |   |______ |           |     __________________
     0:  Packed ASCII   \_|   |   |________ | |           |
     1:  Unpacked ASCII /     |__________ | | |           |
                                        | | | |           |
     0:  CR/LF at end of message    \___| | | |           |
     1:  No CR/LF at end of message /     | | |           |
                                          | | |           |
     0:  OUTTXT is the first word    \____| | |           |
     1:  OUTTXT points to first word /      | |           |
                                            | |           |
     0:  Input in line mode      \__________| |           |
     1:  Input in character mode /            |           |
                                              |           |
     Bit 4 must be a 0 _______________________|           |
                                                          |
     Length (bits 5-11)                                   |     __________________
     If bit 3=1 no. of characters to input   \____________|
     If bit 3=0 maximum size of input buffer /

            Figure 4-12  Line Printer Handler I/O Mode Command and
                              Length Word Format


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                         \_____________/  ^   ^  \_______________________/
                                |         |   |             |
        Unused _________________|         |   |             |
                                          |   |             |
        Bit 4 must be a 1 ________________|   |             |
                                              |             |
        Unused _______________________________|             |
                                                            |
        Task Number ________________________________________|

     Figure 4-13 Line Printer Handler ASSGN Mode Command Word Format














                                     4-33

                             RTS/8 SYSTEM TASKS


     4.10  MASS STORAGE HANDLERS

     ----------------------------------------------------------------------
     | Use the Mass Storage Handlers to perform  I/O  on  DF32  and  RF08 |
     | fixed head disks, RK8 and RK8E moving-head disks, and TC08 DECtape |
     | units.                                                             |
     |                                                                    |
     | Message Format 1:                                                  |
     |                  ZBLOCK 3                                          |
     |                  UNIT                                              |
     |                  RW+PAGES+FIELD                                    |
     |                  BUFADD                                            |
     |                  BLOKNO                                            |
     |                  STATUS                                            |
     |                                                                    |
     | Message Format 2:                                                  |
     |                  ZBLOCK 3                                          |
     |                  1000+UNIT                                         |
     |                  RW+PAGES+FIELD                                    |
     |                  BUFADD                                            |
     |                  BLOKLO                                            |
     |                  STATUS                                            |
     |                  BLOKHI                                            |
     ----------------------------------------------------------------------


                  ------------------ NOTE --------------------
                  |                                          |
                  | Floppy Disk and  LINCtape  mass  storage |
                  | usages  are  discussed elsewhere in this |
                  | manual.                                  |
                  --------------------------------------------

     You normally use Message Format 1 for all devices that have less  than
     4096  blocks.   This  message  format is compatible with the OS/8 file
     structure.  For devices which have more than 4096 blocks (such  as  an
     RK8E  or  an RL01), the handler divides the physical unit into several
     logical units.

     Message Format 2 supports 24 bit device addresses (as opposed  to  the
     12  bit  address of Format 1).  However, Format 2 is incompatible with
     OS/8 for devices which have more than 4096  blocks.   Note  that  this
     message format has one logical device for each physical device.

     If your device has less than 4096 blocks,  Format  2  gives  the  same
     results as Format 1.

     The parameters of the above format statement are as follows:

          UNIT      is  the  number  of  the  logical  unit  on  which  the
                    operation  is  to  be  performed.   DF32 and RF08 disks
                    consist of only one unit.   TC08  DECtape  has  logical
                    units  0-7  corresponding  to their physical units 0-7.
                    RK8 disks have logical units 0-3 corresponding to their
                    physical  units  0-3.  RK8E disk has logical units 0-7.

                                     4-34

                             RTS/8 SYSTEM TASKS


                    In this case, units 0-3 correspond to the outer  (lower
                    track number) half of physical units 0-3, and units 4-7
                    correspond to the inner (higher track number)  half  of
                    physical units 0-3, respectively.

                    In  Format  1,  the  RL01  physical  unit/logical  unit
                    correspondence is as follows:

                         Physical   Logical
                           Unit       Unit

                             0      0,  1,  2
                             1      4,  5,  6
                             2     10, 11, 12
                             3     14, 15, 16


                       ------------------- NOTE -------------------
                       |                                          |
                       | In Format 1,  a  physical  unit  may  be |
                       | divided into more than one logical unit; |
                       | for example, an  RK05  disk  is  divided |
                       | into  RKA0  and  RKB0.  In Format 2, the |
                       | absolute  block  format,  each  physical |
                       | unit is a logical unit.  Here, you would |
                       | specify the  block  number  by  the  two |
                       | words  BLOKHI  and  BLOKLO.   This means |
                       | that Format 2  is  not  compatible  with |
                       | OS/8 for an RK05 or an RL01.             |
                       --------------------------------------------

          RW        is 0  for  a  read  operation  and  4000  for  a  write
                    operation.

          PAGES     specifies the number of (128-word)  pages  to  transfer
                    (times  100  octal).  For example, PAGES=2000 specifies
                    the transfer of 20 (octal) pages  of  2048  words;   if
                    PAGES=0, the Handler transfers 40 (octal) pages or 4096
                    words.

          FIELD     is the PDP-8 field in which the  transfer  takes  place
                    (times  10  octal).   For  example,  if  FIELD=30,  the
                    transfer takes place in field 3.

                    All FIELD specifications for Mass Storage Handlers  are
                    in  bits  6-10.   Of the five field bits, the low order
                    three bits are in positions 6-8 (not 8-10).   The  high
                    order  bit is in bit 10 and the remaining bit is in bit
                    9.

                    If you think of the normal bit order  as  being  ABCDE,
                    then  the  order into which you place these bits in all
                    Mass Storage Handlers is CDEBA.



                                     4-35

                             RTS/8 SYSTEM TASKS


                    Note  that  the  MACREL  directive  XEDF  automatically
                    places the bits into this order.

          BUFADD    is  the  starting  address  of   the   buffer   to   be
                    transferred.

          BLOKNO    is the block  number  on  the  device  from  which  the
                    transfer  begins.  The Handler assumes 256-word blocks.
                    On DECtape, the first 128 words of each  even/odd  pair
                    of 129-word DECtape records are defined as a block.

          STATUS    is a word that the Handler sets on  completion  of  the
                    operation.   It  contains  a  zero  if the operation is
                    successful, otherwise it contains  a  nonzero  quantity
                    that  is  the  contents  of the device status register.
                    Tasks that use the Mass Storage  Handlers  should  test
                    this word after it completes an I/O operation (that is,
                    after the event flag has been posted) to  determine  if
                    any  errors   occurred  during the transfer.  All RTS/8
                    Mass Storage Handlers retry operations three  times  if
                    they encounter errors before setting the STATUS word to
                    a nonzero number.  For the meanings of the STATUS word,
                    see the appropriate device manual.

          BLOKHI   is the high order part of the block address.

          BLOKLO   is the low order part of the block address.

     The middle three words of a message to the RTS/8 Mass Storage Handlers
     are  identical  to  the arguments to an OS/8 Handler when they perform
     the same operation.

     The following figures illustrate bit positions which the Handler uses.


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                         ^        ^  \_________________/ \_______________/
        Call Format _____|        |           |                 |
                                  |           |                 |
        RL01 Mode ________________|           |                 |
                                              |                 |
        Reserved for task use ________________|                 |
                                                                |
        Unit ___________________________________________________|

              Figure 4-14 Mass Storage Handlers Unit Word Format








                                     4-36

                             RTS/8 SYSTEM TASKS


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^  \_________________/ \__________________/   ^
                          |           |                   |             |
                          |_____      |                   |             |
                               |      |                   |             |
        0:  Read operation  \__|      |                   |             |
        1:  Write operation /         |                   |             |
                                      |                   |             |
        No. of pages to transfer _____|                   |             |
                                                          |             |
        0-37:  Field of transfer _________________________|             |
                                                                        |
        Reserved for task use __________________________________________|

            Figure 4-15 Mass Storage Handlers Function Word Format


     Examples:

                      CAL
                      SENDW
                      DTA             /SEND A MESSAGE TO THE DECTAPE
                                      / HANDLER
                      DTAMSG          /WAIT FOR COMPLETION
                      TAD STATUS      /CHECK THE STATUS OF THE OPERATION
                      SZA CLA
                      JMP ERR         /BAD--GO TO ERROR ROUTINE
                      .               /OK--CONTINUE PROCESSING
                      .
                      .
          DTAMSG,     ZBLOCK 3        /MESSAGE HEADER
                      4               /DECTAPE UNIT 4
                      4210            /WRITE 256 WORDS FROM FIELD 1
                      BUFFER          /ADDRESS OF BUFFER
                      55              /INTO BLOCK 55 (RECORDS 132 & 133)
          STATUS,     0               /STATUS OF OPERATION STORED HERE


















                                     4-37

                             RTS/8 SYSTEM TASKS


     4.11  OS/8 FILE SUPPORT TASK

     ----------------------------------------------------------------------
     | Use the OS/8 file support task to  look  up,  create,  and  delete |
     | files in OS/8 directories from a foreground task.                  |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                DEVHND 10+UNIT+FUNCT                                |
     |                FILPTR                                              |
     |                STATUS                                              |
     |                BLOKNO                                              |
     |                LENGTH                                              |
     ----------------------------------------------------------------------

     This task allows you to look up,  create, and  delete  files  in  OS/8
     directories  in  the  same manner as if you were using OS/8.  You need
     not have the OS/8 support task in your system to be able to  use  this
     task.

     If both OS8F and the OS/8 Support Task are present  in  a  system,  an
     interlock  is  set  up  to  prevent simultaneous updating of directory
     blocks by both tasks.  Note that because OS/8 tends to leave directory
     blocks  in  memory  for  long  periods  of time, this interlock scheme
     causes lengthy delays for the OS8F task.

     The parameters of the above format statement are as follows:

          DEVHND          is the task number of the Handler for the desired
                          device.

          UNIT            is the unit number on which the operation  is  to
                          be performed.

          FUNCT  = 0      looks up the filename and  returns  its  starting
                          block  number in BLOKNO, and its length in LENGTH
                          (as a two's complement number).
                 = 2000   enters the specified filename into the first
                          empty space (on the device) whose length is equal
                          to or exceeds the value in LENGTH.  It returns
                          the starting block number of the new file in
                          BLOKNO.  If a file of the same name previously
                          existed on the device, the support task deletes
                          the file. However, it does not change the value
                          of LENGTH.

                 = 4000   deletes the specified filename.

        FILPTR            is a pointer to a 4-word  filename  in  the  same
                          field  as  the message.   You  can use the MACREL
                          pseudo-op FILENAME to generate these filenames.

        STATUS            describes the final status of  the  operation  as
                          follows:


                                     4-38

                             RTS/8 SYSTEM TASKS


                          0    Operation successful.
                          1    File not found on a lookup or delete
                               operation.
                          2    No room for file on enter operation.
                          >2   I/O error.  The value is the hardware error
                               status of the device.
                          -1   Invalid directory on device.


                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                         \_____/ \_________________________/ \___________/
                            |                 |                    |
        Function: __________|                 |                    |
        O Lookup                              |                    |
        1 Enter                               |                    |
        2 Delete                              |                    |
        3 Unused                              |                    |
                                              |                    |
        Task number __________________________|                    |
                                                                   |
        Unit ______________________________________________________|

                      Figure 4-16 OS8F Call Function Word


     Before it performs a delete or enter operation, OS8F waits until  OS/8
     is in a state in which:

          1.  There  is  no  active  temporary  file  on  the  OS/8  device
              corresponding to devhnd and unit.

          2.  OS/8 loads the Keyboard Monitor, Command Decoder, or USR into
              core.

     RTS/8 does not interlock look up operations since they do  not  modify
     the directory.


















                                     4-39

                             RTS/8 SYSTEM TASKS


     4.12  OS/8 SUPPORT TASK

     ----------------------------------------------------------------------
     | The OS/8 support task supports the execution of an OS/8 operating  |
     | system in the background of a foreground/background system.        |
     ----------------------------------------------------------------------

     The OS/8 Support Task executes the OS/8 operating  system  as  a  task
     under RTS/8.  Note that the OS/8 File Support Task is not necessary to
     run this task.  OS/8 is usually run in the  top  two  or  more  memory
     fields  of  a  system.   However,  if  the  system  has a KT8-A memory
     controller, the OS/8 fields, although  still  contiguous,  may  reside
     elsewhere.

     A user incorporates the OS/8 Support Task into a  system  when  it  is
     generated.    When   RTS/8   initializes   OS/8,   it   establishes  a
     correspondence between OS/8 devices and  RTS/8  Handler  tasks.   Note
     that  terminal input and output from OS/8 are ring-buffered by several
     characters to minimize input loss due to the stealing of  the  CPU  by
     tasks  of higher priority.  Because of the large number of trapped CDF
     instructions in OS/8 and its utilities, response time is  slower  than
     that  of  a  stand-alone  OS/8  system;   however,  it  is still quite
     reasonable.

     KT8A systems execute background CDFs, RDFs, and RIFs in the  hardware.
     Consequently,  background processing runs at nearly the same speed as
     that of OS/8 running alone.

     Because a foreground task and the background OS/8 operating system may
     share  the  same  terminal,  you may interactively specify whether the
     terminal belongs to the foreground or the background.  If you  type  a
     CONTROL/B  (^B)  and  a  carriage  return  or  an ESCAPE, the Terminal
     Handler gives control  of  the  terminal  to  OS/8.   If  you  type  a
     CONTROL/F  (^F)  while  OS/8  has  control,  the Terminal Handler will
     return to RTS/8 foreground operation.  For additional information, see
     Section 4.5.

     If you type a B while the terminal belongs to the background or  a  ^F
     while it belongs to the foreground, the terminal treats the command as
     a no-opt

     The OS/8 system that runs under this  task  runs  all  OS/8  utilities
     except BUILD, BOOT, PIP10, RXCOPY, INDUSTRIAL BASIC, and the BASIC and
     FORTRAN laboratory runtime functions.  If the console terminal and the
     OS/8  terminal are not the same, the Handler diverts all references to
     the appropriate device.  In the same manner, the Handler also  diverts
     references  in OS/8 to the LEO, LS8E, LP8, or LV8 line printers to the
     RTS/8 Line  Printer  Handler  if  the  RTS/8  system  has  this  task;
     otherwise,   the  support  task  executes  them.   RTS/8  diverts  the
     following OS/8 device  name  references  to  the  corresponding  RTS/8
     Handler (if that Handler exists in the RTS/8 system):

          DTA0-DTA7
          LTA0-LTA7
          RKA0-RKA3

                                     4-40

                             RTS/8 SYSTEM TASKS


          RKB0-RKB3
          RLOA-RL6A
          RXA0-RXA7

     In addition, RTS/8 diverts the  OS/8  SYS  and  DSK  Handlers  to  the
     handlers specified when the system was generated.  Other references to
     I/O under the OS/8 system may cause the OS/8 support task to hang in a
     loop.  References to a handler called RTS8 are diverted to OS8COM (see
     Section 4.12.1).


                  ------------------ NOTE --------------------
                  |                                          |
                  | If neither the support task nor OS/8 are |
                  | configured  for the handlers you wish to |
                  | use, then you should run OS/8  alone  on |
                  | the  system and use BUILD to incorporate |
                  | the  handlers  into  OS/8.   After   you |
                  | configure   OS/8,  you  may  run  RTS/8. |
                  --------------------------------------------

     If the background OS/8 task is in a loop or hangs up, you  may  reboot
     it without disturbing the foreground by typing a CONTROL/Y ( Y).  This
     reads the OS/8 system header blocks off the  OS/8  system  device  and
     restarts the OS/8 background.

     RTS/8 prints

          FATAL BKG ERROR
               (fatal background error)
     or
          BOOT ERROR


     if it cannot start or restart OS/8 or exit from RTS/8 to OS/8.   These
     error  messages  appear  on  the  background  terminal. These messages
     indicate that the background OS/8 task cannot run.  However, all other
     RTS/8   tasks   still  execute.   These  messages  may  occur  if  you
     inadvertently attempt to run OS/8 from a non-system disk.

     Recovery from this error is not possible while running RTS/8.  To  use
     OS/8  you  must  abort  RTS/8  and  then restart the system, this time
     having the RTS/8.SV image on the OS/8 system disk.


     4.12.1  OS/8-RTS/8 Communication (OS8COM)

     an RTS/8 task.  To perform this communication, the system must include
     the RTS8 Handler.  This Handler can be a dummy;  that is, it need  not
     do  anything.   (In  fact,  it  can be some other Handler to which you
     assign the name RTS8 with an OS/8 ASSIGN command or through  the  OS/8
     BUILD program.)

     The OS/8 Support Task traps all calls to this Handler.  The  arguments
     that an OS/8 program attempts to pass to the RTS8 Handler will instead

                                     4-41

                             RTS/8 SYSTEM TASKS


     be passed to an RTS8 task called OS8COM.

     The OS8COM task performs an RTS/8  RECEIVE  ER.   The  task  can  then
     receive a message any time an OS/8 program reads or writes to the RTS8
     Handler.  This message looks like any other message to a mass  storage
     device.   However, OS8SUP makes one change to the arguments.  Bits 6-8
     of the function word originally contain the field of the  buffer,  and
     this  is  the field where OS/8 expects the buffer to be located.  When
     OS8COM gets  control,  these  bits  identify  the  actual  field  that
     contains  the  buffer.  OS8COM can then return information to the OS/8
     through these arguments.

     An OS/8 program that runs an RTS/8 task  is  shown  in  the  following
     example:

                  USER=7700       /LOCATION OF OS/8 USER SERVICE ROUTINE
                  JMS PRINT       /PRINT MESSAGE "WHAT TASK WOULD YOU
                                  /   LIKE TO RUN?" ON THE OS/8 TERMINAL
                  JMS READ        /READ RESULTS FROM OS/8 KEYBOARD
                                  /   RETURNS TASK NUMBER IN RANGE 1-177
                                  /   (OCTAL) IN AC
                  DCA TASKNO      /STORE IT AWAY
                  CIF 10
                  JMS I (USR      /CALL USR
                  1               /TO DO A FETCH
                  DEVICE RTS8     /OF DEVICE "RTS8"
          ENTRY,  ADDR            /DUMMY ADDRESS (HANDLER WILL ALREADY
                                  /   BE RESIDENT)
                  HLT             /ERROR (HANDLER NOT FOUND)

     /NOTE:  THIS CODE IS NOT REUSABLE.  ALSO, LOCATION "ENTRY"
     /IS SET TO THE ENTRY POINT FOR THIS HANDLER

                  CIF 0
                  JMS I ENTRY     /CALL HANDLER
                  0               /DUMMY READ
          TASKNO, 0               /TASK NUMBER
                  ZBLOCK 2        /DUMMY
                  JMP I (7605     /RETURN TO OS/8

     You should note that the task passes TASKNO  as  the  second  argument
     instead of the first because OS8SUP automatically modifies bits 6-8 of
     the first argument, presuming that it will find a mapped field  number
     there.

     OS8COM expects three arguments after the Handler call  plus  an  error
     return.  You must supply these arguments.

     After writing the OS/8 portion of the program, you must also write the
     OS8COM  task  that handles the RTS/8.  You write OS8COM like any other
     RTS/8 user task, as the following example illustrates:





                                     4-42

                             RTS/8 SYSTEM TASKS


                     .TASK OS8COM            /TASK NUMBER IS OS8COM
                                             /IN THE PARAMETER FILE
                                             /NAMETAB GETS 'OS8COM'
                                             /IT IS RUNNABLE BY DEFAULT
                     .RSECT OS8SCT,LEVEL=0   /ARBITRARY SECTION NAME
          START,     CAL
                     RECEIVE         /IMMEDIATELY GO INTO RECEIVE WAIT
          MADDR,     0               /ADDRESS OF MESSAGE LEFT HERE
                     DCA MSGFLD      /CDF TO MESSAGE FIELD LEFT IN AC
          MSGFLD,    HLT
                     ISZ MADDR       /POINT TO FUNCTION WORD
                     ISZ MADDR       /POINT TO BUFFER ADDRESS
                                     /   (SECOND OS/8 ARGUMENT)
                     TAD I MADDR     /GET TASK NUMBER
                     CAL
                     RUN             /RUN THIS TASK
                                     /OS8COM WANTS TO BE HIGHER PRIORITY
                                     /   THAN TASK IT IS RUNNING
                     TAD MSGFLD
                     DCA EFCDF
                     TAD (-5)
                     TAD MADDR       /GET ADDRESS OF EVENT FLAG MESSAGE
                     CAL
                     POST            /POST MESSAGE
          EFCDF,     HLT
                     JMP START       /GET ANOTHER MESSAGE

     In this example, the task number was put in the second argument of the
     OS/8  call.   However,  it  became the third word of the RTS/8 message
     because OS8SUP always adds a word--namely the unit number--to the mass
     storage  call  argument  list.   For a description of the OS/8 Handler
     call format, see Section 4.1 of the OS/8 Software Support Manual.  For                                         ____________________________
     a  description of the message format for mass storage devices, see the
     appropriate sections in this manual.


     4.12.2  Other Techniques

     Other techniques which you may employ are:

          1.  If the RTS/8 Handler STATUS word  (word  5)  of  the  message
              which  OS8COM  posts  is nonzero, then the handler returns to
              OS/8 at the error return of the Handler call.

          2.  You may pass arguments back  to  OS/8  through  the  argument
              list.

          3.  If you pass more than three words  of  data  to  OS8COM  from
              OS/8,  you  can  pass a CDF and the address of the area where
              the data resides.  If the CDF occurs as the first argument to
              the  Handler  call,  the  Handler  automatically relocates it
              before passing it to OS8COM.  Note that  the  field  of  data
              must be in the locations that OS/8 uses and not the locations
              which RTS/8 can use.


                                     4-43

                             RTS/8 SYSTEM TASKS

     4.13  PDP-8A NULL TASK

     ----------------------------------------------------------------------
     | Use the PDP-8A null task  to  count  in  decimal  on  the  console |
     | accumulator LED display.                                           |
     ----------------------------------------------------------------------

     The PDP-8A null  task  counts  from  1  to  9999  in  decimal  in  the
     accumulator  display,  and  counts  from  1 to 7777 in octal in the MQ
     display.















































                                     4-44

                             RTS/8 SYSTEM TASKS


     4.14  POWER FAIL TASK

     Use this task to provide for an orderly shutdown when  power  is  lost
     and to allow a programmed restart when power returns.

     The Power Fail  Task  provides  the  mechanism  by  which  the  system
     recovers  from  a  power failure.  You use this task only with systems
     that have core memory.

     If a "power low" condition occurs, the power fail hardware  interrupts
     the  running  task.   The  power  fail  interrupt  code then saves the
     processor state and halts the  processor.   When  power  returns,  the
     power  fail  interrupt  code restores the processor state and posts an
     event flag which wakes up the Power Fail Task.  The  Power  Fail  Task
     restores  the clock (if it is present) and also performs an action for
     each task in the system based on the contents of  an  internal  table.
     Each task has a 1-word entry in this table, which contains:

          0         if nothing  should  be  done  for  this  task  (default
                    value).

          -1        if the EFWT (event flag wait) bit should be cleared  in
                    the Task Flags Table entry for this task.

          ADDR      if the task should be derailed to location ADDR in  the
                    field  in which it is executing as well as clearing its
                    EFWT bit.

     The Power Fail Task uses the DERAIL Executive Request to  provide  for
     power fail recovery.

     Each task in the system may alter its entry in the Power  Fail  Task's
     table  by sending a message to the Power Fail Task.  The format of the
     message is:

          PWRMSG,    ZBLOCK 3
                     WORD
     where:

          WORD       is the new contents of the  Power  Fail  Task's  table
                     entry  for the sending task (that is, this task should
                     be taken out of Event Flag Wait).

     The Handler call is as follows:

                  CAL
                  SEND
                  PWRF
                  PWRMSG
                  .
                  .
                  .
          PWRMSG, ZBLOCK 3
                  VALUE


                                     4-45

                             RTS/8 SYSTEM TASKS


     4.15  UDC/ICS HANDLER

     The UDC/ICS Handler gives you the capability to  control  the  various
     types  of  UDC/ICS functional devices.  The Handler performs two types
     of  action:   immediate  and  associated.  Immediate  actions  include
     reading  and  sending analog and digital values to appropriate UDC/ICS
     functional devices.  You may also link associated actions to specified
     events  within  the  UDC/ICS  (counters  overflowing,  switches  being
     thrown, etc.).  The associated actions can do the following:

          1.  Run a specified task when the event occurs.

          2.  Set the Event Flag when the event occurs.

          3.  DERAIL a specified task when the event occurs.

     The number of associated requests that can be  pending  simultaneously
     is  established  when you generate an RTS/8 system.  (See Chapter 2 of
     the RTS/8 System Generation Manual for more information.)         ______________________________

     The UDC/ICS Handler permits the following operations:

           1.  Analog Input        - accepts input from analog subchannel

           2.  Analog Output       - sends a 10-bit value to an analog
                                     channel

           3. Change of State      - finds the current Change-of-State
                                     value for a contact channel

           4. Digital Input        - reads a digital signal

           5. Digital Output       - sends a 12-bit value to a digital
                                     channel

           6. Disable Contacts     - ignores interrupts from a contact
                                     channel

           7. Disable Counter      - disables interrupts from a counter
                                     channel

           8. Enable Contacts      - permits interrupts from a contact
                                     channel

           9. Enable Counter       - permits interrupts from a counter
                                     channel

           10. Get Generic Code    - determines the generic code for a
                                     specified channel

           11. Read Counter        - reads the channel value of the counter
                                     channel




                                     4-46

                             RTS/8 SYSTEM TASKS


     Each of these operations  is  discussed  in  the  following  sections,
     including the format of the message for specifying the operation.  The
     RTS/8 Executive uses the first three words of a message;   the  fourth
     word  specifies  one  of the eleven UDC/ICS operations listed in Table
     4-7.

                                   Table 4-7
                               UDC/ICS Operations

                            -------------------------
                            |  UDC/ICS   |    Value |
                            |------------|----------|
                            |    AO      |       0  |
                            |    DO      |       1  |
                            |    DI      |       2  |
                            |    GC      |       3  |
                            |    EC      |       4  |
                            |    RC      |       5  |
                            |    DC      |       6  |
                            |    ECT     |       7  |
                            |    CS      |      10  |
                            |    DCT     |      11  |
                            |    AI      |      12  |
                            -------------------------

     Word 5 of a UDC/ICS message designates the channel the device uses for
     the operation;  furthermore, certain operations may also require words
     5 through 8 for their complete specification.  Word  9  specifies  the
     value  read  or  the  value returned.  Finally, word 10 of all UDC/ICS
     messages contains the error state (status).

     The general format for a UDC/ICS is:

          ZBLOCK 3
          operation
          channel
          opword 1
          opword 2
          opword 3
          value
          status

     The UDC/ICS Handler does not change the value of the  status  word  in
     some operations unless an error occurs.  Consequently, you must always
     clear this location before performing an operation.  As with all other
     handler  status  words,  you  should  check  this location after every
     operation to insure that the operation executes correctly.









                                     4-47

                             RTS/8 SYSTEM TASKS


     4.15.1  AI (Analog Input)

     ----------------------------------------------------------------------
     | Use the AI operation to accept input from an analog channel.       |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                AI                                                  |
     |                CHANNL                                              |
     |                SUBCHN & GAIN                                       |
     |                ANSWER                                              |
     |                ZBLOCK 2                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       AI        is an RTS/8 mnemonic for Analog Input.             |
     |       CHANNL    is the Analog Input Channel,                       |
     |       SUBCHN    (in bits 9-11 for UDC and 5-11  for  ICS)  is  the |
     |                 subchannel.                                        |
     |       GAIN      (in bits 1-3) is the signal amplitude.             |
     |       ANSWER    is the value to be received.                       |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     The Handler automatically sets bit 0 (enable conversion) and reads the
     control  register  (UDC  bit 8, ICS bit 4).  The ICS analog converters
     must have addresses that are less than 20 (octal) since all  converter
     modules  must be located in the first 16 slots of the ICS unit.  After
     conversion, the Handler places the digitized value in the answer word.

                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                         \_____/ \_______________________________________/
        Subchannel _________|                       |
                                                    |
        Value ______________________________________|

          Figure 4-17 UDC/ICS Handler Subchannel and Gain Word Format

     An example of a message for an input channel is:

          AIEX,   ZBLOCK 3
                  AI                 /ANALOG INPUT
                  17                 /CHANNEL 17
                  3                  /SUBCHANNEL 3, GAIN 1
          AIANS,  0                  /RESULT HERE
                  ZBLOCK 2
          AIERR, 0                   /ERROR INDICATOR

     You should ensure that for each major channel there is sufficient time
     (approximately  250 microseconds for UDC;  5 milliseconds for ICS) for
     each  subchannel  conversion  to  be  completed  before   another   is
     indicated.  In  general,  it  may be helpful if one task initiates all
     analog-to-digital conversions for a major channel.

                                     4-48

                             RTS/8 SYSTEM TASKS


     4.15.2  AO (Analog Output)

     ----------------------------------------------------------------------
     | Use an AO operation to send a 10-bit value to an analog channel.   |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                AO                                                  |
     |                CHANNL                                              |
     |                SUBCHN & VALUE                                      |
     |                ZBLOCK 3                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       AO        is an RTS/8 mnemonic for Analog Output.            |
     |       CHANNL    is the Analog Output channel.                      |
     |       SUBCHN    (bits 0-1) is the subchannel.                      |
     |       VALUE     (bits 2-11) is the value to be transmitted.        |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     The Analog Output operation  takes  a  value  which  you  specify  and
     transforms  it  into  a  form acceptable to an analog device.  It then
     writes this value, whose range is from 0 to 1023, to  the  appropriate
     subchannel.

     The format of the subchannel and value word is shown in Figure 4-18.

                        ---------------------------------------------------
                        | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
                        ---------------------------------------------------
                          ^  \_________/  ^  \___________________________/
                          |__     |       |               |
        Enable conversion __|     |       |               |
                                  |       |               |
        Gain _____________________|       |               |
                                          |               |
        ICS read control register; _______|               |
        (for UDC, bit 8)                                  |
                                                          |
        ICS subchannel; __________________________________|
        (for UDC, bits 9-11)

         Figure 4-18  UDC/ICS Handler Subchannel and Value Word Format

     Example:

          AOEX,   ZBLOCK 3
                  AO                /ANALOG OUTPUT
                  23                /CHANNEL 23
                  4614              /SUBCHANNEL 2, VALUE 614
                  ZBLOCK 3
          AOERR,  0                 /ERROR INDICATOR



                                     4-49

                             RTS/8 SYSTEM TASKS


     4.15.3  CS (Change of State)

     ----------------------------------------------------------------------
     | Use a CS operation to find the current change of state value for a |
     | contact channel.                                                   |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                CS                                                  |
     |                CHANNL                                              |
     |                RESULT                                              |
     |                ZBLOCK 3                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       CS        is an RTS/8 mnemonic for Change of State.          |
     |       CHANNL    is the contact channel  whose  current  change  of |
     |                 state value is to be placed in RESULT.             |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     You use the CS operation to discover if the  "state"  (defined  to  be
     either a logical 0 or 1) of a peripheral device changes.  If the state
     changes, then the device is performing a different operation  than  it
     performed  previously.   Note  that  a  user  task  must keep track of
     previous states.

     The function of this operation is to mask those bits that differ  from
     their  previous  state  during a given interrupt.  Because the handler
     does this operation, you need not  perform  an  exclusive  OR  at  the
     interrupt level.

     Example:

          COSEX,  ZBLOCK 3
                  CS                  /READ COS
                  1                   /CHANNEL 1
          COSANS, 0                   /RESULT HERE
                  ZBLOCK 3
          COSERR, 0                   /ERROR INDICATOR
















                                     4-50

                             RTS/8 SYSTEM TASKS


     4.15.4  DI (Digital Input)

     ----------------------------------------------------------------------
     | Use a DI operation to read a digital signal.                       |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                DI                                                  |
     |                CHANNL                                              |
     |                RESULT                                              |
     |                ZBLOCK 3                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       DI        an RTS/8 mnemonic for Digital Input.               |
     |       CHANNL    is the legal digital input channel.                |
     |       RESULT    contains the value of the channel when read.       |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     The DI operation allows  you  to  receive  a  digital  signal  from  a
     peripheral  device  and  to  store  it into a location in memory.  The
     Handler reads this number, which may be  either  signed  or  unsigned,
     from  the indicated channel and places it in the sixth block of the DI
     message.

     Example:

          DIEX,   ZBLOCK 3
                  DI                /DIGITAL INPUT
                  27                /CHANNEL 27
          DIANS,  0                 /VALUE OF CHANNEL 27 WILL BE HERE
                  ZBLOCK 3
          DIERR,  0                 /ERROR INDICATOR


     4.15.5  DO (Digital Output)

     ----------------------------------------------------------------------
     | Use a DO operation to send a 12-bit value to a digital channel.    |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                DO                                                  |
     |                CHANNL                                              |
     |                VALUE                                               |
     |                ZBLOCK 3                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       DO        is an RTS/8 mnemonic for Digital Output.           |
     |       CHANNL    is a legal digital output channel.                 |
     |       VALUE     is the number to be written.                       |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

                                     4-51

                             RTS/8 SYSTEM TASKS


     The Digital Output operation allows you to send a computed  or  stored
     value  to  a  digital  peripheral  device.   This number may be either
     signed or unsigned.  As not all digital devices  can  receive  a  full
     12-bit word, you must ensure that the value transmitted is appropriate
     for the device.

     Example:

          DOEX,   ZBLOCK 3
                  DO                 /DIGITAL OUTPUT
                  20                 /CHANNEL 20
                  7777               /VALUE = 7777
                  ZBLOCK 3
          DOERR,  0                  /ERROR INDICATOR


     4.15.6  DCT (Disable Contacts)

     ----------------------------------------------------------------------
     | Use a DCT operation to ignore interrupts from a contact channel.   |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                DCT                                                 |
     |                BIT & CHANNL                                        |
     |                ZBLOCK 4                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       DCT       in an RTS/8 mnemonic for Disable Contacts.         |
     |       BIT       (bits 0-3, value 0-13 octal) specifies the bit  on |
     |                 the   contact   channel   from  which  to  disable |
     |                 interrupts.                                        |
     |       CHANNL    (bits 4-11) is the contact channel.                |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     The DCT operation disables interrupts from a contact channel.  Because
     many  analog  devices  transmit  a  continuous stream of values, these
     values can easily fill up system queues and values may be lost.

     If you use this operation in conjunction with the Clock  Handler,  you
     may  schedule  periodic  intervals  in  which you will receive (or not
     receive) information from the channel.

     Example:

          DCTEX,  ZBLOCK 3
                  DCT                /DISABLE CONTACTS
                  5401               /FROM CHANNEL 1, BIT 13 (OCTAL)
                  ZBLOCK 4
          DCTERR, 0                  /ERROR INDICATOR




                                     4-52

                             RTS/8 SYSTEM TASKS


     4.15.7  DC (Disable Counter)

     ----------------------------------------------------------------------
     | Use a DC operation to disable interrupts from a counter channel.   |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                DC                                                  |
     |                CHANNL                                              |
     |                ZBLOCK 4                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       DC        is an RTS/8 mnemonic for Disable Channel.          |
     |       CHANNL    is the counter channel from which the  Handler  is |
     |                 to ignore interrupts.                              |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     You use the DC operation  to  prevent  the  processor  from  receiving
     interrupts  from  a  counter device.  Since a counter device may often
     send more interrupts than the  handler  can  service,  this  operation
     disables  the  interrupts so that it can properly service a portion of
     them.

     Example:

          DCEX,   ZBLOCK 3
                  DC                 /DISABLE COUNTER
                  6                  /CHANNEL 6
                  ZBLOCK 4
          DCERR,  0                  /ERROR INDICATOR
























                                     4-53

                             RTS/8 SYSTEM TASKS


     4.15.8  ECT (Enable Contacts)

     ----------------------------------------------------------------------
     | Use an ECT operation to permit interrupts from a contact channel.  |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                ECT                                                 |
     |                BIT & CHANNL                                        |
     |                ACTION                                              |
     |                ADDR                                                |
     |                ZBLOCK 4                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       ECT       is an RTS/8 mnemonic for Enable Contacts.          |
     |       BIT       (bits 0-3, value 0-13 octal) is the contact bit.   |
     |       CHANNL    (bits 4-11) is the contact channel from  which  to |
     |                 enable interrupts.                                 |
     |       ACTION    specifies what happens when the interrupt occurs.  |
     |       ADDR      is an optional address of the task  that  services |
     |                 the interrupt.                                     |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     This operation specifies the action that the computer takes  after  an
     interrupt  from  a  contact  channel  occurs.   You  must specify this
     operation before the handler ever receives an interrupt  and  after  a
     Disable Contact operation if you wish to process additional interrupts.

     Because the channel has twelve contacts, the handler  requires  twelve
     messages to enable the entire channel.

     ACTION  and  ADDR  specify  what  happens  when  the  contact  channel
     interrupts.   You  can indicate three mutually exclusive possibilities
     by setting the appropriate bit in the event ACTION word as follows:

          Bit 0 = 1  -   Set  Event  Wait  Flag  of  this  job;    continue
                         execution  of this job when the event occurs.  The
                         Handler does not use the address word.

          Bit 1 = 1  -   Run a  task  that  sent  the  message;   run  task
                         specified by bits 4-11 of event ACTION word.

          Bit 2 = 1  -   DERAIL  the  task  that  sent  the  message;   the
                         address  is  used only by the DERAIL operation and
                         specifies the address of  the  DERAIL  subroutine.
                         The  subroutine  must  be in the same field as the
                         calling task.

          Bit 3 = 1  -   Do action just once.  If bit 3 =  0,  the  Handler
                         performs  the  action after each interrupt.  Bit 3
                         indicates whether the action is to occur  once  or
                         repeatedly.


                                     4-54

                             RTS/8 SYSTEM TASKS


     Examples:

          ECTEX1, ZBLOCK 3
                  ECT                /ENABLE CONTACTS
                  5401               /FROM BIT 13 (OCTAL) OF CHANNEL 1
                  2013               /RUN TASK 13 AFTER AN EVENT OCCURS
                  ZBLOCK 3
          ECTER1, 0                  /ERROR INDICATOR
          ECTEX2, ZBLOCK 3
                  ECT                /ENABLE CONTACT
                  1001               /FROM BIT 2 OF CHANNEL 1
                  4000               /ON 1ST OCCURRENCE OF EVENT, POST
                                     /   THE EVENT FLAG
                  ZBLOCK 3
          ECTER2, 0                  /ERROR INDICATOR


     4.15.9  EC (Enable Counter)

     ----------------------------------------------------------------------
     | Use an EC operation to permit interrupts from a counter channel.   |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                EC                                                  |
     |                CHANNL                                              |
     |                INIT                                                |
     |                RELOAD                                              |
     |                ACTION                                              |
     |                ADDR                                                |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       EC        is an RTS/8 mnemonic for Enable Counter.           |
     |       CHANNL    is the counter channel to be enabled.              |
     |       INIT      is the  initial  value  to  be  loaded  into  that |
     |                 channel.                                           |
     |       RELOAD    is the value with  which  to  reload  the  channel |
     |                 after every event.                                 |
     |       ACTION    specifies what action to take after the  interrupt |
     |                 occurs (see Enable Contact for explanation).       |
     |       ADDR      is the address of a DERAIL subroutine.             |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     The EC operation specifies the action  that  the  computer  will  take
     after  an  interrupt  from a counter channel occurs.  You must specify
     this operation before the handler receives any interrupts and after  a
     Disable Counter operation if you wish to process additional interrupts.

     Examples:





                                     4-55

                             RTS/8 SYSTEM TASKS


          EXEX1,  ZBLOCK 3
                  EC                 /ENABLE COUNTER
                  4                  /CHANNEL 4
                  7700               /INITIAL VALUE OF 7700
                  7710               /RESET TO 7710 AFTER EACH EVENT
                  4000               /POST EVENT FLAG ON EVENT EVERY TIME
                                     /   IT OCCURS
                  ZBLOCK 1
          ECERR1, 0                  /ERROR INDICATOR

          ECEX2,  ZBLOCK 3
                  EC                 /ENABLE COUNTER
                  4                  /CHANNEL 4
                  1205               /INITIAL VALUE OF 1205
                  0                  /DON'T RESET
                  2016               /RUN TASK 16 ON EVENT EVERY TIME IT
                                     /   OCCURS
                  ZBLOCK 1
          EXERR2, 0                  /ERROR INDICATOR

          EXEC3,  ZBLOCK 3
                  EC                 /ENABLE COUNTER
                  4                  /CHANNEL 4
                  10                 /INITIAL VALUE OF 10
                  7700               /RESET TO 7700
                  1015               /DERAIL TO TASK 15 EVERY TIME IT
                  5620               / OCCURS AT LOCATION 5620
          ECERR3, 0                  /ERROR INDICATOR


     4.15.10  GC (Generic Code)

     ----------------------------------------------------------------------
     | Use a GC operation to determine the generic code for a specified   |
     | channel.                                                           |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                GC                                                  |
     |                CHANNL                                              |
     |                RESULT                                              |
     |                ZBLOCK 3                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       GC        is an RTS/8 mnemonic for Generic Code.             |
     |       CHANNL    is the channel.                                    |
     |       RESULT    is one of the values listed in Table 4-8.          |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     The Generic Code operation classifies interrupts so that  the  handler
     can  know  how  to  process them.  This operation is similar to a skip
     chain, but the operation occurs at task level  (that  is,  during  the
     UDC/ICS task) rather than at interrupt level.

                                     4-56

                             RTS/8 SYSTEM TASKS

     You may also use this operation to insure that the correct  module  is
     attached.   For  example,  when  you  reconfigure your system, you may
     accidentally invert  a  counter  and  analog-to-digital  module.   The
     generic  code  operation  then  returns a value, in this case 4 rather
     than the expected 7.
                                   Table 4-8
                              Generic Code Values

                 -----------------------------------------------
                 | Generic Codes  |           Meaning          |
                 |   Value        |                            |
                 |----------------|----------------------------|
                 |     0          |  No interrupt              |
                 |     1          |  Controller Error          |
                 |    2,3         |  Contact Interrupt Modules |
                 |     4          |  Counter Module            |
                 |    5,6         |  Unused                    |
                 |     7          |  A/D converter             |
                 -----------------------------------------------


     4.15.11  RC (Read Counter)

     ----------------------------------------------------------------------
     | Use a RC operation to read the channel value of the counter        |
     | channel.                                                           |
     |                                                                    |
     | Message Format:                                                    |
     |                ZBLOCK 3                                            |
     |                RC                                                  |
     |                CHANNL                                              |
     |                RESULT                                              |
     |                ZBLOCK 3                                            |
     |                STATUS                                              |
     |                                                                    |
     | where:                                                             |
     |       RC        is an RTS/8 mnemonic for Read Counter.             |
     |       CHANNL    is the counter channel whose current value  is  to |
     |                 be read.                                           |
     |       RESULT    location where the value read is placed.           |
     |       STATUS    is the error status.                               |
     ----------------------------------------------------------------------

     In many operations, you set a counter to a value and then  count  down
     to zero.  When the counter reaches zero, you perform an interrupt.  In
     some cases, however, you may wish to check the value  of  the  counter
     before  it  reaches  zero  to  determine  how  far  an  operation  has
     progressed.  This is the function of the Read Counter operation.

     Example:
          RCEX,   ZBLOCK 3
                  RC                 /READ COUNTER
                  6                  /CHANNEL 6
          RCANS,  0                  /VALUE OF CHANNEL 6 PUT HERE
                  ZBLOCK 3
          RCERR,  0                  /ERROR INDICATOR

                                     4-57

                             RTS/8 SYSTEM TASKS


     4.15.12  UDC/ICS Status/Error Conditions

     To indicate error conditions, the UDC/ICS Handler places  a  value  in
     the  tenth  word  (the status word) of the task's message.  The values
     and meanings are listed in Table 4-9.


                                   Table 4-9
                               UDC/ICS Messages

     ----------------------------------------------------------------------
     |  Value  |                         Meaning                          |
     |--------------------------------------------------------------------|
     |    0    |  No error                                                |
     |         |                                                          |
     |    1    |  Illegal  generic  code  for  specified  channel  and    |
     |         |  operation                                               |
     |         |                                                          |
     |    2    |  Channel or subchannel value not valid                   |
     |         |                                                          |
     |    3    |  Illegal function code                                   |
     |         |                                                          |
     |    4    |  Not used                                                |
     |         |                                                          |
     |    5    |  UDC/ICS  control  not  responding  (power  off  or      |
     |         |  hardware error)                                         |
     ----------------------------------------------------------------------





























                                     4-58






                                   CHAPTER 5

                            MONITOR CONSOLE ROUTINE


     5.1  MCR FUNCTIONS

     The Monitor Console Routine (MCR) receives interactive commands  which
     control, inspect, and, to some extent, debug an RTS/8 system.  It also
     allows you to schedule  and  execute  tasks  at  specified  intervals,
     suspend task execution, and print system status information.

     An MCR command consists of a command word followed  by  arguments  and
     terminated  by  either a carriage return or an ESCAPE.  Only the first
     two characters of the command are significant,  except  for  the  EXIT
     command, for which you must enter all four letters.

     Commands can be a maximum of 60 characters long.

     If a carriage return terminates the command line, the MCR  returns  to
     the  terminal  for  another  command  when  it finishes processing the
     current command.  If you type an ESCAPE as the final  line  character,
     the  MCR  puts  itself in a wait state when it finishes processing the
     command.

     You wake the MCR from the wait state by typing CONTROL/C (^C)  on  the
     console terminal (if the terminal is in foreground mode).

     The MCR indicates that it is active and ready to  accept  commands  by
     printing  the  prompting  character  > on the system console terminal.
     When the MCR prompts with its > and is waiting for input, only the MCR
     task  can  use  the  terminal  (subject  to  TIMEOUT  restrictions and
     emergency messages sent by the EMT task).  Therefore, if you are using
     the  terminal  for something other than an exclusive MCR terminal, you
     should type an ESCAPE in response to  the  prompting  >  to  free  the
     terminal,  and  to put MCR into a wait state.  This procedure prevents
     the MCR from tying up the terminal. '

     If the MCR terminal handler  has  been  configured  with  the  TIMEOUT
     facility  when  the system was generated, a timed out input causes the
     handler to go into the same wait state as does typing an ESCAPE.


     5.2  MCR COMMAND SYNTAX

     You must use certain syntactic constructions as arguments  to  several
     MCR commands.  The definitions of these arguments are:

          <sp> or ,      You may use a  single  comma  or  a  single  space
                         interchangeably to separate MCR arguments.

          TASK-ID        is either an octal number or a name.  If it  is  a
                         number,  it  represents the 1- to 3-digit internal
                         RTS/8 task number.  In  RTS/8,  this  number  also

                                      5-1

                           MONITOR CONSOLE ROUTINE


                         signifies the priority of the task:  the lower the
                         number, the higher the priority.  If TASK-ID is  a
                         name, the MCR looks up the first six characters in
                         its Task Name Table to locate a task number.

          TIME-OF-DAY    is of the form HH:MM:SS where HH represents  hours
                         past  midnight,  MM  represents  minutes  past the
                         hour, and SS represents seconds past the minute.

          ADDRESS        is an octal number  from  one  to  six  digits  in
                         length that represents a PDP-8 memory address.  If
                         ADDRESS is less than six digits long, the MCR pads
                         the number on the left with 0s.

          WORD           is an octal number from one to four digits long.

     5.3  MCR COMMANDS

     In the following command descriptions, the significant portion of  the
     MCR  command  word  is  printed  in  capital  letters.  If the command 
     accepts an optional argument or arguments, these arguments are  placed 
     within  square brackets ([ ]).  If there is a choice of arguments, the 
     choices are placed within parentheses and separated by an  exclamation 
     point (!).  If a command is preceded by an asterisk (*), it is present 
     only in a system with a clock.


                                   Table 5-1
                              MCR Command Summary
     ----------------------------------------------------------------------
     |     *Cancel       Cancels clock queue entries                      |
     |                                                                    |
     |     *DAte         Sets or lists current system date                |
     |                                                                    |
     |     DEposit       Places words into memory                         |
     |                                                                    |
     |     DIsable       Sets the ENBWT waitbit                           |
     |                                                                    |
     |     ENable        Clears the ENBWT waitbit                         |
     |                                                                    |
     |     EXamine       Opens a word for examination                     |
     |                                                                    |
     |     EXIT          Runs the EXIT task (if present) and exits to     |
     |                   OS/monitor                                       |
     |                                                                    |
     |     NAme          Changes the name by which a task is known to     |
     |                   system                                           |
     |                                                                    |
     |     OPen          Displays a location on the terminal              |
     |                                                                    |
     |     POst          Posts an event flag                              |
     |                                                                    |
     |     REquest       Clears a task's RUNWT bit                        |
     ----------------------------------------------------------------------
                                                (continued on next page)

                                      5-2

                           MONITOR CONSOLE ROUTINE


                               Table 5-1 (Cont.)
                              MCR Command Summary
     ----------------------------------------------------------------------
     |     STop          Sets a task's RUNWT bit                          |
     |                                                                    |
     |     SYstat        Displays system status information               |
     |                                                                    |
     |     *TIme         Sets or lists the current system time            |
     ----------------------------------------------------------------------


     5.3.1  CANCEL

     ----------------------
     |  * CAncel task-id  |
     ----------------------

     The CAncel TASK-ID command cancels any clock queue  entries  involving
     task TASK-ID.  This includes:

          1.  Entries  made  by  the  MCR  (from  previous  timed   REquest 
              commands)

          2.  Entries involving the task made by other tasks (for  example, 
              a timed derail)

          3.  Entries made by the task involving  itself  (for  example,  a 
              timed post)


                  ------------------- NOTE -------------------
                  |                                          |
                  | If the queue entry is a post, the  event |
                  | flag will not be posted and the task may |
                  | hang up forever waiting for it.          |
                  --------------------------------------------


     5.3.2  DATE

     --------------------------------------
     |  * DAte [DD-MON-YY[,TIME-OF-DAY]]  |
     --------------------------------------

     The date, DD-MON-YY, if you  specify  it,  becomes  the  system  date.  
     RTS/8  automatically increments the system date at midnight.  However, 
     it also assumes that all months have 31 days.

     If you specify the second argument, it sets the system TIME-OF-DAY.

     If you do not specify an argument to this command, the MCR prints  the
     current system date on the console terminal.

     The RTS/8 date word is the same date word as the  one  used  by  OS/8.
     Consequently,  if  you  specify  the  date  with  OS/8,  you  need not 

                                      5-3

                           MONITOR CONSOLE ROUTINE


     respecify it when you are using RTS/8 unless the day changes  and  the 
     month does not have 31 days.

     Example:

          >DATE 31-JUL-78
          >DATE
          31-JUL-78


     5.3.3  DEPOSIT

     -----------------------------------------------
     |  DEposit ADDRESS,WORD1[,WORD2][,WORD3]....  |
     -----------------------------------------------

     The DEposit address command deposits its second through nth arguments.

     For example:

          >DEPOSIT 26132,7700,7200,50

     deposits 7700 into location 26132, 7200 into location 26133, and  0050
     into location 26134.

     If you have KT8-A extended memory hardware, you may specify a 6 digit
     address.

     The MCR does not allow insertions to wrap around memory.  It  prevents
     this  at  two  places:   32K  in  systems  without a KT8-A and 128K in 
     systems with a KT8-A.  For example, if you specify:

          >DE 77777 0123,4567

     the second number to be placed in memory  could  go  into  location  0
     (77777 + 1).   The  MCR  prevents  this  from occurring and prints the 
     error message BAD NUMBER.  Note, however,  that  MCR  places  0123  in 
     location 77777.

     This command (as well as all other MCR commands) can contain up to  60
     characters;  thus, all characters beyond this limit are lost.  The MCR
     prints an error message if you enter more than 60 (octal)  characters,
     but it will deposit the first 60 characters of the command.  This loss
     is not a serious problem, but you should check to see  that  the  last
     word  deposited  was  correct (because this command might deposit that
     part of a word that exceeds sixty characters).


     5.3.4  DISABLE

     ---------------------
     |  DIsable TASK-ID  |
     ---------------------
     
     The  DIsable  TASK-ID  command  disables  further  execution  of   the 

                                      5-4

                           MONITOR CONSOLE ROUTINE


     specified task by setting the ENABWT bit in the Task Flags Table entry 
     for task TASK-ID.


     5.3.5  ENABLE

     --------------------
     |  ENable TASK-ID  |
     --------------------

     The ENable TASK-ID command clears the ENABWT bit  in  the  Task  Flags
     Table  entry  for  task  TASK-ID;   this permits the task to run if no 
     other WAITBIT is set.  However, if other bits are  set,  the  task  is 
     still  not  runnable.  If the ENABWT bit is not set, this command is a 
     no-op.


     5.3.6  EXAMINE

     ------------------------------
     |  EXamine ADDRESS [,COUNT]  |
     ------------------------------

     The EXamine command is identical to the OPen command.


     5.3.7  EXIT

     ----------
     |  exit  |
     ----------

     The EXIT command causes the MCR to  terminate  RTS/8  execution (after
     pausing approximately one second for pending I/O to complete) and then
     returns control to the OS/8 monitor at location 07600.


                  ------------------- NOTE -------------------
                  |                                          |
                  | You   must   type   out   this   command |
                  | completely  or it will be interpreted as |
                  | an EXamine command.                      |
                  --------------------------------------------

     If the exit task is included in the system,  this  command  runs  that 
     task before going to location 07600.


     5.3.8  NAME

     --------------------------
     |  NAme TASK-ID,NEWNAME  |
     --------------------------

     The character string NEWNAME becomes the new name of the task and  the

                                      5-5

                           MONITOR CONSOLE ROUTINE


     old  name  of  the  task (if existing) is lost.  NEWNAME can be of any
     length, but the MCR stores only the first six characters.  If  NEWNAME 
     is  the  name  of  any  other  task, the MCR prints the BAD NAME error 
     message.


     Examples:

          >NAME 7 SUPERVISOR

     MCR gives the name SUPERV to task number 7

          >NA SUPERVISOR,EXECUTIVE

     Task number 7, which is internally known as SUPERV, is  now  known  as
     EXECUT.


     5.3.9  OPEN

     ---------------------------
     |  OPen ADDRESS [,COUNT]  |
     ---------------------------

     The OPen ADDRESS command displays the number of locations you  specify
     in  COUNT  beginning  at  ADDRESS.   The  form  in  which MCR displays
     information is:

          address/contents

     The range of locations MCR displays may cross a  field  boundary.   If 
     you do not specify count, MCR assumes it to be 1.

     The MCR prevents the address from wrapping around at two  points:  32K 
     in  systems  without  a  KT8-A and 128K for systems with a KT8-A.  For 
     example, if you type

          >OP 77775,3

     MCR will display  the  contents  of  locations  77775  through  77777.
     However, if you type:

          >OP 77775,4

     MCR displays locations 77775 through 77777 and  then  prints  the  BAD
     NUMBER error message.


     5.3.10  POST

     ------------------
     |  POst ADDRESS  |
     ------------------

     The POst ADDRESS command posts the  event  flag  at  the  address  you

                                      5-6

                           MONITOR CONSOLE ROUTINE


     specify.  This command is useful when you are debugging a system since
     it can simulate the effects of nonexistent tasks or devices.

                  ------------------- NOTE -------------------
                  |                                          |
                  | You should be careful in the way you use |
                  | this  command  because  these  simulated |
                  | postings indicate actions which  do  not |
                  | occur.                                   |
                  --------------------------------------------


     5.3.11  REQUEST

     -------------------------------------------------------------
     |  REquest TASK-ID[,(@TIME-OF-DAY ! INTERVAL)[,INTERVAL] ]  |
     -------------------------------------------------------------

     The REquest TASK-ID command requests a task to run:

          o  Immediately (if you specify only TASK-ID),

          o  At a given TIME-OF-DAY,

          o  After a given INTERVAL, or

          o  At a given INTERVAL.

     INTERVAL is of the form:

          nH    n hours 
          nM    n minutes 
          nS    n seconds
          nT    n system ticks

     Requesting a task clears the RUNWT bit in the task's Task Flags  Table
     entry.  (This command is equivalent to the RUN Executive Request.) The
     interval, given as the third argument, specifies the period  at  which
     the  task  is to be rerun.  If you do not have a clock in your system, 
     the  MCR  ignores  any  timing  arguments  and   executes   the   task 
     immediately.

     The following examples illustrate  three  different  formats  for  the
     REquest  command;   note,  however, that only the first two characters 
     are significant.

     Examples:

          >REQUEST X 

     runs task X immediately. 

          >RE NEW,@2:00



                                      5-7

                           MONITOR CONSOLE ROUTINE


     runs task NEW at 2:00 am (if it is after 2 am, NEW runs tomorrow at  2
     am)

          >RE 5,10M,5M

     runs task 5 ten minutes from now, and every five minutes thereafter.

          >REQ HIPR,1T,6T

     On a machine with a 60 Hz clock,  this  command  runs  the  task  HIPR
     immediately  (that  is, .016 seconds from now, and 10 times per second
     thereafter).


                  ------------------- NOTE -------------------
                  |                                          |
                  | If, at the time  the  MCR  executes  the |
                  | REquest  command  (which  may be several |
                  | hours after you enter it), the task does |
                  | not  have  the RUNWT bit set in its Task |
                  | Flags  Table  entry,  then  the  REquest |
                  | command   is  a  no-op  (no-operation).  | 
                  |                                          |
                  | Similarly, the task will  not  run  upon |
                  | execution  of  the REquest command if it |
                  | has other  WAITBITS  set  beside  RUNWT; |
                  | the   task  runs  only  when  the  other |
                  | blocking bits are cleared.               |
                  --------------------------------------------


     5.3.12  STOP

     ------------------
     |  STop TASK-ID  |
     ------------------

     The STop TASK-ID command suspends execution of the task you specify by 
     turning  on the RUNWT bit in the Task Flags Table entry for that task.  
     (This is identical to the SUSPND ER.) You may restart a task  that  is 
     stopped  by  using  the REquest MCR command.  (In this instance, it is 
     easier to think of the command as a REsume MCR command.)


     5.3.13  SYSTAT

     ----------------------
     |  SYstat [TASK-ID]  |
     ----------------------

     The SYstat command, depending on  whether  you  specify  an  argument,
     prints either a general system status report or a more detailed status
     report on a single task.  If you do not type an argument,  the  SYstat
     command  prints  a  system  status  report.   Each  line of the report
     describes a task in the  system.   For  each  task,  furthermore,  the

                                      5-8

                           MONITOR CONSOLE ROUTINE


     report prints the task number/priority, task name (if it has one), and
     which blocking bits are set in the Task Flags Table  entry.   The  MCR
     prints  each blocking bit as a 1-letter code, preceded by a space.  If
     more than one blocking bit is set, the MCR prints one letter for  each
     bit.  The 1-letter codes and their meanings are:

          D     Disabled

          E     Waiting for event flag

          M     Waiting for a message

          N     Nonresident Wait

          O     Waiting for an event flag or a message

          R     Waiting to be REquested or RUN

          S     Waiting to be swapped in

          U     USERWT bit set

          X     Task does not exist

     In addition, an asterisk (*) printed at the end of the line means  the
     task has messages waiting in its input queue.

     You obtain more detailed information about a task  by  specifying  the
     TASK-ID  as  an argument to the command.  The detailed report contains
     all the information in the general status report, followed  by  either
     five or six octal words:

          WORD 1    The location of the Task State Table  entry  containing
                    words 2-5;  this word is followed by a colon.

          WORD 2    Without KT8-A:
                       Task Link in sign bit,  Instruction  Field  in  bits 
                       6-8,  Data field in bits 9-11 (PDP-8/E and 8/A Flags
                       register)

                    With KT8-A:
                       Task Link in sign bit, the high-order  bits  of  the
                       Instruction  Field  in  bits 1 and 2, the high-order
                       bits of the Data Field in bits 3  and  4,  the  user 
                       mode in bit 5, the low-order bits of the Instruction 
                       Field in bits 6 through 8, and the low-order bits of 
                       the Data Field in bits 9 through 11.

          WORD 3    Task PC

          WORD 4    Task AC

          WORD 5    Task MQ



                                      5-9

                           MONITOR CONSOLE ROUTINE


          WORD 6    Task EAE.  The MCR prints this word only if the system 
                    has EAE hardware and RTS/8 saves the EAE registers.

                    With KT8-A:
                       This word is the Step Count + 4000 (if the system is 
                       in  B  mode)  + 2000 (if the GTF flag is set).  Note
                       that not all machines have a B mode.

                    Without KT8-A:
                       This word is the Step Count + 4000 (if the system is
                       in B mode).

     Examples:

     A general SYSTAT command might produce  the  following  sample  output
     line:

          13 CARD E S *

     This line means task number 13, named CARD, is in Event Flag Wait,  is
     waiting  to  be  swapped  into memory, and has input messages pending.  
     The command

          >SYSTAT CARD

     might produce the single line:

          13 CARD E S * 1320: 0021 1741 0000 2525

     This line indicates, in addition to the information specified  in  the
     general SYSTAT command, that task CARD is stopped at location 21741 in
     data field 1, with its accumulator and Link set at zero, and  2525  in
     its MQ.


     5.3.14  TIME

     --------------------------
     |  * TIme [TIME-OF-DAY]  |
     --------------------------

     If you specify a TIME command, the argument to  this  command  becomes 
     the  system  TIME-OF-DAY.   If  you  enter  this  command  without  an 
     argument, the MCR prints the current system TIME-OF-DAY  in  the  form 
     hh:mm:ss.

     Example:

          >TIME 14:00
          >TIME
          14:00:04


     5.3.15  MCR Errors


                                      5-10

                           MONITOR CONSOLE ROUTINE


     The MCR checks each command line for errors  and,  if  it  finds  one,
     issues  one  of  the following messages.  It will then reprompt on the
     terminal for the corrected command.

     ----------------------------------------------------------------------
     |     Error      |                                                   |
     |    Message     |                    Meaning                        |
     |----------------|---------------------------------------------------|
     |   BAD CHAR     |  Character was not expected where it occurred     |
     |                |                                                   |
     |   BAD NUMBER   |  Number is out of legal range or is missing       |
     |                |                                                   |
     |   BAD DELIM    |  No space or comma where one was expected         |
     |                |                                                   |
     |   BAD NAME     |  Task name is not in name table or is a duplicate |
     ----------------------------------------------------------------------








































                                      5-11






                                   CHAPTER 6

                               NONRESIDENT TASKS


     6.1  NONRESIDENT TASK DESCRIPTION

     A nonresident task is a task or a portion of a task that resides on  a
     mass  storage  device  during the time the task is not runnable.  (The
     mass storage device is called the swap device.) It  can  be  any  mass
     storage  medium;   for example, an RL01 disk or a floppy disk.  When a
     nonresident task becomes executable, the Executive posts  a  residency
     request,  and  then  runs a special swapper task.  This task loads the
     nonresident portion of the task into memory.  (The loading process  is
     called  a  "swap.")  The  memory  area  into which or out of which the
     Executive swaps  the  nonresident  task  is  called  a  partition.   A
     partition  is simply a contiguous block of memory that a task uses for
     its execution;  the partition is readable in  a  single  mass  storage
     call.

     The use of nonresident tasks permits several tasks to share  the  same
     areas of memory, thereby optimizing the use of available memory.

     Tasks can be either totally or partially  nonresident.  However,  very
     few   tasks  are  totally  nonresident;   in  most  applications,  the
     nonresident portion  includes  all,  or  nearly  all,  of  the  active
     locations.   (Active  locations  are  those  that  contain  executable
     instructions or data that other tasks do  not  access.)  The  resident
     portion  (called  the root segment) of a task includes messages, event
     flags, buffers, and similar passive registers  that  other  tasks  may
     need.

     Note that the process that swaps the nonresident  portion  of  a  task
     into memory is similar to the overlay capability found in OS/8 FORTRAN
     IV and related programs.

     RTS/8 requires information concerning two aspects of the code.  If the
     Executive  can  interrupt  and swap the task out of memory without its
     consent, it is "checkpointable." If the task can  be  modified  during
     its  execution,  it  must  be written to the swapping device.  This is
     called "modified" code.  (Note that if the task is not modified during
     execution, it can be overwritten because all that need be saved is the
     processor state.)












                                      6-1

                              NONRESIDENT TASKS

                PDP-8 MEMORY
        -----------------------------                  SWAP DEVICE
     0K |                           |             (Disk, Floppy, etc.)
        | REAL TIME PROGRAM AREA    |                  ***********
        |                           |                *  Contains   *
        | Contains:                 |               *  nonresident  *
        |   1 Resident tasks        |               * portion of a  *
        |   2 Resident portions of  |                *    task     *
        |     non resident tasks    |                  ***********
     pK |---------------------------|                       ^
        |      PARTITION AREA       |                       |
        |                           |                       v
        | 1. Contains non resident  |            ------------------------
        |    portion of nonresident |            |    SWAPPER TASK      |
        |    task when that task is |            |    (SWAP.PA)         | 
        |    being executed         |            |                      |       
        |                           |<---------->| 1. Loads nonresident |
        | 2. Allows multiple tasks  |            | portion of task into |
        |    of same relative size  |            |    memory.           |
        |    to run in the same     |            | 2. Swaps out non-    |
        |    memory area.           |            |    resident task     |
        |                           |            |    onto Swap Device. |
        | 3. The characteristic of  |            | 3. Also loads and    |
        |    a partition is as      |            |    swaps writeable   |
        |    follows:               |            |    and checkpoint-   |
        |                           |            |    able tasks.       |
        | a) has a starting address |            ------------------------
        |                           |
        | b) Resides completely     |
        |    within a single memory |
        |    field                  |
        |                           |
        | c) Length has to be an    |
        |    integral number of     |
        |    pages                  |
        |                           |
        | d) Cannot overlap another |
        |    partition              |
     nK -----------------------------

                  Figure 6-1 Nonresident Task Implementation


     6.1.1  Checkpointable Tasks

     A task is made checkpointable if the Executive  may  swap  it  out  of
     memory  automatically,  without its consent, to make room for a higher
     priority task.  The Executive swaps back a task that  it  checkpointed
     and  swapped  out  of  memory  as  soon  as  all higher priority tasks
     relinquish processor control and  when  the  partition  is  available. 
     Execution  then continues at the point where the Executive interrupted
     it;  the task is not aware that it was interrupted.

     Checkpointing is ideally suited for  long-running  tasks  because  the
     system  can run short tasks in the same area, swap them out of memory,
     and swap the long running task back again.

                                      6-2

                              NONRESIDENT TASKS

     6.1.2  Modified Tasks

     A modifiable task is any task that is self-modifying;   that  is,  the
     task's  code  is changeable during task execution.  It must be written
     to the swapping device because the code in  memory  differs  from  the
     copy  of  the  code  on  the  swapping  device.   The modified feature
     guarantees that the nonresident portion of a task is always up to date
     by  refreshing  the  swap  device  image  of  the  nonresident portion
     whenever the Executive swaps the task out of memory.


     6.1.3  Interaction Between Tasks

     Resident tasks can interact with the root segments of any  nonresident
     task.   Also,  two  nonresident  tasks occupying the same or different
     memory regions  can  interact  with  each  other  through  their  root
     segments.   For  example,  assume that a nonresident task is executing
     and it sends a message.  Because of some  reason  unconnected  to  the
     message, the Executive checkpoints the task.  The message receiver can
     acknowledge the sender's message even though the sender is not totally
     resident.  However, the message sent must be resident.


     6.2  MEMORY PARTITIONS

     The swappable portion of  a  nonresident  task  resides  in  a  memory
     partition.    This  partition  is  simply a contiguous block of memory
     locations assigned by the LINK program.  LINK insures that a partition
     has the following characteristics:

          1.  It is wholly contained in one memory field.  (This means that 
              any nonresident task must fit into one memory field.)

          2.  It has a starting address.

          3.  It has a length (size) that must divide evenly by 200 (octal) 
              since  OS/8  directory-structured  devices  read and write in 
              one-half block (l-page) increments.

          4.  It always begins at an address which is a multiple of 400.

     Note  that  the  partitions  and  the  tasks  residing  in  them  were
     established during the System Generation.

     Partitions are mutually  distinct;   that  is,  one  partition  cannot
     overlap  another.   In  RTS/8,  you  may  have  up to 7 partitions;  a
     maximum of 16 tasks can use the same partition.   The  partitions  are
     numbered from 1 to 7. (Partition 0 contains only resident tasks.) Note
     that tasks are assigned to partitions when the system  was  generated.

     Partitions do not have to be adjacent to one another.

     Only one task can occupy a partition at any time.  The occupying  task
     owns  the  partition until the task executes a FREE command (described 
     in the next section), or (if the task is checkpointable)  as  long  as 
     higher priority tasks that share the partition remain nonexecutable.

                                      6-3

                              NONRESIDENT TASKS


     6.2.1  FREE Command

     ----------------------------------------------------------------------
     | Use a FREE ER to signal the Executive that a task  can  relinquish |
     | control of a partition.                                            |
     |                                                                    |
     | Format:                                                            |
     |        CAL                                                         |
     |        COMMND+FREE                                                 |
     |                                                                    |
     | where:                                                             |
     |       CAL       is an RTS/8 mnemonic for JMS 20.                   |
     |       COMMND    is an RTS/8 Executive Request.                     |
     |       FREE      is an Executive Request mnemonic.                  |
     ----------------------------------------------------------------------

     The FREE command states that the Executive can swap the  issuing  task
     out  of  memory if some other task becomes executable and requires the
     partition before the freeing task cancels the FREE request.

     You typically append a  FREE  request  to  the  function  argument  of
     relevant Executive Requests (for example, SEND, RECEIVE, etc.)


                  ------------------- NOTE -------------------
                  |                                          |
                  | You may place a FREE request  after  any |
                  | Executive   Request.   However,  if  the |
                  | Executive  Request  does  not  put   the |
                  | nonresident  task into a wait state, the |
                  | Executive ignores the FREE.              |
                  --------------------------------------------

     If you enter the sequence

          CAL
          FREE

     the Executive interprets it as:

          CAL
          SEND+FREE

     Only nonresident tasks may issue FREE requests;  the Executive ignores
     FREE  requests  from  permanently resident tasks.  Although a task may
     free its own partition, it can never free  the  partition  of  another
     task.

     A task normally frees its partition whenever it waits  for  an  event. 
     If  any  other  task  has  a  PENDING  request  for the partition, the
     Executive swaps it into the free partition immediately.  If  there  is
     no  PENDING  request  for the partition, the freeing task continues to
     wait in the free partition until some other task requests residency of
     the  same  partition.   In  either case, once the freeing task becomes
     executable again, it must compete for the  partition  along  with  any

                                      6-4

                              NONRESIDENT TASKS


     other executable occupants.

     The freeing task may become executable before  another  task  requests
     residency in the partition.  If this occurs, the Executive cancels the
     FREE  request,  and  the  freeing  task  retains  possession  of   the
     partition.  No read or write operation is necessary to effect the swap
     in this case.  By freeing the partition whenever  the  occupying  task
     (which  may  or  may  not be modified) must wait for an event, you are
     assured that the partition contains a  running  (i.e.,  a  nonwaiting)
     task  whenever  possible.   If  there  are  no  modified  tasks in the
     partition, no swap device I/O is involved in freeing the partition.


     6.2.2  Writing Nonresident Tasks

     A nonresident task must be written with the following  conventions  so
     that it links and initializes correctly.

          1.  No SECT may contain both resident and nonresident code.

          2.  SECTs of the root segment (if any) must  contain  LEVEL=0  in 
              their SECT definition to define the resident portion.

          3.  Although you may include a LEVEL parameter in the nonresident 
              SECT,  DIGITAL  strongly  advises  you  not to do so unless a 
              special need justifies its inclusion.

          4.  One SECT of every task must include  a  .NONRES  macro.   The 
              format  of  this  macro, included in the RTS/8 system when it 
              was generated, is

                   NONRES CHECKPOINTABLE[,WRITEABLE]

              where CHECKPOINTABLE is a 0 or 1 value  with  0  meaning  the 
              task is not checkpointable and 1 meaning it is.  WRITEABLE is 
              an optional argument which also may have a 0 or 1 value.   If 
              this value equals zero, then the task is not writeable.

              If you inadvertently include more than one .NONRES  macro  in 
              an RTS/8 task, MACREL prints an error message.  If this error 
              occurs, you must eliminate .NONRES from  one  of  the  SECTs.  
              You  then  resubmit  the RTS/8 system generation MACREL batch 
              file.

          5.  Normally,  you  do  not  include  FIELD   statements   in   a 
              nonresident  SECT.   Note,  however, that because the message 
              pointer in an RTS/8 Executive Request CAL  must  point  to  a 
              location  in  the same field as the CAL, the nonresident SECT 
              of a task must reside in the same field as the resident SECT.  
              In  this  case,  and  only in this case where the nonresident 
              SECT uses  an  Executive  Request  to  communicate  with  the 
              resident  SECT,  should  you include a FIELD statement in the
              nonresident SECT.  In all  other  cases,  you  should  create 
              field-independent SECTs.


                                      6-5

                              NONRESIDENT TASKS


     You may find it convenient to debug a nonresident task as  a  resident
     task.  If you do this, you should build an RTS/8 system with a swapper
     task.  (This means that you include the DIGITAL swap task in the RTS/8
     system  even  though you may not have any nonresident tasks.) However,
     do not assign your user- task to a partition.  Your task will then  be
     fully  resident. When the task is debugged, you may either rebuild the
     entire system or modify the linker command  string  (included  in  the
     LINK  BATCH  file  produced by the RTS/8 System Generation) to include
     your task in an overlay.  Also, the swap device must be on the  system
     device when you run RTS/8 from OS/8.


                  ------------------- NOTE -------------------
                  |                                          |
                  | The  operations  that  LINK   views   as |
                  | overlays  are converted to partitions by |
                  | the swapper initialization code.         |
                  --------------------------------------------

     The save image of the RTS/8 system contains the initial image  of  the
     nonresident tasks.  In order for LINK to correctly pass information to
     RTS/8, this save image must be run from SYS:. As the RTS/8  system  is
     executed,  modifiable  tasks  cannot be written back over the original
     image.  The /X switch (provided at link time), causes LINK to allocate
     additional  space  in the save image.  This space contains the working
     image of the nonresident task.  Consequently, you  can  run  the  same
     image more than once.  These procedures are transparent to the user.





























                                      6-6






				   Chapter 7

			    PROGRAMMING TECHNIQUES


     7.1  OVERVIEW

     This chapter describes several aspects of writing  tasks  under  RTS/8
     that  rely  heavily  on the user understanding the nature of the RTS/8
     system.  You should only use the techniques described in the following
     sections  after  you  become familiar with RTS/8.  The topics discused
     are:

	  1.  Writing tasks where more than one task shares the information
	      in some locations.

	  2.  Writing tasks that must wait for more than one event flag.

	  3.  Writing tasks that modify system tables.

	  4.  Programming the KL8A.


     7.2  PERFORMING A RESCHUDLE


     7.2.1  Writing Delicate Code

     Frequently, a task needs to manipulate data  in  another  task  or  in
     shared  locations.   Since  tasks  are  running concurrently, problems
     arise if two tasks want to access the same  data  at  the  same  time.
     Consequently, delicate code should run with interrupts disabled when a
     task accesses data which another task can also  access.   You  disable
     the interrupts so that task switching does not occur.


		  ------------------- NOTE -------------------
		  |					     |
		  | You may disable  interrupts  temporarily |
		  | using  either  an  IOF/ION  pair  or, on |
		  | machines with memory management,  a  CIF |
		  | instruction  (which  inhibits interrupts |
		  | until the execution of the next  JMP  or |
		  | JMS instruction).			     |
		  --------------------------------------------

     For example, suppose Task A increments location COUNT occasionally and
     Task B decrements location COUNT from time to time  during  execution.
     The code might look like the following:






				      7-1

			    PROGRAMMING TECHNIQUES


     /		     TASK A

     LOOPA,  .
	     .
	     .
     X,	     ISZ COUNT
	     .
	     .
	     .
	     JMP LOOPA
     COUNT,  0

     /		     TASK B

     LOOPB,  .
	     .
	     .
	     STA
     Y,      TAD COUNT
     Z,      DCA COUNT
	     .
	     .
	     .
	     JMP LOOPB

     If Task A increments COUNT the  same  number  of  times  that  Task  B
     decrements COUNT, you might assume that COUNT would be 0 at the end of
     the program.  However,  this  is  not  necessarily  so  since  a  race
     condition can occur.

     Suppose that Task A has a higher priority than Task B, and Task  A  is
     waiting  for  an  event  to occur with COUNT currently containing a 6.
     Task B is ready to decrement  COUNT.   However,  an  interrupt  occurs
     after the processor executes location Y.  The accumulator contains a 5
     and Task B is ready to store a  5  back  into  COUNT.   The  interrupt
     service  routine,  noting  that the event for which Task A was waiting
     has just occurred, now suspends Task B and resumes Task A.  Task A now
     bumps  COUNT  from  6  to 7, and then goes back to sleep.  Task B then
     resumes with the accumulator containing a 5 and stores a 5 into  COUNT
     which is incorrect for proper program execution.

     You can prevent this situation from arising  by  disabling  interrupts
     around  the  delicate code.  Either of the following two solutions are
     workable:

     Solution 2 (only  usable  on  machines  with  memory  extension)  uses
     the CIF instruction since it temporarily inhibits interrupts until the
     processor executes the next JMP or JMS instruction.

		  SOLUTION 1			    SOLUTION 2

	       /TASK B				 /TASK B
	       LOOPB,  .			 LOOPB,  .
		       .				 .
		       .				 .

				      7-2

			    PROGRAMMING TECHNIQUES

		       .				 .
		       STA				 STA
		       IOF				 CIF .FLD
	       Y,      TAD COUNT		 Y,      TAD COUNT
	       Z,      DCA COUNT		 Z,      DCA COUNT
		       ION				 .
		       .				 .
		       .				 .
		       .				 .
		       JMP LOOPB			 JMP LOOPB


     7.2.2  Inhibiting Task Switching

     Although you can use the procedures in the previous section, they  can
     be  very inefficient.  If the processor performs a considerable amount
     of  manipulation  on  data  accessible  by  other  tasks,  it  may  be
     inappropriate  to turn off interrupts. Moreover, inhibiting interrupts
     for long periods of time could affect other  portions  of  the  system
     where timed events are very important.  Also, an interrupt can be lost
     (for example, clock interrupts) if the processor turns off  interrupts
     for a substantial amount of time.

     For this case, another solution is possible.  A task  can  inform  the
     RTS/8  Executive that it wants to run, and that while it is executing,
     no other task should run even if a task  of  higher  priority  becomes
     runnable.  This process is known as inhibiting task switching.

     You should inhibit task switching only under unusual circumstances and
     perform  this  action  with  care.  While task switching is inhibited,
     interrupts may still occur and an interrupt service routine  will  get
     control.   Note  that  if  you  inhibit  task switching, the interrupt
     service routine always returns control to the interrupted  task  after
     the task services the interrupt, even if higher priority tasks are now
     runnable.


		  ------------------- NOTE -------------------
		  |					     |
		  | If you wish to manipulate data which  is |
		  | accessible    by    an   interrupt-level |
		  | routine, interrupts  must  be  inhibited |
		  | since  inhibiting  task  switching alone |
		  | will not be sufficient in this case.     |
		  --------------------------------------------

     There are two methods of inhibiting task switching:

	  1.  Task switching is automatically inhibited whenever  a  task's
	      program  counter  is  less  than  100.  Thus,  you  may place
	      delicate code in the bottom of page 0  of  any  field  except
	      field 0.





				      7-3

			    PROGRAMMING TECHNIQUES


		  ------------------- NOTE -------------------
		  |					     |
		  | You  should  not  use  locations   20-27 |
		  | because   the   RTS/8  Executive  stores |
		  | information in these locations.	     |
		  --------------------------------------------

	      Also, you should not use an ASECT in  field  0  which  places
	      information  below location 1000.  This is the area where the
	      RTS/8 Executive resides.

	  2.  A task may inhibit task switching by  zeroing  GLOBAL  TSWFLG
	      (the task switching flag).

     In either case, after the task is through with its delicate  code,  it
     may  not  be  sufficient  for the task to reset TSWFLG to its original
     value (which is  1)  because  possibly  another  higher-priority  task
     should  have  run  but  did  not  due  to  task  switching having been
     inhibited.  You can determine this by interrogating  location  TSWFLG.
     If  another  task  became runnable while task switching was inhibited,
     the RTS/8 Executive sets this flag to -1.

     When a task is ready to allow task switching again, it should  examine
     this  flag  before  resetting  it to 1.  If it was -1, the task should
     return control to the RTS/8 scheduler.  A task performs this by  using
     the RESCHD Executive Request as follows:

	  CAL
	  RESCHD

     This ER causes RTS/8 to perform a reschedule that allows the  runnable
     task  of  highest  priority  to  be executed.  If you do not perform a
     RESCHD after re-enabling task switching, then a higher  priority  task
     that is entitled to run might not run until the next interrupt occurs.
     However, the interrupt may never occur or, if it does, it may  be  too
     late for proper program execution.

     The preferred code for inhibiting task switching for Task B (which was
     described previously) is:

     /		     TASK B

     LOOPB,  .
	     .
	     .
	     CLA
	     CDF TSWFLG
	     DCA I (TSWFLG)	     /INHIBIT TASK SWITCHING
	     STA
     Y,      TAD COUNT
     Z,      DCA COUNT
	     ISZ I (TSWFLG)
	     JMP .+3		     /SHOULD WE RESCHEDULE
	     CAL		     /YES
	     RESCHD

				      7-4

			    PROGRAMMING TECHNIQUES


	     CDF .FLD		     /NO
	     .
	     .
	     .
	     JMP LOOPB


		  ------------------- NOTE -------------------
		  |					     |
		  | Interrupt level routines should not look |
		  | at or set the TSWFLG.		     |
		  --------------------------------------------

     A summary of TSWFLG states is shown in Table 7-1.


				   Table 7-1
		       Task Switch Flag (TSWFLG) States

	       ---------------------------------------------------
	       |	   TSWFLG State		    |   Value    |
	       |-------------------------------------------------|
	       | Task switching allowed		    |	  1	 |
	       |				    |		 |
	       | Task switching inhibited	    |	  0	 |
	       |				    |		 |
	       | Task switching inhibited;	    |	  -1	 |
	       | reschedule as soon as possible	    |		 |
	       ---------------------------------------------------


     7.3  MULTIPLE EVENT FLAG WAITS

     Occasionally  you  may  find  it  desirable  to  wait  for  a  logical
     combination  (AND  or OR) of event flags.  Waiting for the logical AND
     of two event flags is quite simple.  The sequence

	  CAL
	  WAITE		 /WAIT FOR EVENT FLAG A
	  A
	  CAL
	  WAITE		 /WAIT FOR EVENT FLAG B
	  B

     waits until both A and B have been posted.

     Waiting for the logical OR of several event flags  is  more  difficult
     since there is a possible race condition between the various tests and
     the  interrupts  (or  task  executions)  that  post  the  event  flags
     involved.   The key to waiting successfully for an OR of several event
     flags is not to allow any interrupts to occur between the  testing  of
     the  first  event  flag and the placing of the task in a wait state if
     none of the flags were posted.

     You accomplish this by using a special sequence of instructions and  a

				      7-5

			    PROGRAMMING TECHNIQUES


     special  RTS/8  call  named  WAITM (defined as JMS I 25).  A task must
     execute this instruction with interrupts off,  the  instruction  field
     set  to  0,  and  the  data field set to the current field.  Also, the
     instruction must be followed by a word containing the blocking  bit(s)
     to be set in the Task Flags Table.

     The action of WAITM is equivalent to  that  of  the  RTS/8  BLKARG  ER
     except  that  a  fast  path  through  the RTS/8 Executive is taken and
     interrupts remain off until the blocking bits are on in the Task Flags
     Table.

     As an example of the use of WAITM, assume that a task  TASK  wants  to
     test  two  event flags, A and B.  If A is posted, control should go to
     location ADONE;  if B is posted, control should go to location BDONE.

     If neither is posted, the task must wait until one of them is  posted.
     The code to perform this function is:

	  TESTAB,    IOF	     /INTERRUPTS OFF--DELICATE CODE
		     TAD A
		     SNA CLA
		     JMP ADONE	     /ADONE MUST TURN INTERRUPTS ON
		     TAD (4000+TASK) /SET A TO "WAITING" STATE INDICATING
				     / THAT THIS TASK IS WAITING ON IT
		     DCA A
		     TAD B
		     SNA CLA
		     JMP BDONE       /BDONE MUST TURN INTERRUPTS ON

		     TAD (4000+TASK) /SET B TO "WAITING" STATE INDICATING
				     / THAT THIS TASK IS WAITING ON IT
		     DCA B
		     CIF RTS8        /RTS8 IS THE FIELD OF RTS8 EXECUTIVE
		     CDF .FLD
		     WAITM
		     EFWT	     /BLOCK TASK ON EVENT FLAG WAIT
		     JMP TESTAB      /WE'RE BACK--ONE OF THE TWO EVENT
				     / FLAGS HAS BEEN POSTED.  GO
				     / BACK TO FIND OUT WHICH ONE.


     7.4  EXECUTIVE INTERNAL TASK TABLES

     The Executive uses the following  five  internal  tables  to  maintain
     information about the tasks in the system:

	       Table				  Description

     Task State Table (TSTABL)	     Contains  information  such   as   the
				     contents of the task's program counter
				     Link, and accumulator at the time  the
				     task stopped running.

     Task Flags Table (TFTABL)	     Contains  information  about  why  the
				     task  is  not  running;   that  is, it

				      7-6

			    PROGRAMMING TECHNIQUES


				     indicates the conditions (blocking  of
				     WAITBITS)   for   which  the  task  is
				     waiting.

     Task Input Message Queue	     Contains messages that have been  sent
     Header Table (MSGTBL)	     to  this task.  This table is referred
				     to simply as the Message Table.

     Residency Table (RESTBL)	     Used for nonresident tasks, this table
				     specifies  where the task is to reside
				     in memory and where it resides on  the
				     swap device.

     Partition Table (PARTBL)	     Used for nonresident tasks, this table
				     contains information about each memory
				     partition.   Nonresident  tasks  share
				     memory partitions.

     The Executive uses each task"s task number as an index into the  first
     four  tables  to  retrieve  and update information for that task.  The
     Executive uses the partition number as an index into the fifth table.

     You may reference a table by using its GLOBAL name.   (Note  that  all
     the tables reside in the field of the RTS/8 Executive.)


     7.4.1  Task State Table (TSTABL)

     The Task State table contains 4-word entries (five  if  the  Executive
     saves  the  EAE  registers) which hold the most recent contents of the
     CPU registers for each task as follows:

	  WORD 1  without KT8-A:
			  -link (bit 0)
			  -Greater Than Flag (bit  1)  if  flag  exists  on
			       machine
			  -User Mode Flag (bit 5) if flag exists on machine
			  -Instruction Field (bits 6-8)
			  -Data Field (bits 9-11)
		  with KT8-A:
			  -link (bit 0)
			  -high-order bits of the Instruction  Field  (bits
			       1-2)
			  -high-order bits of the Data Field (bits 3-4)
			  -user mode (bit 5)
			  -low-order bits of the  Instruction  Field  (bits
			       6-8)
			  -low-order bits of the Data Field (bits 9-11)

	  WORD 2  contains the contents of the Program Counter

	  WORD 3  contains the contents of the Accumulator

	  WORD 4  contains the contents of  the  Multiplier  Quotient  (MQ)
		  register if the system has been assembled to save the MQ.

				      7-7

			    PROGRAMMING TECHNIQUES


	  WORD 5  contains EAE information as follows:
		  -  If the  system  does  not  have  a  KT8-A,  this  word
		     contains  the Step Count + 4000 (if the system is in B
		     mode).

		  -  If the system has a KT8-A, this word contains the Step
		     Count  +  4000 (if the system is in B mode) + 2000 (if
		     the GTF flag is set).  Some machines do not have  a  B
		     mode.

     Whenever the Executive executes a task, it loads the contents  of  the
     task's  Task State Table entries into the corresponding CPU registers.
     Also, whenever a task stops executing, the  Executive  sets  its  Task
     State Table entries to the new contents of these registers.

     Example:

     Consider the following TSTABL entries for a task.

	  4012
	  3376
	  1234
	  0211

     The Executive interrupted the task just as it was about to execute the
     instruction  at  location 3376 (entry 2) of field 1 (bits 6-8 of entry
     1).  At this point, the Executive  enters  the  contents  of  the  CPU
     registers for this task in the TSTABL.  The accumulator is 1234 (entry
     3), and the MQ is 0211 (entry 4).  The link is set (bit 0 of entry  1)
     and the data field is 2 (bits 9-11 of entry 1).


     7.4.2  Task Flags Table (TFTABL)

     The Task Flags table contains a 1-word  entry  holding  various  flags
     (bits)  for  each  task.   The  Executive uses this table to determine
     whether the task is runnable.  A task is runnable  only  if  its  Task
     Flags  Table entry is zero.  Each flag (bit) which is set in a nonzero
     state indicates a reason why  the  task  cannot  run.   The  currently
     defined flags and their meanings are listed in Table 7-2.

				   Table 7-2
			     Waitbit Descriptions

     ----------------------------------------------------------------------
     | Symbolic Name  |  Value  |		 Meaning		  |
     |----------------|---------|-----------------------------------------|
     |    NONRWT      |   4000	|  Nonresident Wait--This task cannot run |
     |		      |		|  because it is not in memory.		  |
     |		      |		|					  |
     |    EFWT        |   2000	|  Event Flag Wait--This task is  waiting |
     |		      |		|  for  an  event  flag (which contains a |
     |		      |		|  WAITING value  corresponding  to  this |
     |		      |		|  task) to be POSTed.			  |
     ----------------------------------------------------------------------
					     (Continued on the next page)
				      7-8

			    PROGRAMMING TECHNIQUES


			      Table 7-2 (Cont.)
			     Waitbit Descriptions

     ----------------------------------------------------------------------
     | Symbolic Name  |  Value  |		 Meaning		  |
     |----------------|---------|-----------------------------------------|
     |    RUNWT       |   1000	|  Run Wait--This task is waiting  for  a |
     |		      |		|  RUN  ER to be executed with its number |
     |		      |		|  in the AC, or for the operator to type |
     |		      |		|  a   REQUEST  command  to  the  Monitor |
     |		      |		|  Console Routine (see Chapter 5).	  |
     |		      |		|					  |
     |    SWPWT       |   0400	|  Swap  Wait--This   task   cannot   run |
     |		      |		|  because  it is in the process of being |
     |		      |		|  brought into memory.			  |
     |		      |		|					  |
     |    EORMWT      |   0200	|  Event or Message  Wait--This  task  is |
     |		      |		|  waiting for an event flag to be POSTed |
     |		      |		|  or  a  message  to  arrive,  whichever |
     |		      |		|  happens first.			  |
     |		      |		|					  |
     |    USERWT      |   0100	|  User Wait--This bit  is  reserved  for |
     |		      |		|  use by user-written tasks.  RTS/8 does |
     |		      |		|  not use this bit.			  |
     |		      |		|					  |
     |    ENABWT      |   0040	|  Enable Wait--This task is  waiting  to |
     |		      |		|  be   enabled.   Use  of  this  bit  is |
     |		      |		|  restricted  to  the  Monitor   Console |
     |		      |		|  Routine.    (See   Chapter  5  for  an |
     |		      |		|  explanation of the ENABLE and  DISABLE |
     |		      |		|  commands.)				  |
     |		      |		|					  |
     |    MSGWT       |   0020	|  Message Wait--This task is waiting  to |
     |		      |		|  be sent a message.			  |
     |		      |		|					  |
     |    DNEWT       |   0001	|  Task does not exist.  This bit  should |
     |		      |		|  never  be  set  or  cleared  by a user |
     |		      |		|  task.				  |
     |		      |		|					  |
     |		      |   0000	|  Task is runnable			  |
     ----------------------------------------------------------------------

     Examples:

     If the TFTABL entry for a task is

	  0020

     the task is waiting for a message.

     If the TFTABL entry for a task is

	  0440



				      7-9

			    PROGRAMMING TECHNIQUES


     the operator disabled the task from running at the MCR terminal  while
     the  nonresident  portion  of  the  task is waiting to be swapped into
     memory.

     If the TFTABL entry for a task is:

     0000

     the task is runnable.  However, this task may not be running if a task
     of higher priority controls the processor.


     7.4.3  Task Input Message Queue Header Table (MSGTBL)

     This table contains a 2-word entry that represents the "head"  (start)
     of the input message queue for each task, as follows:

	  WORD 1    if zero, there  are  no  messages  in  the  queue;   if
		    nonzero,  the  word  is a CDF to the field of the first
		    message in the queue.

	  WORD 2    if word 1 was nonzero, this word is a  pointer  to  the
		    address of the first message in the queue.

     Example:

     Consider the following MSGTBL entries for a task:

	  6211
	  2044

     Since the first entry is nonzero, there  are  messages  in  the  input
     queue waiting for this task to receive them.  The first entry is a CDF
     instruction to field 1.  The second entry is a pointer indicating that
     the first message begins at location 2044 in field 1.


     7.4.4  Residency Table (RESTBL)

     The Residency Table contains a 2-word entry for each nonresident task.

	  WORD 1    contains a pointer to the task's Partition Table  entry
		    in   bits   0-9.    Bit   10   is  set  if  a  task  is
		    checkpointable, and bit 11 is set if the processor  can
		    modify  a task's code during execution.  Checkpointable
		    and modifiable tasks are defined in Section 6.1.

	  WORD 2    contains the absolute block address of the task's  core
		    image on the swap device.


     Example:

     Consider the following RESTBL entries for a task:


				      7-10

			    PROGRAMMING TECHNIQUES


	  1611
	  1124

     This task has a nonresident portion.  The 4-word partition table entry

     that  this  task  uses  begins  at  location  1610.   The  task is not
     checkpointable (bit 10 of entry 1 is  a  0),  but  the  processor  can
     modify it (bit 11 of entry 1 is a 1).

     The disk-resident portion of this task begins at  block  1124  on  the
     swap device.


     7.4.5  Partition Table (PARTBL)

     The Partition Table contains a 4-word entry for each partition.  It is
     accessed through a partition number.

	  WORD 1    contains the length (size) in bits 1-5 and field  (bits
		    6-8)  argument  of  the mass storage device driver call
		    that reads an occupant  into  the  partition  with  the
		    WRITE  bit  set.   Bit 11 of this word is the partition
		    busy flag.

	  WORD 2    contains the memory address of the partition.

	  WORD 3    contains a pointer to word 1 of the  occupant's  RESTBL
		    entry.

	  WORD 4    Reserved for future expansion.

     Example:

     Consider the following PARTBL entries for a particular partition.

	  5421
	  1400
	  1553
	  0000

     This partition is currently in use (bit 11 of entry 1 is  a  1)  by  a
     task whose 2-word RESTBL entry begins at location 1553 (entry 3).  The
     partition begins at location 1400 (entry 2) of field 2  (bits  6-8  of
     entry  1).   The partition is 14 (octal) pages long (bits 1-5 of entry
     1).


     7.4.6  Task Table Structure

     Figure 7-1  summarizes  the  internal  task  table  structure  of  the
     Executive.   The  Residency  Table and Partition Table are optional in
     that the Executive uses them only when nonresident tasks exist in  the
     system.



				      7-11

			    PROGRAMMING TECHNIQUES


		   TASK STATE			     TASK FLAGS	
		  TABLE (TSTABL)		   TABLE (TFTABL)	

     Word 1   Without KT8-A     ______
	    -----------------------------     -----------------------------
	    |				|     | Bits determine if task is |
	    |	 Link GT UM  IF   DF	|     | runnable		  |
	    |				|     |				  |
	    |	 0    1  5  6-8	 9-11	|     |				  |
	    |				|     |				  |
	    -----------------------------     -----------------------------
	      With KT8-A
	    -----------------------------     Task runnable if entry	
	    |				|     contains zero
	    | Link High High UM Low Low |
	    |				|
	    |   0  1-2  3-4  5  6-8 9-11|
	    |				|
	    |---------------------------|
     Word 2 |   Contents of Program     |     ______
	    |	Counter (PC)		|
	    |---------------------------|
     Word 3 |  Contents of Accumulator  |     ______
	    |  (AC)			|
	    |---------------------------|
     Word 4 |  Contents of Multiplier	|     ______
	    |  Quotient (MQ)		|
	    -----------------------------

     Word 5   (Only if EAE)     ______

	      With KT8-A
	    -----------------------------
	    | 4000 + 2000 (GT) + Step	|
	    | Count (if B mode)		|
	    -----------------------------
	      Without KT8-A
	    -----------------------------
	    | 4000 + Step Count		|
	    | (if B mode)		|
	    -----------------------------

	    Upon task execution, TSTABL
	    loaded into corresponding
	    CPU registers		

	    When the task terminates,
	    TSTABL entry set to new
	    contents of CPU registers


	      Figure 7-1 Executive Internal Task Table Structure




				      7-12

			    PROGRAMMING TECHNIQUES


		TASK INPUT MESSAGE		     RESIDENCY
	       QUEUE HEADER (MSGTBL)		   TABLE (RESTBL)
	    ---------------------------     -----------------------------
     Word 1 | If zero, no messages in |	    | Contains pointer to task  |
	    | queue. If nonzero, word |	    | PARTBL entry in bits 0-9; |
	    | is CDF to the field of  |	    | bit 10 - ckeckpointable;  |
	    | first message	      |	    | bit 11 - writeable	|
	    |-------------------------|     -----------------------------
     Word 2 | If nonzero, this word   |     | Block address plus 1 of	|
	    | is pointer to the first |	    | the task's core image on  |
	    | message in the queue    |     | swap device		|
	    ---------------------------     -----------------------------

	    Represents the "head" of        bit 10 of word 1 is set if
	    the input message queue	    task checkpointable
	    for each task	
					    bit 11 of word 1 is set if
					    task modified




			  PARTITION
			TABLE (PARTBL)
	    --------------------------------------
     Word 1 | Contains the length (size) and     |
	    | Field argument (bits 1-8) of the   |
	    | mass storage device driver call    |
	    | that reads occupant into partition |
	    | with 'write' bit set (bit 0).      |
	    |------------------------------------|
     Word 2 | Contains starting address of the	 |
	    | partition			         |
	    |------------------------------------|
     Word 3 | Contains pointer to word 1 of the  |
	    | occupant's RESTBL entry		 |
	    |------------------------------------|
     Word 4 | Unused				 |
	    |					 |
	    --------------------------------------

	    Bit 0 is always set (write)

	    Bit 11 of word 1 is the partition
	    memory flag


	   Figure 7-1 Executive Internal Task Table Structure (cont.)








				      7-13

			    PROGRAMMING TECHNIQUES


     7.4.7  Direct References to System Tables

     A task may directly  interrogate  locations  in  the  RTS/8  Executive
     tables  to  obtain information about itself or any other task, as long
     as you observe the following two restrictions:

	  1.  Due to the interrupt-driven  nature  of  RTS/8,  these  table
	      entries  may  change at any time;  therefore, the task should
	      inhibit interrupts, if necessary, between the time  it  tests
	      these  entries and the time that the processing which depends
	      on the  testing  is  completed.   For  example,  testing  the
	      Message  Queue Header for a task may show no messages, but an
	      I/O interrupt occurring  immediately  after  the  test  might
	      allow  a higher priority task to run.  This task might send a
	      message, invalidating the result of  the  test.   To  prevent
	      this, the task might turn off interrupts during and after the
	      test.

	  2.  Although you can alter  the  system  table  entries,  DIGITAL
	      recommends  that  you  do  so with extreme care and only when
	      absolutely necessary.

     RTS/8  defines  symbols  during  the  sysgen  that   permit   symbolic
     references  to  be  made.   The  symbolic  expressions which yield the
     address of the system table entries for task N are:

	  N+TFTABL	Task Flags Table entry for task N;  if the contents
			are zero, task N is runnable.

	  N^2+MSGTBL	Input Message Queue Header  for  task  N;   if  the
			contents  are  zero,  task N has no messages in its
			queue.

	  N^4+TSTABL	First Word of Task State Table Entry  for  Task  N.
			(The address is N^5+TSTABL if you save the EAE.)

	  N^2+RESTBL	First Word of Residency Table entry for nonresident
			Task N.

     For example, for a task to determine whether it has  messages  in  its
     input queue without issuing a RECEIVE Executive Request, the code is:

	  CDF MSGTBL		  /EXEC TABLES IN FIELD 0
	  IOF			  /TURN INTERRUPTS OFF
	  TAD I (TASK 2+MSGTBL)
	  SNA CLA		  /ANY MESSAGES
	  JMP NONE		  /NO
	  ION			  /YES

     (The code at NONE must eventually turn interrupts back on.)






				      7-14

			    PROGRAMMING TECHNIQUES


     7.5  KL8-A SUPPORT

     The KL8-A support in the Executive allows you to program the RL8-A  in
     a manner similar to the KL8-J.

     First, a task must insert the KL8-A into the interrupt skip chain  and
     provide  a  keyboard and printer interrupt routine to service the line
     if necessary.  For example,

	  .EXTERNAL KL8ACT   /DEFINE SYMBOL AS EXTERNAL
			     /TO MODULE
	  CDF .FLD
	  CIF RTS8	     /FIELD OF RTS/8 EXECUTIVE
	  TAD (LINE^4)
	  JMS I ( KL8ACT )
	  KEYBD INTERRUPT ROUTINE
	  PRINTER INTERRUPT ROUTINE

     where LINE is the line number of the KL8-A.  KL8-A  line  numbers  are
     consecutive,  begin  at 0, and may span across KL8-As.  The KL8-A line
     number is actually of the form 4A+B where A is the number of the KL8-A
     (0,  1, 2,...) and B is the physical line number of the specific KL8-A
     (0-3).

     Second, you must define  the  instruction  corresponding  to  the  TLS
     instruction that you will use when writing to the KL8-A line.

     For example, if the device code for the KL8-A is 40,  then  you  would
     probably define an instruction such as:

	  TLSX=6406

     in the task.

     Normally, a task contains the following code to write a character:

	  TAD char
	  TLS

     When using a KL8-A, the task would first connect up the KL8-A  support
     by  calling  KL8ACT.   Then,  to output a character, you would use the
     following code:

	  TAD line ^400
	  TAD char
	  TLSX

     The TLSX instruction does not clear the AC.








				      7-15






				  APPENDIX A

		 RTS/8 DISTRIBUTED SOURCE FILES AND MNEMONICS


     The following is a list of DIGITAL supplied tasks and handlers.
     ----------------------------------------------------------------------
     | Task Name | File Name |	Task Function				  |
     |-----------|-----------|---------------------------------------------
     | -	 | RTS8.MA   |  RTS/8 Executive				  |
     | CLOCK     | CLOCK.MA  |  Clock Handler Task			  |
     | CSA       | CSA.MA    |  Cassette Driver Task			  |
     | CSAF      | CSAF.MA   |  Cassette File Support Task		  |
     | DTA       | DTA.MA    |  TC08 DECtape Driver Task		  |
     | EXIT      | EXIT.MA   |  Exit Task				  |
     | LPT       | LPT.MA    |  Line Printer Driver Task		  |
     | LTA       | LTA.MA    |  LINCtape Driver Task			  |
     | MCR       | MCR.MA    |  Monitor Console Routine			  |
     | null task | MCR.MA    |  Null Task				  |
     | NULL8A    | NULL8A.MA |  Null Task for PDP-8A			  |
     | OS8       | OS8.MA    |  OS/8 Support Task			  |
     | OS8F      | OS8F.MA   |  OS/8 File Support Task			  |
     | PWRF      | PWRF.MA   |  Power Fail Task				  |
     | RF08/DF32 | RF08.MA   |  RF08/DF32 Fixed-Head Driver Task	  |
     | RK8       | RK8.MA    |  RK8 Disk Driver Task			  |	
     | RK8E      | RK8E.MA   |  RK8, Disk Driver Task			  |
     | RL01      | RL01.MA   |  RL01 Disk Driver Task			  |
     | RX8A      | RX.MA     |  Floppy Disk Handler (1st Controller)	  |
     | RX8B      | RX.MA     |  Floppy Disk Handler (2nd Controller)	  |
     | RX8C      | RX.MA     |  Floppy Disk Handler (3rd Controller)	  |
     | RX8D      | RX.MA     |  Floppy Disk Handler (4th Controller)	  |
     | SWAP      | SWAP.MA   |  Nonresident Task Swapper		  |
     | TTY       | TTY.MA    |  Terminal Driver Task			  |
     | TTY1      | TTY.MA    |  Terminal Driver Task			  |
     | TTY2      | TTY. MA   |  Terminal Driver Task			  |
     | TTY3      | TTY.MA    |  Terminal Driver Task			  |
     | TTY4      | TTY.MA    |  Terminal Driver Task			  |
     | UDC/ICS   | UDCICS.MA |  Universal Digital Controller/		  |
     |           |           |  Industrial Controller Subsystem		  |
     |           |           |  Handler Task				  |
     ----------------------------------------------------------------------

     The following is a list of  task  mnemonics  which  the  RTS/8  System
     Generation Program establishes.

          CLOCK		 Clock Handler
	  CSA		 Cassette Driver Task
	  CSAF		 Cassette File Support Task
	  DF32		 DF32 Disk Driver Task
	  DKC8A		 Auxiliary DKC8A Handler
	  DTA		 DECtape Driver Task
	  EXIT		 Exit Task
	  LPT		 Line Printer Driver Task
	  LTA		 LINCtape Driver Task

				      A-1

		 RTS/8 DISTRIBUTED SOURCE FILES AND MNEMONICS


	  MCR		 Monitor Console Routine
	  NULL8A	 Null Job for PDP-8/A
	  OS8		 OS/8 Support Task
	  OS8F		 OS/8 File Support Task
	  PWRF		 Power Fail Handling Task
	  RF08		 RF08 Disk Driver Task
	  RK8		 RK8 or RK8E Driver Task
	  RX8A		 First Floppy Controller
	  RX8B		 Second Floppy Controller
	  RX8C		 Third Floppy Controller
	  RX8D		 Fourth Floppy Controller
	  SWAP		 Nonresident Task Swapper Task
	  TTY		 Teletype Driver Task
	  UDC		 Universal Digital Controller Task

     The following is a list of system mnemonics you may use when  creating
     tasks.   For  the mnemonics RTS/8 uses for system task parameters, see
     the RTS/8 System Generation Manual.	 ______________________________

     NUMBERS

	  AC7776	CLL STA RAL
	  AC7775	CLL STA RTL
	  AC4000	CLA STL RAR
	  AC3777	CLL STA RAR
	  AC2000	CLA STL RTR
	  AC0002	CLA STL RTL
	  AC5777	CLL STA RTR

     RTS/8 EXECUTIVE

	  CAL		JMS 20
	  POSTDS	JMP I 24
	  WAITM		JMS I 25

	  SEND		0
	  RECEIV	1
	  WAITE		2
	  RUN		3
	  SUSPND	4
	  POST		5
	  SKPINS	6
	  DERAIL	7
	  BLKARG	10
	  SENDW		11
	  UNBARG	12
	  RESCHD	13
	  WAITX		14
	  FREE		4000

     WAITBITS

	  NONRWT	4000
	  EFWT		2000
	  RUNWT		1000

				      A-2

		 RTS/8 DISTRIBUTED SOURCE FILES AND MNEMONICS


	  SWPWT		0400
	  EORMWT	0200
	  USERWT	0100
	  ENABWT	0040
	  MSGWT		0020
	  NETWT		0010
	  DNEWT		0001

     CLOCK

	  MARKTIME	0
	  SCHEDULE	1000
	  TIMEOUT	2000
	  PERIODICALLY	3000
	  CANCEL	7000

     TTY and LPT

	  NOPACK	4000
	  NOCRLF	2000
	  IND		1000
	  NOLINE	400
	  ASSGN		200
	  KL8ALINE	100

     UDC/ICS

	  AO		0
	  DO		0
	  DI		2
	  GC		3
	  EC		4
	  RC		5
	  DC		6
	  ECT		7
	  CS		10	
	  DCT		11
	  AI		12


















				      A-3







				  APPENDIX B


			       RTS/8 FLOWCHARTS



     This appendix contains RTS/8 flowcharts that  graphically  show  RTS/8
     system operation.













































				      B-1

			        RTS/8 FLOWCHARTS


		 ***
	       *      *
	      *	 EXEC  *			Calling Sequence:
	       *      *
	         ***				p-1	TAD VAL
		  |				p	CAL
		  |				p+1	FUNCTION CODE
	          V				p+2	ARG1
	   ----------------			p+3	AGR2 (or return)
  	   |  SAVE AC IN  |			p+4	RETURN
	   |    ACARG     |
	   ----------------			CAL = JMS 20
		  |				Thru Current Field:
		  |				20	0
		  |				21	CDF CUR
		  V				22	CIF 0
	       ////\\\\				23	CMP CALIOF (field 0)
	      /	       \ 			24	DSPOST
	     /	 TASK 	\  TSWFLG = -1		25	XWAITM
	 ---/  SWITCHING \----  No:
	 |  \   ALLOWED  /   |  Rescan
       0 |   \	   ?    /    |  ASAP
      No |    \        /     |
         |     \\\\//// 1    |
	 |	  |    Yes   |
	 -------->|    	     |
		  V	     |	
	 ------------------  |
	 |  INHIBIT TASK  |  |
	 |  SWITCHING.	  |  |
	 |  CLEAR RESCAN  |  |
	 |  FLAG	  |  |
 	 ------------------  |
		  |	     |
		  |<----------	
		  V	
	 ------------------
	 |      ION	  |
	 ------------------
		  |
		  V	
	 ------------------
	 |  SAVE CALLING  |
	 |	FIELD	  |
	 ------------------
		  |
		  V
	 ------------------
	 |  SAVE RETURN   |
	 |   ADDRESS	  |
	 ------------------		
		  |	
		  V
	     To page B-3


				      B-2

			        RTS/8 FLOWCHARTS

	    From page B-2
		  |
	 ------------------	
	 |  GET FUNCTION  |	
	 |	CODE	  |
	 ------------------	
		  |		
		  V			SW designates an operation that
	 ------------------		is performed only when using
	 |      SAVE	  |		nonresident operations.
	 |    COMMAND	  |
	 ------------------		EAE designates an operation that 
	 SW	  |			is performed only when the Extended 
		  |			Arithmetic Element is used.
		  ---------		
		  	  |		
		  	  V
		 ------------------
	 	 |  EXECUTE	  |
		 |  DISPATCH JUMP |	
		 |  THRU COMMAND  |
		 |  TABLE. IGNORE |
		 |  FREE BIT	  |
	 	 ------------------
		          |
        Function          |
        Code	          V				     ****
	    |	 ------------------			   *      *
	    V	 | JMP I .+FUNC+1 |<----------------------* CMDJMP *
		 ------------------			   *      *
	    0	 |     XSEND	  |    Pg. B-5		     ****
		 ------------------
	    1	 |     XRECEIV	  |    Pg. B-17
		 ------------------
	    2	 |     XWAITE	  |    Pg. B-10
		 ------------------
	    3	 |     XRUN	  |    Pg. B-28
		 ------------------
	    4	 |     XSUSPND	  |    Pg. B-28
		 ------------------
	    5	 |     XPOST	  |    Pg. B-20
		 ------------------
	    6	 |     XSKPINS	  |    Pg. B-21
		 ------------------
	    7	 |     XDERAL	  |    Pg. B-22
		 ------------------
	    10	 |     XBLKARG	  |    Pg. B-19
		 ------------------
	    11	 |     XSENDW	  |    Pg. B-5
		 ------------------
	    12	 |     XUNBARG	  |    Pg. B-18
		 ------------------
	    13	 |     XTSTOP	  |    Pg. B-13
		 ------------------
	    14	 |     XWAITX	  |    Pg. B-10
		 ------------------
		  
				      B-3

			        RTS/8 FLOWCHARTS





				     *****
				   *       *
				  *  EXRET  *
				   *       *
				     *****
				       |
				       |
				       V
			       -----------------
			       |     SET UP    |
			       |  RETURN FIELD |
			       -----------------
				       |
				       |
				       |
				       |
				       V
				 ////// \\\\\\	TSWFLG = -1 ---------------
		  TSWFLG=1 	/	      \   Yes	    |  KEEP TASK  |
     ------------   	       / TASKSWITCHING \	    |  SWITCHING  |
     |	Cannot	|<-------------\  NEEDS RESCAN /----------->|  INHIBITED  |
     |  Happen  |		\      ?      /		    ---------------
     ------------		 \\\\\\ //////			    |
				       |			    V
				       | TSWFLG = 0		  *****
				       | No			*       *
				       |		       *  TSTOP  *
				       V			*	*
			       -----------------		  *****
			       |  ALLOW TASK-  |	        (Pg. B-13)
			       |  SWITCHING    |
			       |  JMP I 20     |
			       |  RETURN TO    |
			       |  CALLING TASK |
			       -----------------


















				      B-4

			        RTS/8 FLOWCHARTS

   ---------							  ---------
   | SEND  |							  | SEND  |
   | SENDW |							  | SENDW |
   ---------							  ---------


	     ****		  ***
	   *      *		*     *
	  * XSENDW *	       * XSEND *
	   *      *		*     *
	     ****		  ***
	       |		   |
	       V		   V
	---------------     ---------------	Calling Sequence
	|     SET     |     |    CLEAR    |	p+1  SEND (W)
	|  WAIT FLAG  |	    |  WAIT FLAG  |	p+2  TASK # (Sending to)
	---------------	    ---------------	p+3  MSGADR
	       |		   |		P+4  RETURN
	       ---------------------
			 |
			 |
			 V
	 	 -----------------
		 |  GET TASK     |
		 |  NUMBER TO    |
		 |  SEND MSG TO  |
		 -----------------
			 |
			 |			
			 V
		 -----------------
		 |  GET MESSAGE  |
		 |  ADDRFSS	 |
		 -----------------
			 |
			 |
			 V
		   To page B-6





			Initial Values   |  Becomes
		-------------------------|--------------------
		| p   |	 MSGADR,  0000	 |  Sending Task #   |
		-------------------------|--------------------
		| p+1 |		  0000   |  CDF to next      |
		|     |			 |  msg, if any      |
		-------------------------|--------------------
		| p+2 |		  0000   |  Addr of next     |
		|     |		 	 |  msg (0 if none)  |
		-------------------------|--------------------
		| p+3 |          Start of Message	     |
		----------------------------------------------


				      B-5

			        RTS/8 FLOWCHARTS


				             From page B-5
			       			    |
			       			    V
				           //////////\\\\\\\\\\
					  /		       \
				         /      MESSAGE         \
			          Yes   /   ALREADY IN QUEUE     \
			 ---------------\ (FIRST WORD OF MESSAGE /
			 |	         \	 =0)  ?	        /
			 |		  \		       /
			 |                 \\\\\\\\\\//////////
			 |			    |
			 |			    | No
			 V	        	    |		   ****
	 	-------------------		    |	 	 *	*
		|  BACKUP RETURN  |		    |<----------* MSGFRE *
		|  TO CAL	  |		    |		 *      *
		|  ADDRESS	  |		    |	   	   ****
		-------------------		    V
			 |		   -------------------
	****		 |		   |  BUMP RETURN    |
      *      *		 |		   |  	  TO  	     |
     * MSEFWT *--------->|		   |      CAL+4	     |
      *      *		 |		   -------------------
        ****		 |			    |
			 V			    |
        	-------------------		    V
		|     AC=	  |	   -------------------
		|     MESSAGE	  |	   |  FIND RECEIVING |
		|     ADDRESS	  |	   |  TASK #'s	     |
		-------------------	   |  ENTRY IN	     |
			 |		   |  MSGTBL	     |
			 |		   -------------------
			 V		 	    |
		        ***			    |
		      *	    *			    V
		     * WAITS *		   -------------------
		      *     *		   |    GET DATA     |
			***		   |    FIELD OF     |
		     (Pg. B-10)		   |    MESSAGE	     |
					   -------------------
						    |
						    |
						    V
					           ****
					         *	*
					        * ADDTOQ *
					         *      *
					           ****
					         (Pg. B-7)
			





 				      B-6

			        RTS/8 FLOWCHARTS


				     ****
				   *      *
				  * ADDTOQ *
				   *      *
				     ****
				      |
				      |
				      V
			      ------------------
		 	      |  GET FIRST     |
			      |  QUEUE WORD    |
			      |  (CDF TO NEXT) |
			      ------------------
				      |
				      |
				   ////\\\\
			  Yes	  /	   \
	  -----------------------/  EMPTY   \
	  |			 \  (=0) ?  /
	  |			  \	   /
	  |			   \\\\////
	  |			      |
	  |			      | No
	  |			      V
	  |		      ------------------
	  |	 	      |    CDF INTO    |
	  |		      |    NEXT	       |
	  |		      |    MESSAGE     |
	  |		      ------------------
	  |			      |
	  |			      |
	  |			      V
	  |		      /////////\\\\\\\\\\
	  |		     /                   \
	  |		    /	      IS          \
	  |		   /	 SENDING TASK      \  No    ---------------
	  |		  /  NUMBER LESS THAN TASK  \------>|  FIND NEXT  |
	  |		  \	NUMBER IN THIS      /	    |  MESSAGE IN |
	  |		   \	  QUEUE MSG        /	    |  QUEUE      |
	  |		    \	      ?           /	    ---------------
	  |		     \			 /		   |
	****		      \\\\\\\\\//////////		   |
      *      * 			      |				   V
     * ENDOFQ *---------------------->| Yes			  ****
      *	     *			      |				*      *
	****			      |			       * ADDTOQ *
				      |				*      *
				      V				  ****
				To Page B-8			(Pg. B-7)







				      B-7

			        RTS/8 FLOWCHARTS

		
				From Page B-7
				       |
				       V
			       ------------------
			       |  PUT CDF TO    |
			       |  MSG AND PC OF |
			       |  MSG INTO      |
			       |  QUEUE WORDS   |
			       ------------------
				       |
				       |
				       V
			       ------------------
			       |      IOF	|
			       ------------------
				       |
				       |
				       V
			       ------------------
			       |   GET TASK #	|
			       |   TO SEND	|
			       |   MESSAGE TO 	|
			       ------------------
				       |
				       |
				       V
			       ------------------
			       |  FREE MSG WAIT |
			       |  AND/OR EVENT	|   Via call to FREEJ
			       |  WAIT BITS IN	|
			       |  STATUS TABLE 	|
			       ------------------
				       |
				       |
				       V
			      --------------------
			      |  L=1 IF REVEIV-  |
			      |  ING TASK IS     |   This will be tested if
			      |  RUNNABLE & OF   |   this CAL was a SEND 
			      |  HIGHER PRIORITY |   and not a SENDW.
			      |  THAN SENDER;	 |
			      |  L=0 IF NOT	 |
			      --------------------
				       |
				       |
				       V
				 To Page B-9



				





				      B-8

			        RTS/8 FLOWCHARTS


				From Page B-8
				       |
     D		    ****	       |
     O		  *      *	       |
		 * MSGCDF *----------->|
     N		  *      *	       |
     O              ****	       V
     T			      -------------------
			      |  STORE SENDING  |
     T			      |  TASK NUMBER    |
     O			      |  IN MSG HEADER  |
     U			      -------------------
     C				       |
     H    Link indicates 	       |
	  whether a new		       V
     L    task should be      -------------------
     I    run or not.	      |  STORE CDF TO	|
     N			      |  NEXT MSG IN	|   =0 if none
     K    The link status     |  MSGHDR		|
	  will be checked     -------------------
     I    later on in		       |
     N    POSTEX.		       |
				       V
     T			      -------------------
     H			      |   STORE PC OF   |
     I			      |   NEXT MSG IN   |   =0 if none
     S			      |	  MSGHDR	|
			      -------------------	  Message is now
     C				       |		  linked into the 
     O				       |		  message queue
     D				       |
     E				       V
     				   ////\\\\		   ****
     !				  /        \  No	 *	*
     !				 /  CAL WAS \---------->* POSTEX *
     !				 \  SENDW   /		 *	*
     !				  \   ?    /		   ****
     !				   \\\\////		 (Pg. B-18)
				      |
				      |  Yes
				      V
				    ****
				  *      *
				 * MSEFWT *
				  *      *
				    ****
				  (Pg. B-6)









				      B-9

			        RTS/8 FLOWCHARTS

   ---------							  ---------
   | WAITE |							  | WAITE |
   | WAITX |							  | WAITX |
   ---------							  ---------


                ****		      ****
	      *      *		    *      *
	     * XWAITE *		   * XWAITX *
	      *      *		    *      *
		****		      ****
		  |		       |
		  |		       |
		  V		       V	   Calling Sequence:
	    -------------	---------------
	    |   CLEAR   |	|  SET ACARG  |    p   CAL
	    |   ACARG   |	|    TO -1    |    p+1 WAITE
	    -------------	---------------    p+2 EVENT FLAG ADDR
		  |		       |	   p+3 RETURN
		  -------------------->|
			               |
			               V
			      -------------------
       Enter Here From	      |   GET ADDRESS   |
       SEND or SENDW          |  OF EVENT FLAG  |
       (Pg. B-6)	      -------------------
           ****	              	       |
	 *      *	               |
	* WAITS  *-------------------->|
	 *      *	               |
	   ****			       V
			      -------------------
       ACARG /= -1	      |  SAVE ADDRESS   |
			      |  OF EVENT FLAG  |
			      -------------------
			               |
			               |
			               V
			      -------------------
			      |       IOF	|
			      -------------------
			               |
			               |
			               V
				    ////\\\\		    ****
				   /	    \  Yes	  *      *
				  /  EVENT   \---------->* EXRET  *
				  \ FLAG = 0 /		  *      *
				   \	    /		    ****
				    \\\\////
			               |    No		Restart caller if
				       |		TASKSW allows
				       V		(Pg. B-4)
				  To Page B-11



				      B-10

			        RTS/8 FLOWCHARTS


				From Page B-10
			               |
				       V
			      -------------------
			      |     EVTFLG =    |   Give it waiting
			      |  4000 + TASK #  |   status
			      -------------------
			               |
			               V
				    ////\\\\
			     Yes   /	    \
		------------------/ WAS THIS \
		|		  \ A WAITX  /
		|		   \    ?   /
		|		    \\\\////
		V	               |    No
	-----------------              |
	|  PUSH PC BACK |              V
	|  TO POINT TO  |	   ---------------   Store Event Flag
	|      CAL	|	   |  AC = EFWT  |   Wait in Flag Table
	-----------------	   ---------------
		|			  |
		|			  |
		V			  V
	-----------------		 ****	     Jump with link clear
	|  AC = EORMWT  |	       *      *	     (tested at TSTOP)
	-----------------	      * TSWAIT *     (Pg. B-12)
		|		       *      *
		|		 	 ****
		V
	      ****
	    *	   *
	   * TSWAIT *
	    *	   *
	      ****
	    (Pg. B-12)




















				      B-11

			        RTS/8 FLOWCHARTS


				  (Pg. B-17)
				     ****
				   *	  *         Wait for mesasge.
				  * WAITM3 *        Enter here from RECEIVE.
				   *	  *
				     ****
				       | 
				       | 
				       V
			    -----------------------
			    |  BACKUP CALLING PC  |
			    |  TO DO CALX AGAIN   |
			    -----------------------
				       |
				       V
			      -------------------
			      |     SET LINK	|   Message Wait Status
			      |    AC = MSGWT	|
			      -------------------
	   ****			       |
	 *      *		       |
	* TSWAIT *-------------------->|
	 *      *		       |
	   ****			       V
			      -------------------
			      | SAVE AC IN MASK |
	(Pg. B-19)	      -------------------
	   ****			       |
	 *      *		       |
	* TSWATX *-------------------->|
	 *      *		       |
	   ****			       V
			    -----------------------
			    |  STORE IN TASK #'s  |
			    |  FLAG TABLE ENTRY   |
			    -----------------------
				       |
				       V
			      -------------------   Interrupts were off
			      |       ION	|   here if we came from
			      -------------------   XWAITE.
				       |
				       V
				  To Page B-13












				      B-12

			        RTS/8 FLOWCHARTS


				From Page B-12
				       |
				       V
				     ///\\\
				    /	   \   Yes
				   /  LINK  \------------
				   \  SET ? /		|
				    \	   /		|
				     \\\///		|
			               |   No		|
				       V		|
			      -------------------	|
			      |  CLEAR TASK AC  |	|
			      -------------------	|
	   ****			       |		|
	 *      *		       |		|
	* TSTOP	 *-------------------->|		|
	 *      *		       |		|
	   ****			       V		|
			    ----------------------	|
			    |  SAVE AC IN ACARG  |	|
			    ----------------------	|
				       |		|
				       |<----------------
				       V		
			 -----------------------------
			 |  GET TASK NUMBER'S ENTRY  |
			 |      IN STATUS TABLE      |
			 -----------------------------
				       |
				       V
			      -------------------
			      |   SAVE RESTART  |
			      |  FLAGS, PC, AC  |
			      -------------------
				       |
				       V
			      -------------------
			      |     SAVE MQ	|
			      -------------------
			      EAE      |
				       V
			  ---------------------------
			  |  FREE PARTITION IF FREE |
			  |  BIT WAS SET IN COMMAND |
			  ---------------------------
			      SW       |		    ****
				       |		  *	 *
				       |<----------------* FINDJ  *
				       |		  *	 *
				       |		    ****
				       V		 RTS/8 Scheduler
				 To Page B-14            (Pg. B-30)



				      B-13

			        RTS/8 FLOWCHARTS


				From Page B-13
				       |
				       V
     Schedule next	      -------------------
     runnable task	      |    TASK # = 1   |
     (start scan 	      -------------------
     from top)			       |
				       V
			      -------------------
			      |      ENABLE 	|
			      |  TASKSWITCHING  |
			      -------------------
				       |
				       V
			   -------------------------
			   |  SET 'MACHINE STATUS  |
			   |  UNIMPORTANT' FLAG    |
			   -------------------------
	   ****			       |
	 *      *		       |
	* FINDJL *-------------------->|
	 *      *  ^		       |
	   ****	   |		       V
		   |	    -----------------------
		   |	    |  GET TASK #'s ENTRY |
		   |	    |    IN FLAG TABLE    |
		   |	    -----------------------
		   |		       |
		   |		       |	    Interrupts temporarily
		   |		       |	    inhibited here.
		   |		       |
		   |		       V
		   |		   /////\\\\\		    ****
		   |		  /	     \  Yes	  *      *
		   |		 / FLAGS = 0  \--------->* STARTJ *
		   |		 \ (RUNNABLE) /		  *      *
		   |		  \     ?    /		    ****
		   |		   \\\\\/////		 (Pg. B-15)
		   |	               |    No
		   |		       |
		   |		       |	    Note no end of table
		   |		       |	    check - there must be
		   |		       |	    a runnable task. 
		   |		       |	    (Null task is always
		   |		       |	    runnable.)
		   |		       V
		   |	     ----------------------
		   |	     |  BUMP TASK NUMBER  |
		   |	     ----------------------
		   |		       |
		   |		       |
		   ---------------------




				      B-14

			        RTS/8 FLOWCHARTS


				     ****
				   *	  *	    Here from FINDJ
				  * STARTJ *	    (Scheduler) 
				   *	  *	    Found a runnable task
				     ****
			               |
			               V
			      -------------------
			      |       ION	|
			      -------------------
				       |
			               V
			    -----------------------
			    |  GET TASK #'s ENTRY |
			    |   IN STATUS TABLE   |
			    -----------------------
				       |
			               V
			      -------------------
			      |       IOF	|
			      -------------------
				       |
			               V
			    -----------------------
			    |  SAVE OLD STATUS IN |
			    |    TEMP LOCS OF	  |
			    |  INTERRUPT ROUTINE  |
			    -----------------------
				       |
     Interrupt			       |
     Dismiss code		       |
				       |
			    	       |
	   ****			       |
	 *      *		       |
	* DISMIS *-------------------->|
	 *      *		       |
	   ****			       |
				       V
				   /////\\\\\		    ****
				  /	     \  Yes	  *      *
     This is tested on		 /  PENDING   \--------->* USERSK *
     an 8/E or 8/a only		 \ INTERRUPTS /		  *      *
				  \     ?    /		    ****
		   		   \\\\\/////		 (Pg. B-23)
		   	               |    No
		   		       V
			  ---------------------------
			  |  SWEEP OLD STATUS INTO  |
			  |  DF, IF, AC, PC, ETC.   |
			  ---------------------------
				       |
				       V
				  To Page B-16


				      B-15

			        RTS/8 FLOWCHARTS


				From Page B-15
				       |
				       V
			      -------------------
			      |    RESTORE MQ	|
			      -------------------
			      EAE      |
				       V
			      -------------------
			      |       ION	|
			      -------------------
				       |
				       V
			  ---------------------------
			  |  	    JMP I 0	    |
			  |  RETURN FROM INTERRUPT  |
			  ---------------------------







































				      B-16

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | RECEIV |							 | RECEIV |
   ----------							 ----------


				     *****	    Calling Sequence:
				   *	   *
				  * XRECEIV *	    p-1  TAD ARG
				   *	   *	    p    CAL
				     *****	    p+1  RECEIV
			               |	    p+2  MADDR, 0
				       |	    p+3  RETURN
				       V
			      -------------------
			      |   GET ENTRY IN	|
			      |  MESSAGE QUEUE	|
			      -------------------
				       |
				       V
			      -------------------
			      |  GET FIRST WORD |
			      |  OF QUEUE ENTRY |
			      -------------------
				       |
				       V
				   /////\\\\\		    ****
				  /	     \  Yes	  *      *
     	     ------------------->/   EMPTY    \--------->* WAITM3 *
     	     |			 \ (NO MSGS)  /		  *      *
	     |			  \    ?     /		    ****
	     |	   		   \\\\\/////		 (Pg. B-12)
	     |	   	               |    No
	     |	   		       V
	     |			   /////\\\\\		 -----------------
	     |			  /	     \  No	 |  UNLINK THIS	 |
     	     |			 /  ARG = 0   \--------->|  MESSAGE FROM |
     	     |			 \     ?      /	    ^	 |   THE QUEUE 	 |
	     |			  \          /	    |	 -----------------
	     |	   		   \\\\\/////	    |		 V 
	     |	   	               |    Yes	    |	 -----------------
	     |	   		       V	    |	 |  STORE ADDR   |
	     |			   /////\\\\\	    |	 |  OF MESSAGE   |
     -----------------	  	  /	     \      |    |   IN CAL+2	 |
     |  ADVANCE TO   |	     No	 /  SENDING   \ Yes |    ----------------- 
     |  NEXT MESSAGE |<---------/ TASK OF MSG  \----|		 V
     |  ON THE QUEUE |		\    = ARG     /	 -----------------
     -----------------		 \	      /		 |  AC = CDF TO  |
				  \     ?    /		 |    MESSAGE	 |
				   \\\\\/////		 -----------------
						   	         V
				      		   	        ****
				     			      *      *
				      		     	     * EXRET  *
							      *      *
								****
				      			     (Pg. B-4)
				      B-17

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | UNBARG |							 | UNBARG |
   ----------							 ----------


				     *****
				   *	   *
				  * XUNBARG *
				   *	   *
				     *****
			               |
				       V
			      -------------------
			      |  GET BIT MASK	|
			      |  FROM ARG LIST  |
			      -------------------
				       |		     ****
				       |		   *	  *
				       |<-----------------* UNBLOK *
	 			       |		   *	  *
	   			       V		     ****
			      -------------------
			      |	      IOF	|
			      -------------------
				       |	    Call FREEJ
				       V	  
			     ---------------------  L=1 if clearing mask
			     |  CLEAR MASK BITS  |  bits makes task
			     |   IN FLAG TABLE   |  runnable and it is
			     ---------------------  higher priority; 
				       |	    L=0 otherwise.
				       V	  
			      -------------------
			      |	      ION	|
	(Pg. B-9)	      -------------------
	   ****			       |
	 *      *		       |
	* POSTEX *-------------------->|
	 *      *		       |
	   ****			       V
				   /////\\\\\		    ****
				  /	     \  No	  *      *
     				 /  RUN NEW   \--------->* EXRET  *
     				 \    TASK    /	 L = 0	  *      *
				  \     ?    /		    ****
		   		   \\\\\/////		 (Pg. B-4)
		   	               |    Yes
		   		L = 1  |
				       V
				      ****
				    *	   *
				   * TSTOP  *
				    *	   *
				      ****
				   (Pg. B-13)

				      B-18

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | BLKARG |							 | BLKARG |
   ----------							 ----------


				     *****	    Calling Sequence:
				   *	   *
				  * XBLKARG *	    p-1  TAD TASK #
				   *	   *	    p    CAL
				     *****	    p+1  BLKARG
			               |	    p+2  WAITBITS
			               |	    p+3  RETURN
				       V
			      -------------------
			      |  GET WAIT BITS  |
			      |  FROM ARG. LIST |
	(Pg. B-28)	      -------------------
	   ****			       |
	 *      *		       |
	*  BLOK  *-------------------->|
	 *      *		       |
	   ****			       V
				   /////\\\\\
				  /	     \		    ****
				 /  CALLING   \  Yes	  *      *
     				/  TASK TO BE  \-------->* TSWATX *
     				\    BLOCKED   /	  *      *
				 \ (TASK# = 0)/		    ****
				  \    ?     /		 (Pg. B-12)
		   		   \\\\\/////
		   	               |    No
		   		       V
			    -----------------------
			    |  SET MASK BITS IN   |
			    |  FLAG TABLE ENTRY   |
			    |  OF SPECIFIED TASK  |
			    -----------------------
				       |
				       V
				     *****
				   *	   *
				  *  EXRET  *
				   *	   *
				     *****
				  (Pg. B-4)











				      B-19

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   |  POST  |							 |  POST  |
   ----------							 ----------


				     *****
				   *	   *
				  *  XPOST  *
				   *	   *
				     *****
			               |	    Calling Sequence:
				       V
			      -------------------   p-1  TAD EFPTR
			      |  SAVE ORIGINAL  |   p    CAL
			      |   EVENT FLAG    |   p+1  POST
			      -------------------   p+2  ECDF, CDF EFFLD
				       |	    p+3	 RETURN
				       V
			     ----------------------
			     |  CLEAR EVENT FLAG  |
			     ----------------------
				       |
				       V
			       /////////\\\\\\\\\
			      /			 \		    ****
			     /    WAS SOMEONE     \  No		  *	 *
			    /  WAITING FOR THIS TO \------------>* EXRET  *
			    \	HAPPEN (OLD FLAG   / 	  	  *	 *
			     \	    NEGATIVE)     /  L=0	    ****
			      \	       ?         /	 	 (Pg. B-4)
		   	       \\\\\\\\\/////////
		   	          L=1  |    Yes
		   		       V
			   -------------------------
			   |  GET WAITING TASK'S #  |
			   |  FROM LOW ORDER BITS   |
			   |  OF THE OLD FLAG       |
			   --------------------------
				       |
				       V
			  ---------------------------
			  |  CLEAR BOTH EVENT FLAG  |
			  |    WAIT AND EVENT OR    |
			  |         MESG WAIT	    |
			  ---------------------------
				       |
				       V
				     *****
				   *	   *
				  * UNBLOK  *
				   *	   *
				     *****
				  (Pg. B-18)



				      B-20

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | SKPINS |							 | SKPINS |
   ----------							 ----------


				     *****	    Calling Sequence:
				   *	   *
				  * XSKPINS *	    p    CAL
				   *	   *	    p+1  SKPINS
				     *****	    p+2  MODULE ADDR
			               |	    p+3  RETURN
			               |
				       V
			      -------------------
			      |    GET FIRST    |
			      |   MODULE NAME   |
			      -------------------
				       |
				       V
				   /////\\\\\
				  /	     \  No      -------------------
    				 /  IS IT 0   \-------->|  ALREADY IN THE |
     				 \ 	?     /		|  SKIP CHAIN !!! |
				  \          /		-------------------
		   		   \\\\\/////			  |
		   	               |    Yes			  V
		   		       V			*****
			    -----------------------	      *	      *
			    |  PUT DISMIS ROUTINE |	     *  EXRET  *
			    |   ADDR IN 1st WORD  |	      *	      *
			    -----------------------		*****
				       |		     (Pg. B-4)
				       V
			    --- -------------------
			    |   PUT CDF, CIF OF   |
			    |  DISMIS IN 2nd WORD |
			    -----------------------
				       |
				       V
			   -------------------------
			   |  PUT MODULE ADDRESS   |
			   |  AND CDF, CIF IN LAST |
			   |  MODULE OF INTERRUPT  |
			   |      SKIP CHAIN       |
			   -------------------------
				       |
				       V
				     *****
				   *	   *
				  *  EXRET  *
				   *	   *
				     *****
				  (Pg. B-4)



				      B-21

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | DERAIL |							 | DERAIL |
   ----------							 ----------


				     ****
				   *	  *
				  * XDERAL *
				   *	  *
				     ****
			               |
				       V
			      -------------------   Calling Sequence:
			      |   GET TASK #'s  |
			      |   STATUS TABLE  |   p-1  TAD TASK #
			      |     POINTER     |   p    CAL
			      -------------------   p+1  DERAIL
				       |            p+2  SUBROUTINE
				       V	    p+3  RETURN
			      -------------------
			      |  STORE RESTART  |
			      |   PC IN SUBR    |
			      -------------------
				       |
				       V
			      -------------------
			      |  STORE SUBR+1   |
			      |  IN RESTART PC  |
			      -------------------
				       |
				       V
				     *****
				   *	   *
				  *  EXRET  *
				   *	   *
				     *****
				  (Pg. B-4)



















				      B-22

			        RTS/8 FLOWCHARTS


				   *********
				 *	     *
				*  INTERRUPT  *
				*   ROUTINE   *
				 *           *
				   *********
				       |
				       |
				       V
				   /////\\\\\
				  /	     \		    *******
     				 /    TIME    \  Yes	  *  GO TO  *
				/    SHARING   \--------->*   OS/8    *
				\   INTERRUPT  /          * SUPPORT *
     				 \      ?     /		    *******
				  \          /		  if present
		   		   \\\\\/////
		   	               |    No
				       |
		   		       V
			      -------------------
			      |     SAVE THE    |
			      |  MACHINE STATUS |
	(Pg. B-15)	      -------------------
	   ****			       |
	 *      *		       |
	* USERSK *-------------------->|
	 *      *		       |
	   ****			       V
			     ---------------------
			     |   USER-INSERTED   |
			     |   SKIPS FOR ANY   |
			     |  CRUCIAL DEVICES  |
			     ---------------------
				       |
				       |
				       V
	     *****		   /////\\\\\
	  *	    *		  /	     \ 
	*    GO TO    *	    Yes	 /    KL8A    \
	* APPROPRIATE *<---------\  INTERRUPT /
	*  INTERRUPT  *		  \     ?    /
	  * MODULE  *  		   \\\\\/////
	     *****	               |    No
				       |
		   		       V
				 To Page B-24









				      B-23

			        RTS/8 FLOWCHARTS


				From Page B-23
				       |
		   		       V
				   /////\\\\\	        -------------------
				  /	     \  Yes     |  SET UP LOC 0   |
     				 /   POWER    \-------->|  FOR POWER FAIL |
     				 \  FAILURE   /		|     RESTART     |
				  \     ?    /		-------------------
		   		   \\\\\/////			 |
		   	               |    No			 V
		   		       V		     ********
				   /////\\\\\ 		    *	     *
	   *******		  /	     \		    *  HALT  *
	 *  GO TO  *	    Yes	 /   CLOCK    \		    *	     *
	*   CLOCK   *<-----------\ 	      /		     ********
	 * HANDLER *		  \     ?    /
	   *******	   	   \\\\\/////		 as CPU restarts
        if present	               |    No		   ************
		   		       V		  * 	       *
				    *********		  *  POWER-UP  *
				 *             *	  *  RESTART   *
				*  GO TO FIRST  *	  * 	       *
				*  USER INTER-  *	   ************
				*  RUPT MODULE  *		 |
				 *             *		 V
				    *********		-------------------
							|  AC = POWER-UP  |
							|   EVENT FLAG    |
							|     ADDRESS     |
							-------------------
								 |
								 V
							       ****
							     *	    *
							    * DSPOST *
							     *	    *
							       ****
							    (Pg. B-25)


















				      B-24

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | POSTDS |							 | POSTDS |
   ----------							 ----------


				  (Pg. B-24)
				     *****
				   *	   *
				  *  DSPOST *
				   *	   *
				     *****
				       |	      Come here from user
				       V	      issusing POSTDS
				   /////\\\\\
	   ****			  /	     \ 	      p-3  CDF EFFLD
	 *      *	    Yes	 /   AC = 0   \	      p-2  TAD EFPTR
	* DISMIS *<--------------\ 	?     /	      p-1  COF 0
	 *      *		  \          /	      p    POSTDS
	   ****	   		   \\\\\/////
	(Pg. B-15)	               |    No
		   		       V
			     ----------------------
			     |    SAVE THE OLD    |
			     |  EVENT FLAG VALUE  |
			     ----------------------
				       |
				       V
			      ---------------------
			      |  ZERO EVENT FLAG  |
			      ---------------------
				       |
				       V
				////////\\\\\\\\
			       /                \		    ****
			      /       WAS A      \  Yes	          *      *
			     /    TASK WAITING    \------------->* DISMIS *
			     \ ON THIS FLAG? (OLD /	          *	 *
			      \ VALUE NEGATIVE)  /		    ****
			       \       ?        /	         (Pg. B-15)
				\\\\\\\\////////
		   	               |    No
		   		       V
			   --------------------------
			   |  CLEAR EVENT FLAG AND  |
			   |    EVENT OR MESSAGE    |   Call FREEJ
			   |   WAIT BITS IN TABLE   |
			   |   ENTRY OF WAIT TASK   |
			   --------------------------
				       |
				       V
				 To Page B-26





				      B-25

			        RTS/8 FLOWCHARTS

			
				From Page B-25
				       |
				       V
				   /////\\\\\
     Run the waiting task if	  /	     \		     ****  
     its flag word is now 	 /    RUN     \  No	   *      *
     zero and it is higher	/   WAITING    \--------->* DISMIS *
     priority than the 		\    TASK      /	   *      *
     current user.		 \     ?      /		     ****
				  \          /		  (Pg. B-15)	
		   		   \\\\\/////
		   	               |    Yes
		   		       V
				   /////\\\\\
				  /	     \  	  -----------------
				 /    TASK    \  Yes      |  SET RESCAN   |
     				/   SWITCHING  \--------->|     FLAG      |
				\   INHIBITED  /  	  |  CTSFWLG = -1 |
     				 \  	?     /		  -----------------
				  \          /			  |
		   		   \\\\\/////			  V
		   	               |    No			****
		   		       V		      *	     *
				   /////\\\\\		     * DISMIS *
				  /	     \ 		      *	     *
     			     No	 /  IS SAVE   \			****
     		-----------------\ STATE FLAG /		     (Pg. B-15)
		|		  \   -1     /
		|   		   \\\\\/////
		|   	               |    Yes
		|   		       V
		|	    ------------------------
		|	    |  SAVE CURRENT TASK'S |
		|	    |     PC, AC IN ITS    |
		|	    |  STATUS TABLE ENTRY  |
		|	    ------------------------
		|		       |
		|		       V
		|	      -------------------
		|	      |  SAVE TASK'S MQ |
		|	      -------------------
		|	      EAE      |
		|--------------------->|
				       V
			      -------------------
			      |       ION	|
			      -------------------
				       |
				       V
				 To Page B-27






				      B-26

			        RTS/8 FLOWCHARTS


				From Page B-27
				       |
				       V
			      -------------------
			      |    PREPARE TO   |
			      |  START NEW TASK |
			      -------------------
				       |
				       V
				   /////\\\\\			    ****
				  /	     \  No		  *      *
     				 /   IS IT    \----------------->*  FINDJ *
     				 \  RESIDENT  /			  *      *
				  \     ?    /			    ****
		   	      SW   \\\\\/////			 (Pg. B-30)
		   	               |    Yes
		   		       V
				     ****
				   *	  *
				  * STARTJ *
				   *	  *
				     ****
				  (Pg. B-15)
			
































				      B-27

			        RTS/8 FLOWCHARTS


   ---------							  ---------
   |  RUN  |							  |  RUN  |
   ---------							  ---------


				     *****
				   *	   *
				  *  XRUN   *
				   *	   *
				     *****
				       |		Calling Sequence:
				       V
			      -------------------	p-1  TAD TASK #
			      |   AC = RUNWT    |	p    CAL
			      -------------------	P+1  RUN
				       | Run Wait	p+2  RETURN
				       V
				     *****
				   *	   *
				  * UNBLOK  *		Go and set the 
				   *	   *		flag bits.
				     *****
				  (Pg. B-18)





   ----------							 ----------
   | SUSPND |							 | SUSPND |
   ----------							 ----------


				     *****
				   *	   *
				  * XSUSPND *
				   *	   *
				     *****
				       |		Calling Sequence:
				       V
			      -------------------	p-1  TAD TASK #
			      |   AC = RUNWT	|	p    CAL
			      -------------------	p+1  SUSPND
				       |		p+2  RETURN
				       V
				     *****
				   *	   *
				  *  BLOK   *
				   *	   *
				     *****
				  (Pg. B-19)





				      B-28

			        RTS/8 FLOWCHARTS


   ---------							  ---------
   | WAITM |							  | WAITM |
   ---------							  ---------


				     *****
				   *	   *
				  *  XWAITM  *
				   *	   *
				     *****
				       |
				       V
			      -------------------
			      |    SAVE AC IN   |
			      |    'COMMAND'  	|
			      -------------------
			      SW       |
				       V
			      -------------------
			      |   CLEAR AC, L   |
			      -------------------
				       |
				       V
			      -------------------
			      |   FAKE A CAL	|
			      -------------------
				       |
				       V
			      -------------------
			      |  DISABLE TASK   |
			      |   SWITCHING	|
			      -------------------
				       |
				       V
			      -------------------
			      |     PUT WAIT	|
			      |    BITS IN AC	|
			      -------------------
				       |
				       V
				     *****
				   *	   *
				  *  TSWAIT *
				   *	   *
				     *****
				  (Pg. B-12)










				      B-29

			        RTS/8 FLOWCHARTS


				     *****
				   *	   *		RTS/8 SCHEDULER
				  *  FINDJ  *		FIND A TASK TO RUN
				   *	   *
				     *****
				       |
				       V
			      -------------------
			      |   ENABLE TASK	|
			      |    SWITCHING	|
			      -------------------
				       |
				       V
			    -----------------------
			    |      GET SET TO     |
			    |  EXAMINE FIRST TASK |
			    -----------------------
				       |
				       V
			      -------------------
			      |    ZERO SAVE	|
			      |    STATE FLAG	|
			      -------------------
				       |
		---------------------->|
		|		       V
		|	      -------------------
		|	      |       ION	|
		|	      -------------------
		|		       |
		|		       V
		|	      -------------------
		|	      |     BUMP TO 	|
		|	      |     NEXT TASK	|
		|	      -------------------
		|		       |
		|		       V
		|	      -------------------
		|	      |       IOF	|
		|	      -------------------
		|		       |
		|		       V
		|	      -------------------
		|	      |  GET TASK FLAGS |
		|	      -------------------
		|		       |
		^		       V
	From Page B-31		  To Page B-31








				      B-30

			        RTS/8 FLOWCHARTS


	   To Page B-30		 From Page B-30
		^		       |
		|		       V
		|		  //////\\\\\\
		|		 /            \
		|		/     ANY      \
	 	|	  Yes  /    BLOCKING    \
	 	|--------------\BITS OTHER THAN /
				\     NRWT     /
				 \     ?      /
				  \\\\\\//////
				       |     No
				       V
				   /////\\\\\			    ****
				  /	     \  Yes		  *      *
     				 /  IS TASK   \----------------->* STARTS *
     				 \  RESIDENT  /			  *      *
				  \     ?    /			    ****
		   		   \\\\\/////			 Start task
		   	          SW   |    No			 (Pg. B-15)
		   		       V
			      -------------------
			      |    PUT TASK	|
			      |    INTO SWPWT	|
			      -------------------
			      SW       |
				       V
			      -------------------
			      |   TAKE SWAPPER	|
			      |   OUT OF RUNWT	|
			      -------------------
			      SW       |
				       V
				     *****
				   *	   *
				  *  FINDJ  *
				   *	   *
				     *****
				  (Pg. B-30)

















				      B-31






				  APPENDIX C

				   GLOSSARY

     ACCUMULATOR
	A part of the arithmetic unit of a computer.  It is a register that
	receives  the results of a computation or holds one of the operands
	in a computation.

     ADDRESS
	1. A name, label, or number which identifies a register, a location
	   in storage, or any other data source or destination.
	2. The part of an instruction that specifies  the  location  of  an
	   operand of that instruction.

     ANALOG
	Signals, and other such quantities, which  can  occur  anywhere  on
	some continuous scale.

     ANALOG-TO-DIGITAL CONVERTER (ADC)
	A circuit which converts analog signals to digital data.

     ARGUMENT
	1. A variable or constant which is given in a function  call  or  a
	   subroutine as information to it.
	2. The known reference factor necessary to find an item in a  table
	   or array (i.e., the index).

     ASSEMBLER
	A program which  translates  assembly  language  instructions  into
	machine  language  instructions  and  assigns  memory  locations to
	variables and constants.

     ASYNCHRONOUS
	The scheduling of operations by "ready" and "done" signals rather
	than by time intervals.

     AUTO-INDEX REGISTER
	Whenever one of the absolute locations from 0010  through  0017  in
	any  memory  field  is  addressed  indirectly, the contents of that
	location is incremented by one, rewritten in the same location, and
	used  as the effective address of the current instruction.  Because
	these registers increment by one, the programmer can  use  them  in
	automatically indexing tables.

     AUTORESTART
	The ability to start up the CPU automatically on power up.

     BACKGROUND PROCESSING
	The automatic execution of a low  priority  computer  program  when
	higher-priority  programs  are  not  using  the system's resources.
	RTS/8  protects  the  foreground  from  the  background   but   the
	background is not protected from the foreground.


				      C-1

				   GLOSSARY

     BAUD
	A unit  of  signalling  speed  equal  to  the  number  of  discrete
	conditions  or  signal  events  per  second.  For example, one baud 
	equals one-half dot cycle per second in  Morse Code,  one  bit  per 
	second in a train of binary signals, and one 3-bit value per second 
	in a train of signals, each  of  which  can  assume  one  of  eight 
	different values.

     BIT (BINARY DIGIT)
	In the binary notation, either of the characters 0 or 1.

     BLKARG
	An RTS/8 Executive Request which stands for Block Argument.

     BLOCK
	1. A set  of  consecutive  machine  words,  characters,  or  digits 
	   handled  as  a  unit, particularly in reference to I/O.  An OS/8 
	   block is 400 (octal) contiguous words.
	2. To inhibit a process from continuing.

     BLOCK GAP
	The blank space between blocks on a recording medium.

     BLOCKING BITS
	Bits in an RTS/8 monitor table which specify why a  given  task  is 
	blocked.

     BYTE
	A group of bits considered as a unit;  usually a subdivision  of  a 
	word.  Bytes on the PDP-8 are six bits in length.

     CAL
	An RTS/8 mnemonic which indicates JMS 20.

     CASSETTE
	A small case containing a length of magnetic tape--the tape remains 
	in the case for convenient use.

     CENTRAL PROCESSING UNIT (CPU)
	The part of the computer  containing  the  arithmetic  and  logical 
	units,  the  instruction control unit, and other circuits necessary 
	for controlling the interpretation and execution of instructions.

     CHECKPOINTABLE TASK
	A task that may be swapped out of memory automatically, without its 
	consent, to make room for higher-priority tasks.

     CHECKSUM
	A value representing the sum of all bytes in a program.   When  the 
	program  is  loaded,  the sum of the bytes can be compared with the 
	checksum to make sure that the entire program has been loaded.

     CLEAR
	1. To erase the contents of a storage  location  by  replacing  the 
	   contents with zeros or spaces.
	2. In binary code, to set to zero.

				      C-2

				   GLOSSARY


     CLOCK
	A device that generates periodic signals for synchronization.

     COMMUNICATION REGION
	Locations 20-27 of every field, used to simplify passing  Executive 
	Requests across field boundaries.

     COMPUTE BOUND
	Requiring extensive (or total) use of the  CPU  relative  to  other
	hardware elements (such as I/O devices).

     CONFIGURATION
	1. A particular selection of computer, peripherals, and interfacing
	   equipment that function together.
	2. A list of the devices and computers of a computer system.

     CONTIGUOUS
	Code which resides in memory immediately adjacent to other sections
	of code.

     CONTROLLER
	The device or portion of a device which controls the  operation  of
	connected  devices.   Some  controllers  can  initiate simultaneous
	positioning commands to some of its devices and can then perform  a
	transfer for one of its devices.

     CORE IMAGE FILE
	A file in core image format (i.e.,  a  'picture'  of  core);   also 
	known as a SAVE file.

     CORE MEMORY
	The main high-speed storage of a computer in which binary  data  is
	represented  by  the  switching  polarity  of magnetic cores.  (See 
	also, MOS memory.)

     COUNTER CHANNEL
	A UDC/ICS functional device.

     CPU REGISTERS
	High-speed  circuitry  used  to  store  information  affecting  the
	operation of the CPU (for example, PC, IF, DF).

     DATA
	A general term used to denote any or all facts,  numbers,  letters,
	and symbols.

     DATA FIELD (DF)
	A register which determines the memory field  from  which  operands
	are taken in indirectly addressed instructions.

     DEBUG
	To detect, locate, and correct mistakes in a program.

     DEFERRED ACTIONS
	Actions which are considered low priority  and  are  not  performed

				      C-3

				   GLOSSARY


	until higher-priority actions are serviced.

     DEFERRED REQUESTS
	Requests which are considered low priority and are  serviced  after
	high priority requests.

     DERAIL
	To  transfer  control  or  execution  of  a  specified  task  to  a
	subroutine.

     DEVICE CODES
	Numbers assigned to each device in the system, used in the computer
	instructions for those devices.

     DEVICE STATUS REGISTER
	A register which contains the current status of a device.

     DIGITAL
	Representing information by discrete units  instead  of  continuous
	gradations.  (Note:  "digital" is not synonymous with "binary".)

     DIRECTORY-STRUCTURED DEVICE
	A storage volume with a true volume directory at its beginning that
	contains information (file name, file type, length, etc.) about all
	the files on the volume.  Such volumes include all disks, diskettes
	(floppies), and DECtapes.

     DRIVER, see Handler.

     DYNAMIC
	Pertaining to a quantity that is affected by some  condition  (such 
	as  time) and is therefore relative to that condition;  also refers 
	to features at system run-time.

     ENTRY POINT
	The location in a routine to which control can be  transferred  and
	execution begun.

     EVENT
	A change in the processor status or an indication of the occurrence
	of some activity that concerns an individual process.

     EVENT FLAG
	A bit that can be set or cleared to indicate the occurrence of  the
	event   associated  with  that  flag.   Event  flags  are  used  to 
	synchronize activities in a process or among processes.

     EXECUTIVE
	The central component of the operating system.  It co-ordinates and
	controls all other tasks in the system.

     EXECUTIVE REQUESTS
	Means of communication between tasks and the RTS/8 Executive.



				      C-4

				   GLOSSARY


     FIELD
	A division of memory on a PDP-8 computer referring to a 4K  section
	of memory.

    FILE GAP
	An area on a storage medium, such as tape, used to indicate the end
	of a file.

    FLAG
	A variable or register used to record  the  status  of  a  task  or
	device. In the latter case, it is sometimes called a device flag.

    FREE
	An RTS/8 Executive Request that tells the  Executive  it  can  swap
	another task into a partition.

    GAIN
	Amplification.

    HANDLER
	A routine which is designed to control the operation of a device.

    HEADER
	The control information prefixed in a message text;   for  example,
	source or destination code, priority, or message type.

    HERTZ
	A unit of frequency equal to one  cycle  per  second.   Cycles  are
	referred  to  as Hertz in honor of the experimenter Heinrich Hertz.
	Abbreviated Hz.

    HIBERNATION
	A state in which a task is inactive, but  known  to  the  Executive 
	with  all  of  its  current  status.  A hibernating process becomes 
	active again when a wake request is issued (such  as  clearing  its 
	RUNWT bit).  A task can schedule a wake request before hibernating, 
	or another process can issue the wake request.

    I/O BOUND
	A condition in which a process is performing  much  I/O  but  using
	very little CPU time.

    IDLE TIME
	That part of CPU time in which no job can run because all jobs  are
	halted or are waiting for some external action such as I/O.

    INDIRECT ADDRESS
	An address in a computer instruction which indicates a location  in
	memory where the address of the referenced operand is found.

    INITIALIZATION CODE
	Code which sets counters, switches, and addresses to zero or  other
	starting  values  at  the beginning of or at prescribed points in a
	computer routine.


				      C-5

				   GLOSSARY


    INPUT BUFFER
	A section of memory used for storage of input data.

    INSTRUCTION FIELD (IF)
	A register which holds the  contents  that  determines  from  which
	field  the  operand  of  a directly addressed instruction should be 
	taken.

    INTERACTIVE
	Pertaining to the exchange of information  and  control  between  a
	user and a computer process or processes.

    INTERFACE
	A shared  boundary,  for  example,  the  wires  and  perhaps  other
	electronics connecting two subsystems.

    INTERLOCK SCHEME
	Arranging the  control  of  devices  so  that  their  operation  is
	interdependent.

    INTERRUPT
	1. To break the normal operation of the routine being executed  and
	   pass  control  to  a specific location--generally accompanied by
	   saving the state of the current  routine  so  that  control  can
	   return later.
	2. Also, the signal which causes the interrupt.

    INTERRUPT PROCESSING ROUTINE 
    INTERRUPT SERVICE ROUTINE
	The routine entered when a device interrupt occurs.

    INTERVAL QUEUE
	A list of actions to perform, each accompanied by the  interval  of
	time  which  is  to  elapse from the previous action to the current 
	one.

    LINE FREQUENCY CLOCK
	A clock whose ticking occurs  at  a  multiple  of  the  power  line
	frequency.

    LINK
	1. A 1-bit register in the PDP-8.
	2. An address pointer generated automatically by the  assembler  to
	   indirectly address an off-page symbol.

    LOGICAL OR
	A logical function of two or more inputs  which  is  true  whenever
	either input is true.

    LOOP
	A portion of a program that is  constructed  so  that  the  central
	processor  repeats  the same sequence of instructions over and over
	again until a predefined condition occurs.



				      C-6

				   GLOSSARY


    MASS STORAGE
	A device such as disk or DECtape which stores large amounts of data
	readily accessible to the CPU.

    MEMORY ADDRESS
	A register which holds the address specified by a memory  reference
	instruction.

    MEMORY REFERENCE INSTRUCTION
	A computer instruction that accesses the computer memory during its
	execution, as opposed to a register instruction which only accesses
	registers in the CPU and I/O instructions  which  are  commands  to
	peripheral devices.

    MESSAGE
	A contiguous area of memory containing information that is used  in
	intertask communication or information to be used by an I/O device.

    MESSAGE DRIVEN
	A task is message  driven  if  it  executes  only  in  response  to
	messages received from other tasks.

    MNEMONIC
	A symbolic representation of an  operation  code  or  address  (for
	example, ATL for Atlanta, JMP for jump, etc.).

    MODULE
	A routine which handles a particular function.

    MONITOR CONSOLE ROUTINE (MCR)
	The routine providing the user with functions which  allow  him  to
	control, inspect, and debug a system.

    MOS (METAL-OXIDE SEMICONDUCTORY) MEMORY
	A type of memory that stores data by using a  charge  to  represent 
	the  value of a bit.  This memory is volatile in that a charge must
	continually be applied to  it;   consequently,  if  such  a  system
	crashes,  it  no longer retains the information stored in it.  Thus
	power fail hardware cannot be used to restore it if a power failure
	occurs.

    MULTIPLIER QUOTIENT (MQ)
	A 12-bit register used with the accumulator to perform mathematical
	operations.

    MULTIPROGRAMMING
	A technique that allows scheduling such that more than one job at a
	time  is  in  an executable state.  Thus, even with one CPU, it can 
	appear that more than one program is running simultaneously because 
	the  CPU  is  giving  small  bits  of  its  time to each executable 
	program.

    NONRESIDENT TASK
	A task or a portion of a task that is swapped into memory  when  it 
	becomes executable.

				      C-7

				   GLOSSARY


    NO-OP
	An instruction which specifically  instructs  the  computer  to  do 
	nothing for one cycle and then to get the next instruction.

    NULL CHARACTERS
	Characters with ASCII code of 000.

    OVERFLOW
	A condition occurring when a mathematical operation yields a result
	whose magnitude is larger than that which the program is capable of
	handling.

    OVERLAY
	The technique of repeatedly using the same area  of  memory  during 
	different  stages  of  a  program.   When  one routine is no longer 
	needed in memory, another routine can replace it.

    PACK
	1. To compress data in memory or on a peripheral storage device  by 
	   taking  advantage  of  known characteristics of the data so that 
	   the original data can be recovered.
	2. A disk pack (that is, a removable set  of  disks  mounted  on  a 
	   common shaft).

    PAGE
	1. That portion of a text file delimited by  form  feed  characters 
	   and generally 50-60 lines long.
	2. A 128-word section of memory, beginning at an address which is a 
	   multiple of 128.

    PARITY BIT
	A binary digit appended to an array of binary digits  to  make  the 
	sum of all bits in a word or byte always odd or always even.

    POINTER
	1. A location or register containing an address rather  than  data.  
	   A pointer may be used in indirect addressing or in indexing.
	2. An instruction indicating the address, position, and length of a 
	   byte of information (for example, a byte pointer).

    POST
	To set an event flag to a FINISHED state  via  an  RTS/8  Executive 
	Request.

    POSTDS
	An RTS/8 system mnemonic which  allows  posting  at  the  interrupt 
	level.

    POSTED
	One of the states of an event flag, indicating that  the  event  is 
	complete;  same as FINISHED.

    POWER FAIL
	Logic circuits that protect  an  operating  program  in  the  event
	computer  primary  power  dies.   The  circuits automatically store

				      C-8

				   GLOSSARY


	current operating parameters, restore them, and  resume  processing
	when power returns.

    PRIORITY SCHEME
	A scheme by which certain operations or the execution of a  set  of
	instructions is given preference over other operations.

    PROGRAM COUNTER
	A register in the  CPU  that  holds  the  address  of  the  current
	instruction being executed plus one word;  in other words, it holds
	the address of the next instruction unless the current  instruction
	causes a jump.

    PROMPTING CHARACTER
	A character which prints on the console terminal and cues the  user
	to perform some action.

    QUEUE
	A waiting list (for  example,  a  queue  of  programs  waiting  for
	processing time).

    READY FLAG
	A bit which a device controller sets when it  is  ready  to  accept
	commands from the CPU.

    REAL-TIME SYSTEM
	A system in which computation is performed while a related physical
	process  is occurring so that the results of the computation can be
	used in guiding or measuring the physical process.

    RECEIV
	An RTS/8 Executive Request which informs the Executive that a  task
	wishes to receive a message.

    RECEIVER
	The task which has received a message from another task (sender).

    RECORD
	A collection of related items  of  data  treated  as  a  unit,  for 
	example,  a  line  of  source  code,  a person's name, rank, serial
	number, etc.

    RECORD HEADER AREA
	An area of at least 40  (octal)  words  in  length  which  contains
	information necessary to perform cassette operations.

    RESCHD
	An RTS/8 Executive Request which instructs the Executive to execute
	the highest executable task.

    RESPONSE TIME
	The time between the generation of an inquiry or  request  and  the
	receipt  of  the  response  or  the accomplishment of the requested
	action.


				      C-9

				   GLOSSARY


    RING BUFFER
	A storage area for data accessed on a  first-in,  first-out  basis.
	Similar to QUEUE, but usually involves storage of character codes.

    ROOT SEGMENT
	The portion of a nonresident task that is always in memory.

    RUN
	An RTS/8 Executive Request which clears a task's RUN WAIT bit.

    SCHEDULING
	The operation of sharing resources among computing tasks.

    SEMAPHORE
	A common word used to  control  the  exchange  of  signals  between
	concurrent processes.

    SEND
	An RTS/8 Executive Request which transmits a message  to  one  task
	from another.

    SENDER
	The task which has sent a message to another task (receiver).

    SENDW
	An RTS/8 Executive Request which transmits a message to  one  task,
	then  places  the  task  into Message Wait until the receiving task
	acknowledges receipt of the message.

    SIGN BIT
	In complementary arithmetic, the bit directly to the  left  of  the
	number  indicates  the  sign (+ or -) of the number.  A 1 indicates
	negative numbers while a 0 indicates positive.

    SIMULATE
	To represent the function of a  device,  system,  or  program  with
	another device, system, or program.

    SKIP CHAIN
	An instruction sequence which determines the source of an interrupt
	request;   contains  one or more tests for each possible (hardware)
	interrupt condition.

    SKPINS
	An RTS/8 Executive Request that links interrupt processing routines
	into a skip chain.

    STATE
	A complete description of the condition of a piece of  hardware  or
	of a task.

    SUSPEND
	1. To temporarily halt execution of a task while  another  task  of
	   higher priority runs.
	2. An RTS/8 Executive Request action which sets a waitbit.

				     C-10

				   GLOSSARY

    SWAPPING
	The movement by the Executive of a task between memory and  a  mass
	storage  device.   This  allows  more than one task to use the same
	memory space.

    SWAPPING DEVICE
	A mass storage device from which swapping occurs.  It must  be  the
	system device.

    SYNCHRONIZATION
	A means of coordinating tasks (through event  flags)  so  that  one
	task executes while others wait.

    SYSTEM SOFTWARE
	DIGITAL-supplied  programs  which  come  in  the   basic   software
	packages.

    SYSTEM TICKS
	An RTS/8 convention designed to obviate the  tasks  in  the  system
	from knowing the frequency of the clock.

    TABLE
	A collection of data sorted for ease of  reference;   generally  an
	array.

    TASK
	A routine which performs a  specific  function  and  which  may  be
	resident or nonresident.  A resident task is permanently located in
	memory.  A nonresident task is loaded into memory as it  is  needed 
	and can be overlaid after its completion.

    TASK FLAGS TABLE
	A table of 1-word entries in the  RTS/8  Executive  whose  contents
	determine whether a task is runnable.

    TASK INPUT MESSAGE QUEUE HEADER TABLE
	A table of 2-word entries which represent the  head  of  the  input
	message queue for each task.

    TASK NUMBER
	A unique number between 1 and 127 (decimal) assigned to  each  task
	in an RTS/8 system.

    TASK STATE TABLE
	A table of 4- or 5-word entries  which  contains  the  most  recent
	contents of CPU registers for each task.

    TASK SWITCHING
	The act of stopping execution of one task and continuing  execution
	of another from the point that it was last stopped.

    TERMINAL
	A device that permits data entry into or data exit from a  computer
	system  or  computer  network.   Terminals  may accommodate data in 
	human or machine readable form.


				     C-11

				   GLOSSARY


    TIME OUT
	A specified amount of time that the system waits  for  a  response.
	If there is no response within the specified time, an error occurs.

    UNBARG
	An RTS/8 Executive Request which clears a bit (or bits) in a task's
	Task State Table.

    UTILITIES
	Routines to perform non-Monitor related functions.

    WAITBITS
	Bits which the RTS/8 Executive sets or clears.  These bits indicate
	conditions that prevent a task from running.

	WAITE
	An RTS/8 Executive Request telling the Executive that a task wishes
	to wait until another task posts an event flag.

    WAITM
	An RTS/8 mnemonic telling the  Executive  to  wait  until  multiple
	event flags have been posted.

    WAITX
	An RTS/8 Executive Request telling the Executive that a task wishes
	to wait until another task posts a particular event flag.

    WAKE
	To activate a hibernating process.  A hibernating  process  can  be
	awakened  by  another  process  or by the clock, if the hibernating
	process scheduled a wake-up call.

    WORD
	In the PDP-8, a 12-bit unit of data which  may  be  stored  in  one
	addressable location.





















				     C-12







				     INDEX

     > (MCR prompt), 5-1		  Concurrent information
					      manipulation,
					      see Delicate code
					  Console handler,
     ALARMH, 4-14			      see Terminal handler
     ALARML, 4-14
     Analog input UDC/ICS operation,
	 4-48
     Analog output UDC/ICS operation,     DAte, MCR command, 5-3
	 4-49				  DECcassettes, 4-3
					  Delicate code, 7-1
					  DEposit, MCR command, 5-4
					  DERAIL, 3-7
     Background terminal,		  DF32 handler,
       see Terminal driver		    see Mass storage handler
     BLKARG, 3-4			  Digital input UDC/ICS operation,
     Blocking,				      4-51
       see Executive requests,		  Digital output UDC/ICS
	 BLKARG				      operation, 4-51
					  Disable contacts UDC/ICS
					      operation, 4-52
					  Disable counter UDC/ICS
     CAL, 3-1				      operation, 4-53
     CAncel, MCR command, 5-3		  DIsable, MCR command, 5-4
     Cassette file support handler,       Diskette,
	 4-8				    see Floppy disk handler
       header formats, 4-9		  DNEWT, 3-5
       message format, 4-9
       message words, 4-8
       operations, 4-8
     Cassette handler, 4-3		  EFWT, 3-5
       message format, 4-3		  Emergency breakthrough task,
       message words, 4-4		      4-21
       record size, 4-3			    message format, 4-21
     Cassette utility function		  Emergency conditions,
	 handler, 4-6			    see Executive requests, DERAIL;
       message format, 4-6		      Emergency breakthrough task
       message words, 4-7		  ENABWT, 3-5
     Change of state UDC/ICS		  Enable, MCR command, 5-5
	 operation, 4-50		  Enable contacts UDC/ICS
     Checkpointable tasks, 6-2		      operation, 4-54
     Clock handler, 4-11		  Enable counter UDC/ICS operation,
       CLASS specification, 4-11	      4-55
       commands, 4-12			  EORMWT, 3-5
       immediate response subroutine,	  ER,
	 4-14				  see Executive requests
       HERTZ, 4-11			  Event flags, 2-2, 3-16
       maximum interval, 4-12		  multiple event waits, 7-5
       message format, 4-11		    setting, 3-11
       SHERTZ, 4-11			    states, 2-2, 2-3


				    Index-1

				 INDEX (CONT.)

     Event flags (Cont.)		  Interrupts, 2-6
       waiting for any, 3-26		  Intertask communication,
       waiting for specific, 3-28	    see Task execution
     EXamine, MCR command, 5-5
     Executive, 1-1
       location, 3-2
     Executive requests, 3-1		  KL8-A, 7-15
       BLKARG, 3-4			  KT8-A, 5-9, 7-7
       DERAIL, 3-7, 4-45
	 dangers, 3-8
	 restrictions, 3-7, 3-8
       FREE, 3-10, 6-4			  LEVEL definition, 6-5
       POST, 2-2, 3-11			  LINCtape handler, 4-29
	 task control transfer, 3-11	    message format, 4-29
       RECEIV, 3-12			    message words, 4-29
       RESCHD, 3-14, 7-4
       RUN, 3-15
       SEND, 3-16			  Line printer handler, 4-32
	 task control transfer, 3-16	    see also, Terminal handler
       SENDW, 3-17			      message format, 4-32
       SKPINS, 3-18
       summary, 3-2
       UNBARG 3-24			  Mass storage handler, 4-34
       wait states, 3-31		    message format, 4-34
       WAITE, 2-3, 3-9, 3-26		    message word, 4-34
       WAITX, 3-9, 3-26, 3-27		    RL01 format, 4-35
     EXIT, MCR command, 5-5		    RL01 physical unit/logical
     Exit task, 4-23			      unit correspondence, 4-35
					  MCR,
					    CAncel command, 5-3
					    command length, 5-1
     Floppy disk handler, 4-24		    command summary, 5-2
       interleave scheme, 4-28		    DAte command, 5-3
       message format, 4-24		    DEposit command, 5-4
       message words, 4-24		    DIsable command, 5-4
       status bits, 4-26		    ENable command, 5-5
     Foreground operation,		    error messages, 5-10
       see Terminal driver		    EXamine command, 5-5
     FREE, 3-10, 6-4			    EXIT command, 5-5
					    invoking, 4-17
					    NAme command, 5-5
					    OPen command, 5-6
     Generic code UDC/ICS operation,	    POst command, 5-6
	 4-53				    prompt, 5-1
					    REquest command, 5-7
					    STop command, 5-8
					    syntax, 5-1, 5-2
     Immediate response subroutine,	    SYstat command, 5-8
       see Clock handler		    TIme, 5-10
     Interrupt processing routines,       Message queue header table
	 3-18				      (MSGTBL), 7-10
       execution time, 3-19		    location, 7-14
       restrictions, 3-19		  Message queues, 2-4, 3-12
       skip chain, 3-18
	 ordering, 3-18


				    Index-2

				 INDEX (CONT.)


     Messages,				  Power fail task, 4-45
       see Task communication,		  Priority
	 messages			    see Task priority
     Mnemonics, A-1
     Modifiable nonresident tasks,
	 6-3
     MSGTBL, 7-10			  Read counter UDC/ICS operation,
     MSGWT, 2-4				    4-57
     Monitor console routine,		  Real-time operation, 1-3
       see MCR				  RECEIV, 3-12
					  REquest, MCR command, 5-7
					  RESCHD, 3-14, 7-4
					  Residency table (RESTBL), 7-10
     NAme, MCR command, 5-5		    location, 7-14
     Nonconsole handler,		  RESTBL, 7-10
       see Terminal handler		  RF08 handler,
     NONRES macro, 6-5			    see Mass storage handler
     Nonresident tasks, 3-10, 6-1	  RK8 handler,
       checkpointable tasks, 6-2	    see Mass storage handler
       debugging, 6-5			  RK8E handler,
       FIELD definition, 6-5		    see Mass storage handler
       LEVEL definition, 6-5		  RL01 format,
       modifiable tasks, 6-3		    see Mass storage handler
       NONRES macro, 6-5		  RL01 handler,
       root segment, 6-1		    see Mass storage handler
       SECT definition, 6-5		  RTS/8, described, 1-1, 1-3
     NONRWT, 2-5			  RTS/8 Executive,
     Null task, 4-44			    see Executive
					  RTS/8 mnemonics, A-1
					  RTS/8-OS/8 communication, 4-41
					  RTS/8 system execution, 2-8
     OPen, MCR command, 5-6		  RUN, 3-15
     OS/8 background terminal,		  RUNWT, 3-5, 3-15
       see Terminal driver
     OS/8 file support task, 4-38
       message format, 4-38
       message words, 4-38		  Scheduler,
     OS/8-RTS/8 communication, 4-41	    see Task scheduling
     OS/8 support task, 4-40		  SEND, 3-16
       rebooting, 4-41			  SENDW, 3-17
					  SKPINS, 3-18
					  STop, MCR command, 5-8
					  SUSPND, 3-22
					  Swap device, 6-1
     PARTBL, 7-11			  SWPWT, 3-5
     Partition table, 7-11		  Synchronization,
     Partitions,			    see Task communication
       see Task partitions		  SYstat, MCR command, 5-8
     PDP 8-A null task, 4-44		  System execution, 2-8
     POST, executive request, 2-2,	  System status report, MCR
	 3-11				      command, 5-8
     POST, MCR command, 5-6		  System tasks, 1-2
     POSTDS, 3-19, 4-14			    summary, 4-1
     Posting
       see Task communication

				    Index-3

				 INDEX (CONT.)


     Task communication, 2-2		  Terminal handler, 4-16
       messages, 2-4, 2-5		    assigning tasks to, 4-18
	 acknowledging, 3-11		    background ownership, 4-17,
	 event completion signalling,	      4-40
	   3-11				    character mode, 4-18
	 formats, 2-4			    emergency breakthrough task,
	 message queues, 2-4, 2-5,	      see Emergency breakthrough
	   3-12					task
	 not waiting for, 3-13		    foreground ownership, 4-17
	 posting, 2-4			    line mode, 4-18
	 queues, 2-4, 2-5, 3-12		    MCR invocation, 4-17
	 receiving, 3-12		    message format, 4-16
	 send, 3-16			    message words, 4-16
	 send and wait, 3-17		    timeout, 4-17
	 waiting for, 3-12		  TFTABL, 7-8
	 with Executive, 3-1		  TIme, MCR command, 5-10
       nonresident tasks, 6-1		  Timeout,
       synchronization, 2-2		    see Terminal handler
     Task creation, 2-6			  TSTABL, 7-7
     Task execution, 2-2
       changing, 3-7
       resumption, 3-15
       suspension of, 3-4, 3-22		  UDC/ICS handler, 4-46
     Task flag's table (TFTBL), 7-8	    analog input, 4-48
       location, 7-14			    analog output, 4-49
     Task flag's word, 3-4, 3-24, 5-8	    change of state, 4-50
     TASK macro, 2-7			    digital input, 4-51
     Task partition, 3-10, 6-1, 6-3	    digital output, 4-51
       competition for, 6-4		    disable contacts, 4-52
       freeing, 6-4			    disable counter, 4-53
       number, 6-3			    error messages, 4-58
     Task priority, 2-1, 2-5		    enable contacts, 4-54
       function, 2-1			    enable counter, 4-55
     Task scheduling, 2-6, 3-14, 7-4	    generic code, 4-56
     Task state table (TSTABL), 7-7	    operation summary, 4-47
       location, 7-14			    read counter, 4-57
     Task switching, inhibition,	  UNBARG, 3-24
	 7-3, 7-5			  USERWT, 3-5
     Task tables, 7-6
       locations, 47-12
       message queue header table,      
	 7-10				  WAITBITS, 3-4, 3-24, 5-8
       partition table, 7-11		    symbolic names, 3-5
       residency table, 7-10		  WAITE, 2-3, 3-9, 3-26
       summary, 7-6			  WAITM, 7-6
       task flag's table, 7-8		  WAITX, 3-9, 3-26, 3-27
       task state table, 7-7
     Tasks, 1-3








				    Index-4



							     RTS/8
							     User's Manual
							     AA-0724D-TA


			       READER'S COMMENTS


     NOTE:  This form is for document comments only. DIGITAL will
	    use comments submitted on this form at the company's
	    discretion. If you require a written reply and are
	    eligible to receive one under Software Performance
	    Report (SPR) service, submit your comments on an SPR
	    form.


     Did you find this manual understandable, usable, and well-organized?
     Please make suggestions for improvement.

     ----------------------------------------------------------------------

     ----------------------------------------------------------------------

     ----------------------------------------------------------------------

     Did you find errors in this manual? If so, specify the error and
     the page number.

     ----------------------------------------------------------------------

     ----------------------------------------------------------------------

     ----------------------------------------------------------------------

     Please indicate the type of reader that you most nearly represent.

	     o Assembly language programmer
	     o Higher-level language programmer
	     o Occasional programmer (experienced)
	     o User with little programming experience
	     o Student programmer
	     o Other (please specify)


     Name_______________________________________ Date______________________

     Organization__________________________________________________________

     Street _______________________________________________________________

     City_____________________________ State________ Zip Code _____________
						      or
						     Country



















     -------------------------------Fold Here------------------------------

















     -----------------Do Not Tear - Fold Here and Staple-------------------

							  +---------------+
							  |  FIRST CLASS  |
							  | PERMlT NO. 33 |
							  | MAYNARD. MASS.|
							  +---------------+
	BUSINESS REPLY MAIL					   ========
	NO POSTAGE STAMP NECESSARY IF MAILED IN THE UNITED STATES  ========
     ======================================================================
	Postage will be paid by:				   ========
								   ========
			  +-+-+-+-+-+-+-+			   ========
			  |d|i|g|i|t|a|l|			   ========
			  +-+-+-+-+-+-+-+			   ========
								   ========
		      Software Communications                      ========
		      146 Main Street  ML5-5/E39		   ========
		      Maynard, Massachusetts  01754		   ========